## Slide 1: Multi-Domain Model-Based Engineering
Hans Peter de Koning (ESA/ESTEC, The Netherlands)

## Slide 2: Glossary of Terms
Domain = (short for) Domain of Expertise ≈ Discipline
Multi-Domain ≈ Multi-Disciplinary
Universe of Discourse = Domain of Discourse
  “Scope taken into account”
Systems Engineering (INCOSE) = System Engineering (ECSS)

## Slide 3: Background of this presentation
Standardisation work on ECSS E-TM-10-23 and E-TM-10-25
  Model based system engineering conceptual data models for European space
Co-organisation of 14 annual NASA-ESA Product Data Exchange Workshops
Contributions to SysML v1.2 and v1.3 (QUDV)
Standardisation work on ISO 10303 (STEP) and related standards
  Cross-industry & multi-disciplinary
  15 years chair of Dutch normalisation committee for “Industrial automation”
MBSE Panel at INCOSE IS11 (Denver)
Work on ESA space projects in general and ESA’s Concurrent Design Facility in particular
Development lead on ESA’s Open Concurrent Design Tool (OCDT)
  New multi-domain conceptual modelling environment (in progress)

## Slide 4: ESA Concurrent Design Facility (CDF)
For details see http://www.esa.int/SPECIALS/CDF/
Concurrent engineering of conceptual design of all candidate ESA missions
including risk, cost, programmatics
10 to 15 studies per year

## Slide 5: CDF Layout
Break out room
Meeting room
Big screen
Main CDF room
Glass pane
Integrated audio & video: all inputs / output switchable
Video conferencing at each seat

## Slide 6: CDF Typical Domain Seats 22 typical in full study / 32 max
Team Leader
System Eng.
SE Assistent
Configuration (3D)
Cost Analysis
Risk Assessment
Customer
Technical Author
Structural
Thermal Control
Mission Analysis
Programmatics
Ground Systems & Ops
(Remote, ESOC)
AOCS
GNC
Propulsion
Communications
Data Handling
Functional
Simulation
Power
Mechanisms
Instruments

## Slide 7: Systems Engineering: 3 Main Areas of Concern & 1 Central Task
Coordination and
Control
Facilitate lead and control collaboration between all disciplines and parties
Requirements
Design
Manufacturing,
Assembly & Integration,
Verification & Validation
Customer
Supplier
Specify
the Problem
Define
the Solution
Realise
the Product
E-ST-10C: "System engineering integration and control"
E-ST-10C: "Design and configuration“ and “Analysis”
E-ST-10C: "Requirements engineering" and “Analysis”
E-ST-10C: "Verification" and "MAIT"

## Slide 8: Concurrent (System) Engineering
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
…
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
Attitude & Orbit Control
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
Thermal
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
Comms
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
Propulsion
Requirements
Design
Manufacturing,
Integration,
Verification,Validation
Power
Requirements
Design
Manufacturing,
Assembly & Integration,
Verification & Validation
System
Collaborate,
Coordinate and
Control
Iterate between
Requirements,
Design, and MAIV&V
Iterate across
Disciplines

## Slide 9: System Engineering in the Supply Chain (Product Tree / WBS)
Prime Contractor
Requirements
Design
M,
A & I,
V & V
Customer
Supplier
Customer
Supplier
Requirements
Design
M,
A & I,
V & V
Requirements
Design
M,
A & I,
V & V
Requirements
Design
M,
A & I,
V & V
Requirements
Design
M,
A & I,
V & V
Requirements
Design
M,
A & I,
V & V
Customer
Supplier
Top Customer
1st Tier Subcontractors
2nd Tier Subcontractors
nth Tier Subcontractors

## Slide 10: Effort along the System Life-Cycle
FAR
Requirements
Design
Manufacturing,
Assembly & Integration,
Verification & Validation
time
effort
SRR
PDR
CDR
MDR
PRR
Specify
the Problem
Define the Solution
Realise the Product
QR
Phase 0 A B C D

## Slide 11: Model Based System Engineering (MBSE)
Coordination and
Control
Requirements
Design
Manufacturing,
Assembly & Integration,
Verification & Validation
Customer
Supplier
Specify
the Problem
Define
the Solution
Realise
the Product
System / Architectural Design Model
Trade-offs & Design Rationale
Structure and Behaviour Models
Analysis and Simulation Results
Requirements Models
including traceability links
M, A & I Models (including Logistics)
V & V Models (procedures,
testcases, results, NCRs, waivers, close-out, VCDs)
Data Common to all Disciplines
Interfaces between Disciplines
Configuration Control & Baselines
Provide all needed views and all needed reports
on all system data
from a consistent source model

## Slide 12: “Model Based Engineering” is actually not new at all …
Has been done for almost all (non-SE) disciplines for a long time
Methods and tools for all domains of expertise are mature
Mechanical engineering analysis and simulation
Electrical engineering analysis and simulation
Functional, Control and Communication analysis and simulation
MAIT & Operations preparation
Cost and Complexity analysis
Human Factors and Ergonomics simulation
…
Traditionally modelling focus is primarily on design … and some on verification … (too) little on problem specification / requirements

## Slide 13: “Model Based Engineering” is actually not new at all … but there are problems
The big problem is integration across all domains/disciplines
Sharing the right information at the right time
  across all domains ⇒ interoperability between all tools & models
  achieving high data consistency and quality across all models
  achieving information consistency ⇒ consistent data interpretation
  achieving across-domain configuration control
Modelling requirements specifications precisely for early validation
  most specs are too informal, too imprecise for early validation
    validation in the sense of “Are we very clear about what problem to solve?” and “Do we have a complete and consistent problem specification (for the current stage of development)?”
Access to MAIV&V results data for model based V&V

## Slide 14: Role and Benefit of MBSE “Data Hub”
Natural hub for data common to all domains / disciplines
Assists in performing SE coordination and control task across all domains
Data Hub does not necessarily need to be physical – can be virtual / distributed
May have some data warehousing features
Can be used to compute / report continuous development “dashboard”
  Main budgets (mass, power, …)
  Key performance indicators
  Measures of Effectiveness
We need a top-down vision and a bottom-up realisation of the MBSE Data Hub

## Slide 15: Need for Standard Semantic Data Model
MBE requires a shared underlying Semantic Data Model, aka Conceptual Data Model, (upper) Ontology
  Provides authoritative, precise definition of data and its meaning
  Expressed in commonly agreed (formal) data modelling language
    Should be based on formal logic
    With controlled natural language to support review and validation by all stakeholders
  Defines data structure, population constraints, validation rules, …
  Must be completely independent from any (IT) implementation technology
  Should be modular and extensible
  Foundational modules for e.g. generic property types / quantities / scales / units, composite structure (function tree, product tree, WBS), version control, identification / naming / labelling, …
    Also called “building blocks”, “resource libraries”, “upper ontologies”
  Sufficiently rich as source for model transformation / code generation

## Slide 16: Standardise on Single Tool Set?
No single tool vendor (however large) can possibly master all methods and tools for all domains
  to a required level of excellence and price/performance level
Industrial consortia / supply chains not static, but differ per project
Engineering analysis, simulation and modelling tools are non-trivial and require substantial investments in training, licences, reusable components
Healthy competition between tool vendors is beneficial for end-user and promotes innovation
Even with a single tool suite, there will be different versions creating interface problems at a smaller scale
So, not a good idea …

## Slide 17: Point-to-point vs Standard-based Data Interfaces
N x (N-1) interfaces
2N interfaces
Point-to-point
Standard-based
standard
format /
protocol

## Slide 18: Data Model Layers and Automated Transformation (MDA-like)
Semantic Data Model for
Space Systems Engineering
Relational
Logical Data Model
Hierarchical
Logical Data Model
Object-Oriented
Logical Data Model
Conceptual Model
Logical Model
Physical Model
Relational Data Model
Hierarchical Data Model
Object-oriented
Data Model
e.g. Oracle SQL, Hibernate, …
e.g. XSD, DTD
e.g. Java, Javascript, .NET C#, Python, …
e.g.
- UML with dedicated Profile,
Fact Based Modeling
RDF/OWL
Express
Eclipse EMF / Ecore
…

## Slide 19: Evolving ECSS Semantic Data Models in support of MBSE
E-TM-10-23
Focuses on detailed models
in later life cycle phases (B, C, D, E)
E-TM-10-25
Focuses on conceptual models
in early life cycle phases (0, A)
Developed in tandem
Where possible common approach and semantics
Defined in UML2/OCL
Where possible aligned with OMG SysML (including QUDV)
E-TM-10-25A made available Oct 2010
E-TM-10-23A made available Nov 2011
Intended future merge to single real standard

## Slide 20: Concurrent Engineering in Early Phases vs Collaborative Engineering in Later Phases
Early Phases (0, A)
Later Phases (B, C, D, E)
Tens of users
One or few organisations
Near-real-time data sharing in minutes, hours
Trade studies / Strawman models
Requirements in state of flux
Support decision making / programme formulation
Few relatively small models
Fine-grained version control (object level)
Hundreds of users
Tens of organisations
Synchronisation times in days, weeks, months
Formal configuration/version control
Strict requirements baseline
Formal, detailed V&V
Orders of magnitude more models/data
Coarser-grained version control (“dataset” level)
time
baseline
Transition around SRR (first half Phase B)

## Slide 21: Standards validated through tool implementations and pilot projects
E-TM-10-25 → Open Concurrent Design Tool (OCDT)
  Validation of E-TM-10-25 data model w.r.t. to CDF-like CE process
  Three–tier architecture: Client / REST Webservice / Persistent Data Store
  Entirely built on open source components
  Community Open Source Software (for ESA Member States)
  Extensive use of model-based software engineering / code generation
  Main client integrated with Excel for lowest possible learning curve
  Designed for distributed design sessions
  Software Development Kit for Domain Specific Tool adapters
E-TM-10-23 → Virtual Spacecraft Design (VSD)
  Validation of E-TM-10-23 data model with GOCE Phase B design
  Sophisticated generation of code and GUI directly from data model
  Successful use of Eclipse Modeling Framework as a platform
  Client / Server architecture built on open source components
  Follow-up in Astrium and Thales-Alenia Space for use in projects

## Slide 22: Standards and Tool Implementations
Database
Semantic Data Model Standard
Semantic Data Model
“Master Definition of Concepts”
addresses “what” not “how”
Derived Logical and
Physical Data Models
“Reference Data Libraries (RDLs) “
Runtime loadable
predefined objects,
including QUDV and Categories
Software Implementations
Tool
Tool
Tool
Database
Database
Automated transformations
Interoperable tools and databases
(including adapters around existing tools)
Generated
Runtime use

## Slide 23: ECSS Improvement w.r.t. SysML: Explicit Occurrence and Realisation in system decomposition

## Slide 24: ECSS Improvements w.r.t. SysML: “Category” concept
Category is added as explicit concept in model
Category is a runtime, user-defined classification feature
User-defined validation rules / constraints on basis of Category
Adds flexibility to extend models with functionality that was unforeseen at design time without need for update of software implementations
Similar to on-the-fly extensibility of RDF/OWL based ontologies

## Slide 25: ECSS Improvements w.r.t. SysML: Evolution of “QUDV”
ParameterType (SysML ValueProperty type) is extended with CompositeParameterType that allows for non-scalar multi-value parameter / properties (including mathematical nth order tensors )
MeasurementScale is added as concept, with precise subclasses
  OrdinalScale
  IntervalScale
  RatioScale
  CyclicRatioScale
  Base10LogarithmicScale
  NaturalLogarithmicScale
Mathematical NumberSet is added in definition of QuantityKind
Full ISO/IEC 80000 (14 parts) is captured as Reference Data Library

## Slide 26: Possible Extension of “QUDV”: “PropertyValueCube” for Analysis/Test Results
Derived from “STEP-NRF datacube”
Hypercube for efficient representation of large amounts of results data
Re-uses SysML / ECSS ValueProperty, Block/Element, state ValueProperty
Each cell of the hypercube is a property value (can be non-scalar, any datatype)
Store slices of data for given time, frequency or other state variable
Has been implemented, tested and used with high-speed, low-memory footprint open source HDF5 library
states
observable items: blocks, elements
properties
typically: sampled time or frequency

## Slide 27: ECSS-E-TM-10-25 improvements for interactive multi-domain concurrent engineering (1/2)
DomainOfExpertise is explicit concept in model
Participant in an engineering activity is a Person with a Role and represents a single DomainOfExpertise at a time
Any Requirement, Element, Parameter (i.e. ValueProperty) is “owned” by a DomainOfExpertise, who is responsible for its existence and value
DomainOfExpertise (other than owner) can take subscription on a Parameter, in order to use it as an input in his/her analysis
Value updates of Parameters happen for non-owners only after explicit “publication” in order to prevent disruptions caused by continuous value changes
Value of a Parameter (i.e. ValueProperty) can be overridden at Usage, Occurrence or Realisation level
  Provides “value inheritance” in addition to “type inheritance”

## Slide 28: ECSS-E-TM-10-25 improvements for interactive multi-domain concurrent engineering (2/2)
Built-in version control at object level with subversion-like revisions
(Design) Option is explicit concept in model
Architecture can be configured for different Options
For each Option the ElementOccurrence tree (explicit full system structure) is generated on the fly from the implicit ElementDefinition and ElementUsage composite structure
Net difference between Options can be used in system trades
Requirements can be expressed as machine readable boolean expressions

## Slide 29: Limitations of UML2/OCL based data models
UML2 is not sufficiently precise to define rock solid semantic data models
  Can fix a lot with UML profiles, but not ideal
UML2 meta-model (in MOF) is overly complicated, and as a consequence XMI or tool APIs are hard to use and lack interoperability
OCL helps, but OCL tooling is only reasonably mature for Java, not for other programming languages
Better “real” semantic modeling language and tooling is needed
Most likely candidates: RDF/OWL and FBM (Fact Based Modeling)
For intermediate period EMF Ecore seems solid, practical industrial solution

## Slide 30: Learn from non-SE domains (1/2)
M-CAx / E-CAx - design, analysis, simulation, V&V
  Geometry and topology – 2D, 3D, CSG, parametric design
  Structured modular approach (separate part and assembly definition)
  Electronic catalogues / libraries of reusable items / materials
  Integrated configuration / variant / revision management (PLM)
  Integrated digital approval / sign-off (PLM)
  Scaleability to big models, including analysis/simulation results
Control engineering and system simulation
  Executable block diagrams
  Modeling languages:
    MATLAB/Simulink and derivatives
    Modelica and similar object-oriented non-causal simulation languages

## Slide 31: Learn from non-SE domains (2/2)
Software engineering (and IT)
  Object-oriented models – separation of concerns, inheritance, encapsulation, polymorfism, … BUT: Software OO models are not the same as System OO models
  Configuration / version control – "trunk", branching, merging – “light PLM”
  Time-boxed, incremental, iterative "agile" development approach as opposed to traditional waterfall → has consequences for procurement / contractual approach
  Test-driven SW development → V&V-driven system engineering?
  Wikis / multi-authoring → useful to bridge documents / models

## Slide 32: New collaboration initiative: INCOSE and NAFEMS Working Group
NAFEMS is a world-wide professional society, like INCOSE and IEEE
NAFEMS is an “independent not-for-profit body with the sole aim of promoting the effective use of engineering simulation methods such as finite element analysis, multibody system dynamics and computational fluid dynamics”, see http://www.nafems.org
Extensive knowledge on mechanical engineering analysis and simulation: CAD, FEM, CFD, Thermal, Kinematics, Multi-Physics, …
Announcement on https://www.incose.org/newsevents/news/details.aspx?id=266 Joint cross organizational working group on Systems Modeling & Simulation, including MBE
Tomorrow first open WG meeting 1-5 PM in Tallahassee Boardroom

## Slide 33: References
ECSS: http://www.ecss.nl
Eclipse: http://www.eclipse.org in particular http://www.eclipse.org/modeling/
ESA CDF: http://www.esa.int/SPECIALS/CDF/
Fact Based Modelling (FBM): http://www.factbasedmodelling.org
RDF/OWL: http://www.w3.org/standards/semanticweb/
SysML: http://www.omgsysml.org/
UML: http://www.omg.org/uml/