Date: October 2009

SysML-Modelica
Transformation Specification

Version Alpha 1

____________________________________________________
OMG Document Number: dtc or ptc/200x-xx-xx
Standard document URL: http://www.omg.org/spec/acronym/1.0/PDF
Associated File(s)*: http://www.omg.org/spec/acronym/200xxxxx
  http://www.omg.org/spec/acronym/200xxxxx
____________________________________________________

Source document: Title (document number)
* Original file(s): Title (document number)

List of issues to discuss:
1. Name for SysML4Modelica → what is a better name? If we compare this to UML4SysML then it refers to a subset of UML, not a profile.
2. We discussed on10/21/09 that isFinal should be defined although isLeaf already exists with the same semantics. We decided to take the opposite approach for isAbstract which corresponds to the Modelica “partial” keyword. PROPOSAL: be consistent and use isLeaf rather than isFinal.
3. When should a reference to a stereotype be capitalized? The definition is capitalized but an instance has the same name in lowercase...
4. I'm struggling with our decision to make all restricted classes map to SysML blocks. Ultimately, we need to associate values with Modelica variables. Since all types that have values derive from the Modelica predefined types, the predefined types should somehow be able to have a value. In the current mapping, the predefined types derive from the SysML valueTypes Real, Integer, etc. However, if all restricted classes map to blocks, then this causes problems since blocks cannot specialize valueTypes.
   Proposed solution: make the Modelica predefined types instances of «modelicaType» (which derives from «block»). Unlike other «modelicaType»'s (which can only modify existing types including predefined types), the predefined types themselves have value properties as defined previously in the mapping (Chapter 6). The only difference would be to add a value property called “value” rather than have the predefined type specialize the SysML valueType Real (or Integer, Boolean, etc.). This is consistent with the approach taken in Modelica. In Modelica, the predefined types also have a “value” property, but the compiler refers to that value automatically. That is, for a usage, myReal, of the type Real, one should refer to “myReal” rather than “myReal.value”.
5. Related to the previous issue: rather than distinguishing between «modelicaPart», «modelicaPort» and «modelicaValueProperty», we could now drop «modelicaValueProperty». However, I propose that we keep «modelicaValueProperty» because some of the stereotype attributes are specific to «modelicaValueProperty»'s (i.e., flowFlag, variability, and declarationEquation).
6. Review of the constraints – my inexperience in writing this kind of documents makes it difficult for me to judge whether the constraints are written in an appropriate form and whether they are complete. Any feedback would be welcome.
7. Is a «modelicaConnection» a Property? If so, then it should be added in constraint [1] of «modelicaModel».

Notes:
include example section to overall document...
add annotations and comments throughout
Part II ̶̵̶ SysML4Modelica Profile
This part describes the mapping of Modelica constructs to SysML. This mapping is the foundation for the SysML4Modelica profile. It is organized according to the chapters of the Modelica 3.0 specification, skipping those chapters that are irrelevant to the SysML-Modelica mapping. When necessary, new stereotypes (extensions of SysML) and associated tags are introduced.
# Class Definition
## Overview
The class concept is the basic structural unit in Modelica. Classes provide the structure for objects and contain equations and algorithms, which ultimately are the basis for the executable simulation code. The most general class is “model”. Specialized classes such as “record”, “type”, “block”, “package”, “function” and “connector” have most of the properties of a “model” but with restrictions, which need to be preserved in SysML to support round-trip mapping.
The following production rules define the different specialized classes. The reference in parentheses on the right indicates the section of this document in which the particular language element is discussed in detail:
stored_definition:
   [ within [ name ] ";" ]	(5.2)
   { [ final ] class_definition ";" }	(5.2)

class_definition :
   [ encapsulated ]	(5.2)
   [ partial ]	(5.2)
   ( class	(5.2)
    | model	(5.3)
    | record	(5.4)
    | block	(5.5)
    | [ expandable ] connector	(5.6)
    | type	(5.7)
    | package	(5.8)
    | function )	(5.9)
   class_specifier

class_specifier :
     IDENT string_comment composition	(7)
   | IDENT "=" base_prefix name [ array_subscripts ]	(5.7)
   [ class_modification ] comment	(5.11)
   | IDENT "=" enumeration "(" ( [enum_list] | ":" ) ")" comment	(5.10)
   | IDENT "=" der "(" name "," IDENT { "," IDENT } ")" comment	(5.9)
   | extends IDENT [ class_modification ] string_comment composition	(5.11)
   end IDENT
The following table lists the SysML stereotypes for representing the specialized Modelica classes. Using this approach the modeler only needs to apply the respective stereotype to indicate all the semantics and restrictions of the associated Modelica class. This information is represented graphically in Figure 1. In the following subsections, the details of each stereotype are described.

# : Mapping for the Modelica specialized classes.
Modelica Construct	SysML Base Class	SysML4Modelica
		New Stereotype	Comments
Class	UML4SysML::Classifier	«modelicaClass»	See Section 5.2
Model	SysML::Blocks::Block	«modelicaModel»	See Section 5.3
Record	SysML::Blocks::ValueType	«modelicaRecord»	See Section 5.4
Block	SysML::Blocks::Block	«modelicaBlock»	See Section 5.5
Connector	SysML::Blocks::ValueType	«modelicaConnector»	See Section 5.6
Type	SysML::Blocks::ValueType	«modelicaType», «modelicaEnumeration»	See Sections 5.7 and 5.10
Package	SysML::Blocks::Block	«modelicaPackage»	See Section 5.8
Function	UML4SysML::Behavior	«modelicaFunction»	See Section 5.9

: Package diagram with an overview of the stereotypes for Modelica Classes
## «modelicaClass»
###### Stereotypes
Classifier (from UML4SysML)
###### Abstract Syntax
See Figure 1.
###### Description
A Modelica class is the basic structural unit in Modelica. However, because it lacks precise semantics, the class construct should never be used in Modelica. Without precise semantics, a Modelica tool cannot easily check whether any restrictions are violated. Therefore, the constructs that are specialized from Modelica class should be used instead.
In the context of the SysML4Modelica profile, the Modelica class construct is mapped to the stereotype «modelicaClass» which is abstract and thus cannot be instantiated directly. This choice has been made because it is desirable to have the additional semantics specified by the specialized classes. In addition, as clearly shown in See Figure 1, the stereotypes associated with the specialized classes derive from different SysML constructs and thus cannot be mapped to a single common construct for a Modelica class. The abstract stereotype «modelicaClass» serves the purpose of grouping the attributes that apply to all the Modelica specialized classes. It stereotypes UML::Classifier, which is a common generalization for the stereotypes of all the specialized classes.
Just like UML Classifiers, a «modelicaClass» can contain nested class definitions. Such nested definitions can be of any restricted class type derived from «modelicaNestedClass». For instance, a «modelicaConnector» can contain a «modelicaPackage».
Modelica classes are often defined using a short class definition syntax. For example, the type Force could be defined as:
type Force = Real[3](unit={"N.m","N.m","N.m"});
Rather than supporting such short class definitions explicitly, the SysML4Modelica profile supports only the longer (but equivalent) form (Note: in the Modelica abstract syntax the two forms are often represented identically):
type Force
  extends Real[3](unit={"N.m","N.m","N.m"});
end Force;
In the remainder of this section, all the common attributes and associations for all the constructs specialized from Modelica class are described. In subsequent sections for the individual specialized constructs, only the constraints on these attributes and associations will be described in detail.
###### Attributes
/isFinal : Boolean [0..1]
In Modelica, the definition of a class can be qualified to be final (Modelica Specification 7.2.6). This means that the declared class cannot be further modified through (local) type modifications. Note that this is identical to the UML attribute isLeaf for redefinable elements (UML Specification 7.3.46) which, if true, indicates that no further redefinitions are possible.
The isFinal attribute is true when the final prefix is present in Modelica; false otherwise. Its default value is false. This is derived.

isModelicaEncapsulated : Boolean [0..1]
As explained in Modelica Specification 5.3.2, the Modelica encapsulated construct limits the scope of name lookup. An encapsulated package can be moved within the package hierarchy without affecting the local name resolutions.
These semantics are different from the isEncapsulated attribute of Blocks in SysML (SysML Specification 8.3.2.2). An encapsulated block is treated as a black box; no connections can be made to its internal parts directly.
A second difference in semantics is that in Modelica the encapsulated prefix can be applied to all classes, although it is most commonly applied to packages. It is therefore necessary to introduce isModelicaEncapsulated as a new attribute so that it becomes available also for specialized class stereotypes that do not derive from a SysML Block.
The isModelicaEncapsulated attribute is true when the encapsulated prefix is present in Modelica; false otherwise. Its default value is false.

isAbstract : Boolean [0..1]
The Modelica partial construct has the same semantics as the isAbstract attribute in SysML. Since «modelicaClass» stereotypes UML::Classifier, the isAbstract attribute is automatically inherited. The default value is false.
###### Associations
No additional associations.
###### Constraints
1. isFinal has the same value as isLeaf
  isFinal = self.isLeaf
2. «modelicaClass» is an abstract stereotype and cannot be instantiated.
3. Any generalization relationship to/from «modelicaClass» must be stereotyped to a «modelicaExtends» relationship.
4. A «modelicaClass» can only contain nestedClassifiers stereotyped to a restricted type derived from «modelicaClass»
###### Additional Notes
The Modelica within clause is explained in Modelica Specification 13.2.2.3. It defines where in the package hierarchy the subsequent class definitions are located. This is important in Modelica to allow large package structures to be divided over multiple model files. As long as fully qualified type identifiers are used, the within clause is not relevant in SysML.
## «modelicaModel»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
###### Abstract Syntax
See Figure 1.
###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes
No additional attributes.
###### Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaModel» must have a Name.
2. An instance of a «modelicaModel» can only have Properties that are stereotyped to «modelicaPart», «modelicaPort», or «modelicaValueProperty».
3. An instance of a «modelicaModel» can only contain Behaviors that are stereotyped to «modelicaFunction», «modelicaAlgorithm», or «modelicaInitialAlgorithm».
4. An instance of a «modelicaModel» can only contain Constraints that are stereotyped to «modelicaEquation» or «modelicaInitialEquation».
5. An instance of a «modelicaModel» can only specialize other classifiers derived from «modelicaRecord», «modelicaBlock», or «modelicaRecord». The stereotype «modelicaExtends» must be applied to the generalization relationship.
6. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated.
###### Example
A Modelica model for a translational Mass is defined as a specialization of PartialRigid, as is illustrated in Figure 2. (Model extracted from the Modelica Standard Library – Modelica.Mechanics.Translational.Components.Mass). The corresponding Modelica model is shown in Figure 3.
: SysML4Modelica model for translational mass
The corresponding Modelica models (with annotations omitted):
: Modelica Model for a Mass from the Modelica Standard Library
Remarks:
- The name of each model (Mass and PartialRigid) appear as the Name attribute of the corresponding «modelicaModel»
- The parameters of each model (m and stateSelect) appear as «modelicaValueProperty» in «modelicaModel»
- The connectors flange_a and flange_b appear as ports stereotyped to «modelicaPort»
- The equation sections are each mapped to a «modelicaEquation», which are shown as any other constraint in the concrete graphical syntax
## «modelicaRecord»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
Abstract Syntax
See Figure 1.
Description
The Modelica specialized class record is restricted to contain only public declarations of components that in turn also contain only public declarations. A complete description of record is available in Section 4.6 of the Modelica Specification:
Only public sections are allowed in the definition or in any of its components (i.e., equation, algorithm, initial equation, initial algorithm and protected sections are not allowed). May not be used in connections. The elements of a record may not have prefixes input, output, inner, outer, or flow. Enhanced with implicitly available record constructor function. Additionally, record components can be used as component references in expressions and in the left hand side of assignments, subject to normal type compatibility rules.

###### Attributes
No additional attributes.
###### Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaRecord» must have a Name.
2. An instance of a «modelicaRecord» can only have Properties that are stereotyped to «modelicaValueProperty».
3. Any «modelicaValueProperty» owned by an instance of «modelicaRecord» must have visibility=public, flowFlag=non-flow, causality=null, scope=null.
4. An instance of a «modelicaRecord» can only specialize other classifiers derived from «modelicaRecord». The stereotype «modelicaExtends» must be applied to the generalization relationship.
5. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated; and the ownedElements: Behavior, Constraint.
###### Example
[To be added]
## «modelicaBlock»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
###### Abstract Syntax
See Figure 1.
###### Description
The Modelica specialized class block is very similar to a model except that all its connectors must be either an input or output making it similar to a Simulink block. A complete description of block is available in Section 4.6 of the Modelica Specification:
Same as model with the restriction that each connector component of a block must have prefixes input and/or output for all connector variables. [The purpose is to model input/output blocks of block diagrams. Due to the restrictions on input and output prefixes, connections between blocks are only possible according to block diagram semantic]

###### Attributes
No additional attributes.
###### Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaBlock» must have a Name.
2. An instance of a «modelicaBlock» can only have Properties that are stereotyped to «modelicaPart», «modelicaPort», or «modelicaValueProperty».
3. Any «modelicaValueProperty» owned by an instance of «modelicaBlock» must have causality=input or output.
4. An instance of a «modelicaBlock» can only contain Behaviors that are stereotyped to «modelicaFunction», «modelicaAlgorithm», or «modelicaInitialAlgorithm».
5. An instance of a «modelicaBlock» can only contain Constraints that are stereotyped to «modelicaEquation» or «modelicaInitialEquation».
6. An instance of a «modelicaBlock» can only specialize other classifiers derived from «modelicaBlock» or «modelicaRecord». The stereotype «modelicaExtends» must be applied to the generalization relationship.
7. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated.
###### Example
[To be added]
## «modelicaConnector»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
Abstract Syntax
See Figure 1.
Description
The Modelica specialized class connector is a model that cannot contain equations or algorithms in any of its components. A complete description of block is available in Section 4.6 and Chapter 9 of the Modelica Specification:
No equations or algorithms are allowed in the definition or in any of its components. Enhanced to allow connect(..) to components of connector classes.

###### Attributes
isExpandable : Boolean
As explained in Modelica Specification 9.1.3, the Modelica expandable prefix can be applied to a connector. The primary purpose of expandable connectors is to allow for the convenient modeling of bus interfaces. The default value is false.
###### Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaConnector» must have a Name.
2. An instance of a «modelicaConnector» can only have Properties that are stereotyped to «modelicaPart», «modelicaPort», or «modelicaValueProperty».
3. None of the Properties owned by an instance of «modelicaConnector» can contain Behaviors or Constraints (at any level of containment).
4. An instance of a «modelicaConnector» can only specialize other classifiers derived from «modelicaConnector», «modelicaType», or «modelicaRecord». The stereotype «modelicaExtends» must be applied to the generalization relationship.
5. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated; and the ownedElements: Behavior, Constraint.
###### Example
[To be added]
## «modelicaType»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
###### Abstract Syntax
See Figure 1.
###### Description
The Modelica specialized class type is restricted to predefined types, enumerations, arrays of type or classes extending from type. It is enhanced to allow extension of predefined types. In the SysML4Modelica profile, the extension from predefined types is handled by making the predefined types instances of «modelicaType» (See Chapter 6).
The only additional distinct type for which a corresponding representation needs to be defined in SysML4Modelica is an enumeration. Enumerations are handled separately through the stereotype «modelicaEnumeration»
###### Attributes
No additional attributes.
###### Associations
No additional associations.
Constraints
1. An instance of a «modelicaType» must have a Name.
2. An instance of a «modelicaType» can only specialize other classifiers derived from «modelicaType». The stereotype «modelicaExtends» must be applied to the generalization relationship.
3. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated; and the ownedElements: Property (including part, port and value properties), Behavior, Constraint.
###### Example
[To be added]

## «modelicaPackage»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- «block» (from SysML)
###### Abstract Syntax
See Figure 1.
###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes
No additional attributes.
Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaPackage» must have a Name.
2. An instance of a «modelicaPackage» can only have Properties that are stereotyped to «modelicaValueProperty».
3. Any «modelicaValueProperty» owned by an instance of «modelicaPackage» must have variability=constant.
4. An instance of a «modelicaPackage» can only specialize other classifiers derived from «modelicaPackage». The stereotype «modelicaExtends» must be applied to the generalization relationship.
5. All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated; and the ownedElements: Behavior, Constraint.
###### Example
[To be added]
## «modelicaFunction»
###### Generalizations
- «modelicaClass» (from SysML4Modelica)
- FunctionBehavior (from UML4SysML)
###### Abstract Syntax
See Figure 1.
###### Description
The Modelica specialized class function represents a callable section of procedural algorithmic code. It is similar to a SysML FunctionBehavior. Compared to a general Modelica class, quite a few restrictions and enhancements apply; refer to the Modelica Specification sections 12.2 for details. Instead of including the procedural algorithmic code in an algorithm section, a Modelica function may refer to an external function specifier (e.g., an external C or Fortran function).
At this point, SysML4Modelica only allows for function definitions; functions cannot be “called” explicitly – they can only be referred to in concrete Modelica syntax portions of the model.
###### Attributes
- isExternal: Boolean [1]
  Default value is false.
- externalLanguage: String [0..1]
  The language in which the external function specifier is defined. It should only be defined when isExternal = true. Default value is “C”.
- externalFunctionSpecification: String [0..1]
  The complete specification of the externally defined function (see Modelica Specification 12.8 for details). If is not defined, then the name of the «modelicaFunction» is used. It should only be defined when isExternal = true. Default value is null.
- externalAnnotation: String [0..1]
  String containing a Modelica annotation associated with the external function call. It should only be defined when isExternal = true. Default value is null.
###### Associations
No additional associations.
###### Constraints
1. An instance of a «modelicaFunction» must have a Name.
2. An instance of a «modelicaFunction» can only have Parameters that are stereotyped to «modelicaFunctionParameter».
3. Any «modelicaFunctionParameter» (owned by an instance of «modelicaPackage») for which causality=input may not be assigned values in the body of the function (i.e., it is read-only).
4. An instance of a «modelicaFunction» can only have zero or one body attribute.
5. If isExternal=false then externalLanguage, externalFunctionSpecification, and externalAnnotation must not be defined.
6. If isExternal=true then body and language must not be defined.
7. An instance of a «modelicaFunction» must have language=“Modelica” if the body attribute is defined.
8. The body of the function must be represented in the Modelica syntax and must constitute a valid Modelica algorithm section.
9. An instance of a «modelicaFunction» can only specialize other classifiers derived from «modelicaFunction». The stereotype «modelicaExtends» must be applied to the generalization relationship.
10. All other attributes or associations inherited from FunctionBehavior or Classifier may not be used.
###### Example

function functionname
input TypeI1 in1;
input TypeI2 in2;
input TypeI3 in3 := default_expr1 "Comment" annotation(...);
...
output TypeO1 out1;
output TypeO2 out2 := default_expr2;
...
protected
<local variables>
...
algorithm
...
<statements>
...
end functionname;

A more specific example illustrating the different types of variables:
function testFunction
   parameter Real x = 5;
   constant Real y=1;
   input Real z;
   output Real k;
   // Real invalid; --> if public, must be input or output
protected
   Real valid = z*x; // this is ok, because it is protected
algorithm
   k := valid + y;
end testFunction;
###### Discussion and Comments:
Must accommodate short definitions specifically with “der”
must accommodate ExternalObject models – ExternalObject should be defined as an M1 abstract model
## «modelicaEnumeration»
###### Generalizations
«modelicaType» (from SysML4Modelica)
###### Abstract Syntax
See Figure 1.
###### Description
The stereotype «modelicaEnumeration» corresponds to the Modelica enumeration type which is of the restricted class type. It is defined in detail in the Modelica Specification 4.8.5.
###### Attributes
- value: Integer [1]
  The value of the instances of the enumeration.
- quantity: String [1]
  The quantity kind for the enumeration. Default value is the empty string.
- min: Integer [1]
  The “minimum” value of the enumeration to be interpreted as the rank in the ordered set of ownedLiterals. Default value is the first literal in the ordered set of ownedLiterals.
- max: Integer [1]
  The “maximum” value of the enumeration to be interpreted as the rank in the ordered set of ownedLiterals.Default value is the last literal in the ordered set of ownedLiterals.
- start: Integer [1]
  The initial value of the enumeration. Default value is the first literal in the ordered set of ownedLiterals.
- fixed: Boolean [1]
  If this attribute is true then the attribute start is interpreted as a hard constraint to be satisfied at the beginning of the simulation. If it is false then the attribute start is interpreted as only a guess value. Default value is false.
###### Associations
ownedLiteral: EnumerationLiteral[*]
The ordered set of literals for this «modelicaEnumeration». Subsets Element::ownedMember.
Constraints
All other attributes or associations inherited from «block» or Classifier may not be used. This includes the attributes: isActive, isEncapsulated; and the ownedElements: Property (including part, port and value properties), Behavior, Constraint; «modelicaEnumerations» cannot specialize any other «modelicaClass».
###### Example

type Size = enumeration(small, medium, large, xlarge);
## «modelicaExtends»
###### Generalizations
UML4SysML::Generalization
###### Abstract Syntax
: «modelicaExtends» stereotype definition
###### Description
The extends clause of Modelica is equivalent to a SysML Generalization. The only difference is that in Modelica the type being extended can be locally modified (Modelica Specification 7.1):
extends_clause :
   extends name [ class_modification ] [annotation]

constraining_clause :
   extends name [ class_modification ]
Similar local type modifications can be used when defining usages (i.e., Modelica components – see Chapter 7). In both cases the SysML4Modelica mapping currently captures the local modifications only as a text string in Modelica syntax. A separate modification can be defined for every component of a «modelicaClass»; in Modelica these modifications are grouped separated by commas in parentheses. Each such modification is represented in SysML4Modelica as a separate string. It corresponds thus to an argument as defined in the following extract of the Modelica EBNF (Modelica Specification 7.2):
class_modification :
    "(" [ argument_list ] ")"
argument_list :
    argument { "," argument }
argument :
    element_modification_or_replaceable
  | element_redeclaration
element_modification_or_replaceable:
    [ each ] [ final ] ( element_modification | element_replaceable)
element_modification :
    component_reference [ modification ] string_comment
element_redeclaration :
    redeclare [ each ] [ final ]
   ( ( class_definition | component_clause1) | element_replaceable )
element_replaceable:
    replaceable ( class_definition | component_clause1)
        [constraining_clause]
component_clause1 :
    type_prefix type_specifier component_declaration1
component_declaration1 :
    declaration comment
Muliple inheritance is supported in Modelica. Therefore, more than one «modelicaExtends» relationship is allowed for a single «modelicaClass». The extends clause can be applied to any of the restricted classes (including packages).
If the extends clause appears in a protected section of the Modelica model, then all the elements of the base class become protected elements of the specialized class. It is therefore important to specify whether the «modelicaExtends» relation is public or protected.
###### Attributes
modelicaModification: String [0..*]
An inherited Modelica class can be locally modified. The modifications are defined by this attribute in Modelica syntax. Each modification (as specified in the Modelica concrete syntax as a comma-separated expression) is specified as a separate instance of this attribute. Default value is null.
###### Associations
No additional associations.
###### Constraints
1. Both the source and target of a «modelicaExtends» relation must be typed to instances of «modelicaClass».
2. The visibility attribute of «modelicaExtends» can only take on values of public or protected.
###### Example
[To be added]
## Short Class Definitions
Modelica provides a short-hand notation for definition of classes. It is equivalent to an inheritance construct, and is therefore redundant and not supported separately in the SysML4Modelica profile.
# Predefined Types
## Overview
The following primitive types are available in the Modelica language: Real Type, Integer Type, Boolean Type, String Type, Enumeration Types, StateSelect, ExternalObject, Graphical Annotation Types. These primitive types are defined as predefined types in SysML4Modelica::BasicTypes. Although these types have direct counterparts in SysML, they are defined again to account for the additional attributes associated with them in Modelica. An example for ModelicaReal is shown in the diagram below:

Note that in Modelica, the properties such as “start”, “quantity”, etc, are not really equivalent to user-defined complex data-types. For instance, if one defines “Real x;” then one cannot refer to “x.min” in an equation. The only way one can specify a value for these special properties is as part of a type definition or local modification: e.g., “Real x(start=1, unit=”m”);

SysML / Abstract Syntax Reference	SysML4Modelica
	Predefined Type
SysML::Blocks::ValueType	ModelicaReal
SysML::Blocks::ValueType	ModelicaInteger
SysML::Blocks::ValueType	ModelicaBoolean
SysML::Blocks::ValueType	ModelicaString
UML4SysML::Enumeration	ModelicaEnumeration
SysML::Blocks::ValueType	ModelicaStateSelect
SysML::Blocks::Block	ModelicaExternalObject

SysML::Blocks::ValueType
ModelicaAnnotation
## ModelicaReal

The following tables list the tag values associated with the new stereotypes. All of the tags listed below are optional and can only be defined once, i.e. their multiplicity is [0..1]. Empty “Initial Value” field implies an empty string (null).

SysML4Modelica Predefined Type ModelicaReal (inherits from Real in SysML)
Property Name	Property Value Type	Multiplicity, Default Value	Comment
Quantity	String	[0..1],	Inherited from ValueType  corresponds to quantityKind (dimension in the SysML 1.1)

unit	String	[0..1],	Unit used in equations. / Inherited from ValueType.
displayUnit	String	[0..1],	Default display unit
Min	Real	[0..1], -Inf	Inf denotes a large value.
Max	Real	[0..1], +Inf;	Inf denotes a large value.
Fixed	Boolean	[0..1], true, // default for parameter/constant; / false; // default for other variables
Start	Real	0	Initial value. Initial guess value when fixed=false.
Nominal	Real	[0..1],	Nominal value used for scaling
stateSelect	ModelicaStateSelect	[0..1], StateSelect.default

## ModelicaInteger
SysML4Modelica Predefined Type ModelicaInteger (inherits from Integer in SysML)
Property Name	Property Value Type	Default Value	Comment
Quantity	String		Inherited from ValueType  corresponds to quantityKind (dimension in the SysML 1.1)
Min	Integer	-Inf	Inf denotes a large value.
Max	Integer	+Inf;	Inf denotes a large value.
Fixed	Boolean	true, // default for parameter/constant; / false; // default for other variables
Start	Integer	0	Initial value. Initial guess value when fixed=false.

## ModelicaBoolean
SysML4Modelica Predefined Type ModelicaBoolean (inherits from Boolean in SysML)
Property Name	Property Value Type	Default Value	Comment (from Modelica specification)
Quantity	String		Inherited from ValueType  corresponds to quantityKind (dimension in the SysML 1.1)
Start	Boolean	false;	Initial value.

## ModelicaString
[ToDo]
## ModelicaStateSelect
SysML4Modelica Predefined Type ModelicaStateSelect
Property Name	Property Value Type	Comment (from Modelica specification)
Never	Enumeration literal	Do not use as state at all.
Avoid	Enumeration literal	Use as state, if it cannot be avoided (but only if variable appears differentiated and no other potential state with attribute default, prefer, or always can be selected)
Default	Enumeration literal	Use as state if appropriate, but only if variable appears differentiated.
Prefer	Enumeration literal	Prefer it as state over those having the default value (also variables can be selected, which do not appear differentiated).
Always	Enumeration literal	Do use it as a state

## «modelicaExternal»
[ToDo]
## «modelicaAnnotation»
[ToDo] – do we really need to include this? Maybe we can just capture the entire annotation as a string....
## Additional Predefined Types
TO DO: These do not need to be predefined types if we consider treating the declaration equations and modifications explicitly as a Tag. We should include the Modelica expression syntax and the modification syntax as part of our profile definition.  we should move this section to the later in the document, maybe as subsections of 2.1.2 where declarationEquation and modifications are defined.
The following predefined types are not defined in Modelica. The reason for including them is to capture Modelica semantics that would be omitted otherwise. These are used as types for tags or properties where appropriate.
NOTE: It seems like some of the omitted semantics would actually be useful when referring to Modelica models within a SysML model. For instance, when assigning an initial value to a variable, it would often be useful to do so as a function of a quantity defined elsewhere in the SysML model (maybe as a structural property). By representing expressions as text, the semantics of the name of the quantity are lost, making references to other SysML quantities cumbersome to maintain and error prone. SUGGESTION: We need to consider constructs besides a simple string to capture both ModelicaExpression and ModelicaModification.
To illustrate the use of ModelicaExpression and ModelicaModification, consider the following example:

model Oscillator
   import SI = Modelica.SIunits;
  parameter SI.Mass fullMass = 1000;

  /* parameter value defined using ModelicaExpression */
  parameter SI.Mass quarterMass = fullMass/4;

  /* component type modified using ModelicaModifications */
  Modelica.Mechanics.Translational.Components.Mass mass1(
    L=1,
    m=quarterMass,
    s(start=-0.5));
  Modelica.Mechanics.Translational.Components.Spring spring1;
  Modelica.Mechanics.Translational.Components.Fixed fixed1;
equation
  connect(spring1.flange_b, fixed1.flange);
  connect(mass1.flange_b, spring1.flange_a);
end Oscillator;
# Component Declarations
## Overview
In the Modelica language, instances (or usages) of a class are referred to as “components”. In SysML these can be mapped to Block Properties, such as Value Property,, Part Property,, or FlowProperties. Note that Modelica does not have the equivalent of a reference property — properties are never shared. [SysML Spec, pg. 34]]

The following production rules define Modelica Components:

component_clause:
   type_prefix type_specifier [ array_subscripts ] component_list

type_prefix :
   [ flow ]
   [ discrete | parameter | constant ] [ input | output ]

type_specifier :
   name

component_list :
   component_declaration { "," component_declaration }

component_declaration :
   declaration [ conditional_attribute ] comment

conditional_attribute:
   if expression

declaration :
   IDENT [ array_subscripts ] [ modification ]

## «modelicaComponent»

###### Generalizations
property
###### Abstract Syntax

###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes
SysML4Modelica Stereotype «modelicaPart»
Tag Name	Tag Value Type	Multiplicity, Default Value	Comment

isFinal	Boolean	[1], false	final prefix

modification	ModelicaModification	[0..*],	Modification refers to the short-hand notation used in Modelica for modify or redeclare values and types in usages and specialisations. The parenthesis “(” and “)” are omitted.
redeclaration	ModelicaRedeclaration = enumeration (replaceable, redeclare)	[0..1],	replaceable or redeclare prefixes. / Replaceable is necessary to be allowed to redeclare the type. Modifications other than type redeclaration can be made regardless of the replaceable prefix being spedified.
conditionalExpression	ModelicaExpression	[0..1],	The result of ModelicaExpression must be of type Boolean. This string contains the expression. The keyword “if” is omitted. / Only if the condition is true then the «modelicaPart» is created; the condition is only evaluated at compile time and is often used for configuration changes.

arraySize
]One string that contains the full array specification (e.g., “[1,3,:]”	ModelicaExpression	[0..1]	One string that contains the full array specification (e.g., “[1,3,:]”

###### Associations

###### Constraints

###### Example

###### Additional Notes

In order to include all necessary aspects of a component declaration four new stereotypes are introduced. The overarching stereotype for any kind of Modelica component is «modelicaComponent». This stereotype is then further refined into three stereotypes corresponding to the type of construct used as a SysML representation.three sare

SysML / Abstract Syntax Reference	SysML4Modelica
	New Stereotype
UML4SysML::Association and UML4SysML::Property with aggregationKind = composite	«modelicaPart»
UML4SysML::Port	«modelicaPort»

SysML::Blocks::ValueProperty
«modelicaValueProperty»	Applied when the Modelica Component is of specialized class Record or is (a subtype of) one of the predefined (primitive) types

(Note: Component, Usage, Object, Instance are equivalent in Modelica; they are different concepts in SysML – property, instance, type.)

Tag summary for «modelica
Attribute Name	«modelicaPart»	«modelicaPort»	«modelicaValueProperty»
Visibility	•		•
Scope	•		•
Causality		•	•
flowFlag			•
Variability			•
isFinal	•	•	•
modification	•	•	•
redeclaration	•	•	•
conditionalExpression	•	•	•
declarationEquation			•
arraySize	•	•	•

These are common
## «modelicaPart»
###### Generalizations
«modelicaComponent»
###### Abstract Syntax

###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes

###### Associations
###### Constraints

###### Example

###### Additional Notes
The following table lists all associated tags of the «modelicaPart» stereotype. Multiplicity [1] indicates a mandatory value and [0..1] indicates optional values. Empty “Initial Value” field implies an empty string (null).

SysML4Modelica Stereotype «modelicaPart»
Tag Name	Tag Value Type	Multiplicity, Default Value	Comment
Visibility	ModelicaVisibility = enumeration(public, protected)	[1], public	The default value can be omitted in Modelica. Although SysML does not explicitly define visibility, most implementation do have a visibility tag for properties because they are built on top of UML.

scope	ModelicaScope = enumeration(inner, outer)	[0..1], null	“lexical” is not a keyword in Modelica; “lexical” is the default when neither “inner” nor “outer” are specified. Note that the resolution of the scope is performed by the Modelica compiler in the instance hierarchy

## «modelicaPort»
Generalizations
«modelicaComponent»
###### Abstract Syntax

###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes
SysML4Modelica Stereotype «modelicaPort»
Tag Name	Tag Value Type	Multiplicity, Default Value	Comment
Causality	ModelicaCausality = enumeration(input, output)	[0..1], null	“none” is not a keyword in Modelica; “none” is the default when neither “input” nor “output” are specified. / Can only be applied to primitive types, records, or arrays; not to models, blocks, functions.

###### Associations

###### Constraints

###### Example

###### Additional Notes
## «modelicaValueProperty»
###### Generalizations
«modelicaComponent»
Abstract Syntax
###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes
SysML4Modelica Stereotype «modelicaValueProperty»
Tag Name	Tag Value Type	Multiplicity, Default Value	Comment
Visibility	ModelicaVisibility = enumeration(public, protected)	[1], public	The default value can be omitted in Modelica. Although SysML does not explicitly define visibility, most implementation do have a visibility tag for properties because they are built on top of UML.
Scope	ModelicaScope = enumeration(inner, outer)	[0..1], null	“lexical” is not a keyword in Modelica; “lexical” is the default when neither “inner” nor “outer” are specified. Note that the resolution of the scope is performed by the Modelica compiler in the instance hierarchy
Causality	ModelicaCausality = enumeration(input, output)	[0..1], null	“none” is not a keyword in Modelica; “none” is the default when neither “input” nor “output” are specified. / Can only be applied to primitive types, records, or arrays; not to models, blocks, functions.
flowFlag	ModelicaFlowFlag = enumeration(flow, non-flow)	[1], non-flow	“non-flow” is not a keyword in Modelica; “non-flow” is the default when “flow” is not specified. / This tag can only be applied to variables that are a subtype of ModelicaReal. It can only be used inside «modelicaConnector» or to define a Type. Input/output cannot be combined with flow.
Variability	ModelicaVariability = enumeration(constant, parameter, discrete, continuous)	[0..1], continuous	In the context of Modelica, the read-only flag in UML/SysML will be ignored. Although the variability “parameter” could potentially be expressed as “read-only” in SysML, a new tag (variability) is defined to account for all the Modelica variabilities
declarationEquation	ModelicaExpression	[0..1],	The result must be of the same type as the «modelicaPart» itself. Declaration Equation refers to the shorthand notation in Modelica. In this case the value of the tag is the right-hand-expression of the equations. The “=” sign is omitted, i.e., it is implicit.

###### Associations

###### Constraints

###### Example
###### Additional Notes
## «modelicaFunctionParameter»
: Definition of the «modelicaFunctionParameter» stereotype

# Equation and Algorithm Sections
## Overview
Equations and Algorithm are the main Modelica constructs for defining behavior of classes. These constructs are mapped to UML Constraint.

SysML / Abstract Syntax Reference	SysML4Modelica
	New Stereotypes
UML4SysML::Constraint	«modelicaInitialEquation»
UML4SysML::Constraint	«modelicaEquation»
UML4SysML::Constraint	«modelicaInitialAlgorithm»
UML4SysML::Constraint	«modelicaAlgorithm»

Each of the stereotypes includes the tag “specification” which contains the actual equation or algorithm section. The equation itself is captured in the Constraint Specification field.
## «modelicaEquation»
###### Generalizations
Constraint (from UML4SysML)
###### Abstract Syntax

###### Description
###### Attributes
No additional attributes
###### Associations
No additional associations
###### Constraints

###### Example

###### Additional Notes
## «modelicaInitialEquation»
###### Generalizations
Constraint (from UML4SysML)
###### Abstract Syntax

###### Description

###### Attributes
No additional attributes
###### Associations
No additional associations
###### Constraints

###### Example

###### Additional Notes
## «modelicaAlgorithm»
###### Generalizations
Behavior (from UML4SysML)
###### Abstract Syntax

###### Description

###### Attributes

###### Attributes
No additional attributes
Associations
###### No additional associations
###### Example

###### Additional Notes
## «modelicaInitialAlgorithm»
###### Generalizations
Behavior (from UML4SysML)
Abstract Syntax
###### Description

###### Attributes

Associations

Constraints

Example

Additional Notes
## «modelicaConnection»
###### Generalizations
Connector (from UML4SysML)
###### Abstract Syntax

###### Description
The Modelica specialized class model is the most general specialized class. All the Modelica class elements are allowed in models: variables, connectors, sub-models, equations and algorithm sections. A model can include state variables.
###### Attributes

###### Associations

###### Constraints
###### Example
###### Additional Notes

In Modelica the causality of the connector is defined in the type while the flow direction of a FlowPort is associated with a usage. Thus Modelica connector cannot be mapped to FlowPort.
Alternatives:
  - (preferred solution) discard the direction attribute of an atomic FlowPorts, and FlowPort to an instance of a Modelica Connector in a Modelica Model/Block.
  - Connector Modelica is conceptually an interaction point, same is a Port in UML -> Define a new SysML construct form UML Ports, call it ???

Based on alternative 1: «modelicaConnector» is a type for an atomic FlowPort. FlowPort name is the name of the instance of a connector in a «modelicaModel» or «modelicaBlock».
Modelica connection is mapped to SysML connector. No new stereotype provided the FlowPorts are typed by FlowSpecification having «modelicaConnector» applied to it.

UML4SysML:: Connector	Connection clause

# Related non-Modelica Constructs
## «modelicaSimulation»
###### Generalizations
Block
###### Abstract Syntax

###### Description

###### Attributes

###### Associations

###### Constraints

###### Example

###### Additional Notes
«modelicaSimulation» (mapped to SysML Block) is not a Modelica language construct. However, it is introduced in order to distinguish between the model and its simulation. The following tags are associated with this stereotype:

SysML / Abstract Syntax Reference	SysML4Modelica
	New Stereotypes	Constraints
SysML::Blocks::Block	«modelicaSimulation»

SysML4Modelica Stereotype «modelicaSimulation»
Tag Name	Tag Value Type	Default Value	Comment
startTime	Real	0.0	Simulation start time
stopTime	Real	1.0	Simulation stop time
Model	«modelicaModel», «modelicaBlock»		Reference to the model to be simulated

We need to come up with a way to get to the results…