# Part IV ̶̵̶ Transformation
This document defines an incomplete mapping between the SysML4Modelica profile defined in Part II and the abstract syntax defined in Part III. As the definitions found in Part II and III evolve, this transformation document will also change. The majority of this mapping document is composed of tables relating elements in the SysML4Modelica profile to elements of the Modelica abstract syntax. It is also intended to be implementation independent.
Each mapping table may consist of 4 sections:
1. A general statement describing which element in the SysML profile is being mapped to which element of the Modelica abstract syntax.
2. A Required section describing the required conditions necessary to make the transformation valid
3. A Conditional section describing possible links between attributes based on conditional expressions
4. An Attributes section describing the mapping between any additional attributes
# Class Definition
## Overview

: Overview of mapping from new SysML stereotypes to Modelica specialized classes.
SysML4Modelica	Modelica		Attributes
	Abstract Syntax	Concrete Syntax
Classes::ModelicaClassDefinition	Absyn.Class.Class	N/A	See Below
Specializations:
Classes::ModelicaClass	Absyn.Class.Class	Class	See Section Error: Reference source not found
Classes::ModelicaModel	Absyn.Class.Class	Model	See Section Error: Reference source not found
Classes::ModelicaRecord	Absyn.Class.Class	Record	See Section Error: Reference source not found
Classes::ModelicaBlock	Absyn.Class.Class	Block	See Section Error: Reference source not found
Classes::ModelicaConnector	Absyn.Class.Class	Connector	See Section Error: Reference source not found
Classes::ModelicaType	Absyn.Class.Class	Type	See Section Error: Reference source not found
Classes::ModelicaPackage	Absyn.Class.Class	Package	See Section Error: Reference source not found
Classes::ModelicaFunction	Absyn.Class.Class	Function	See Section Error: Reference source not found

SysML4Modelica		Modelica
Classes::ModelicaClassDefinition	maps to	Absyn.Class.Class
Attributes:
IsFinal	always maps to	finalPrefix
IsModelicaEncapsulated	always maps to	encapsulatedPrefix
IsAbstract	always maps to	PartialPrefix

## «modelicaClass»
SysML4Modelica		Modelica
Classes::ModelicaClass	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Class
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaModel»

SysML4Modelica		Modelica
Classes::ModelicaModel	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Model
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaRecord»

SysML4Modelica		Modelica
Classes::ModelicaRecord	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Record
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaBlock»
SysML4Modelica		Modelica
Classes::ModelicaBlock	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Block
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaConnector»
SysML4Modelica		Modelica
Classes::ModelicaConnector	maps to	Absyn.Class.Class
Conditional:
IsExpandable equal to false	maps to	restriction equal to Restriction.R_CONNECTOR
IsExpandable equal to true	maps to	restriction equal to Restriction. R_EXP_CONNECTOR
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaType»

SysML4Modelica		Modelica
Classes::ModelicaType	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Type
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaPackage»

SysML4Modelica		Modelica
Classes::ModelicaPackage	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Package
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaFunction»

SysML4Modelica		Modelica
SysML4Modelica::Classes::ModelicaFunction	maps to	Absyn.Class.Class
Required:
		restriction equal to Restriction.R_Function
Conditional:
IsExternal equal to true		Type of Class.body equal to ClassDef.PARTS / Type of Class.blody.classParts equal to ClassPart.EXTERNAL / Type of Class.body.classParts.externalDecl equal to ExternalDecl.EXTERNALDECL
ModelicaFunction::externalLanguage	Always maps to	Class.body.classParts.externalDecl.lang
ModelicaFunction::externalFunctionSpecification	Always maps to	Class.body.classParts.externalDecl.funcName
Attributes same as SysML4Modelica::Classes::ModelicaClassDefinition

## «modelicaEnumeration»
Currently not covered in this draft.
## «modelicaExtends»
Currently not covered in this draft.
## Short Class Definitions
Currently not covered in this draft.
# Predefined Types
## Overview
The following primitive types are available in the Modelica language: Real Type, Integer Type, Boolean Type, String Type, Enumeration Types, StateSelect, ExternalObject, Graphical Annotation Types. These primitive types are defined as predefined types in SysML4Modelica::BasicTypes. Although these types have direct counterparts in SysML, they are defined again to account for the additional attributes associated with them in Modelica.

SysML4Modelica	Modelica
BasicTypes	Predefined Type
ModelicaReal	Real
ModelicaInteger	Integer
ModelicaBoolean	Boolean
ModelicaString	String
ModelicaEnumeration	Enumeration
ModelicaStateSelect	StateSelect
ModelicaExternalObject	ExternalObject
ModelicaAnnotation	Annotation

# Component Declarations
## Overview

SysML4Modelica	Modelica	Attributes
Component::ModelicaComponent	Absyn.Element.Element	See Section 3.2
Component::ModelicaPart	Absyn.Element.Element	See Section 3.3
Component::ModelicaPort	Absyn.Element.Element	See Section 3.4
Component::ModelicaValueProperty	Absyn.Element.Element	See Section 3.5

## «modelicaComponent»

SysML4Modelica		Modelica
Component::ModelicaComponent	maps to	Absyn.Element.Element
Required:
		Type of specification equal to ElementSpec.COMPONENTS / Type of specification.components equal to ComponentItem.COMPONENTITEM / Type of specification.components.component equal to Componenet.COMPONENT
Attributes:
name	always maps to	name / specification.components.component.name(?)
scope	always maps to	Type of innerOuter
conditionalExpression	always maps to	specification.components.condition
modification	always maps to	specification.components.component.modification
redeclaration	always maps to	redeclareKeywords
arraySize	always maps to	specification.components.component.arrayDim

## «modelicaPart»

SysML4Modelica		Modelica
Component::ModelicaPart	maps to	Absyn.Element.Element
Required:
		Type of specification equal to ElementSpec.COMPONENTS / Absyn.Class.Class referenced by specification.typeSpec has Restriction not equal to R_Connector or R_Type / Type of specification.components equal to ComponentItem.COMPONENTITEM / Type of specification.components.component equal to Componenet.COMPONENT
Attributes:
name	always maps to	name / specification.components.component.name(?)
Scope	always maps to	Type of innerOuter
conditionalExpression	always maps to	specification.components.condition
modification	always maps to	specification.components.component.modification
redeclaration	always maps to	redeclareKeywords
arraySize	always maps to	specification.components.component.arrayDim

## «modelicaPort»

SysML4Modelica		Modelica
Component::ModelicaPort	maps to	Absyn.Element.Element
Required:
		Type of specification equal to ElementSpec.COMPONENTS / Absyn.Class.Class referenced by specification.typeSpec has restriction equal to R_Connector or / Type of specification.components equal to ComponentItem.COMPONENTITEM / Type of specification.components.component equal to Componenet.COMPONENT
Attributes:
name	always maps to	name / specification.components.component.name(?)
conditionalExpression	always maps to	specification.components.condition
modification	always maps to	specification.components.component.modification
redeclaration	always maps to	redeclareKeywords
arraySize	always maps to	specification.components.component.arrayDim

## «modelicaValueProperty»

SysML4Modelica		Modelica
Component::ModelicaValueProperty	maps to	Absyn.Element.Element
Required:
		Type of specification equal to ElementSpec.COMPONENTS / Absyn.Class.Class referenced by specification.typeSpec has restriction equal to R_Type / Type of specification.components equal to ComponentItem.COMPONENTITEM / Type of specification.components.component equal to Componenet.COMPONENT / Type of specification.components.component.attributes equal to ElementAttributes.ATTR
Attributes:
name	always maps to	name / specification.components.component.name(?)
scope	always maps to	Type of innerOuter
flowFlag	always maps to	specification.components.component.attributes.flowPrefix
causality	always maps to	Type of specification.components.component.attributes.direction
variability	always maps to	Type of specification.components.component.attributes.variability
conditionalExpression	always maps to	specification.components.condition
modification	always maps to	specification.components.component.modification
redeclaration	always maps to	redeclareKeywords
arraySize	always maps to	specification.components.component.arrayDim

## «modelicaFunctionParameter»
Currently not covered in this draft.
# Equation and Algorithm Sections
## Overview

SysML4Modelica	Modelica / Abstract Syntax	Attributes
Equations and Algorithms::ModelicaEquation	Absyn.EquationItem.EQUATIONITEM	See Section 4.2
Equations and Algorithms::ModelicaConnection	Absyn.Equation.EQ_CONNECT	See Section 4.3
Equations and Algorithms::ModelicaAlgorithm	Absyn.EquationItem.ALGORITHMITEM	See Section 4.4

## «modelicaEquation»

SysML4Modelica		Modelica
Equations and Algorithms::ModelicaEquation	maps to	Absyn.EquationItem.EQUATIONITEM
Required:
constraint.specification	parsed to	equation
Conditionals:
If IsInitial equal to false		EQUATIONITEM contained in record typed to ClassPart.EQUATIONS
If IsInitial equal to true		EQUATIONITEM contained in record typed to ClassPart.INITIALEQUATIONS

## «modelicaAlgorithm»

SysML4Modelica		Modelica
Equations and Algorithms::ModelicaAlgorithm	maps to	Absyn.AlgorithmItem.ALGORITHMITEM
Required:
constraint.specification	parsed to	algorithm_
Conditionals:
If IsInitial equal to false		ALGORITHMITEM contained in record typed to ClassPart.ALGORITHMS
If IsInitial equal to true		ALGORITHMITEM contained in record typed to ClassPart.INITIALALGORITHMS

## «modelicaConnection»

SysML4Modelica		Modelica
Equations and Algorithms::ModelicaConnection	maps to	Absyn.Equation.EQ_CONNECTOR
Required:
ConnectorEndA.Role	maps to	connector1
ConnectorEndB.Role	maps to	connector2