Date: October 2009

SysML-Modelica
Transformation Specification

Version Alpha 1

____________________________________________________
OMG Document Number: dtc or ptc/200x-xx-xx
Standard document URL: http://www.omg.org/spec/acronym/1.0/PDF
Associated File(s)*: http://www.omg.org/spec/acronym/200xxxxx
  http://www.omg.org/spec/acronym/200xxxxx
____________________________________________________

Source document: Title (document number)
* Original file(s): Title (document number)

List of issues to discuss:
-
Part III Modelica Abstract Syntax
The abstract syntax (AST = abstract syntax tree) of Modelica is not standardized. The abstract syntax described in this document is one possible definition, defined in an extended subset of Modelica (also known as MetaModelica) and used in the OpenModelica specification/implementation of Modelica which originated as a Structural Operational Semantics/Natural Semantics specification, the first version from 1998.
However, even if the abstract syntax of Modelica is not standardized, given the structure of the language as described in this document, the difference in abstract syntax between the different tools are likely to be relatively small. Any difference in terminology or minor differences in structure can be handled with tool-specific transformations that will be performed on the ASTs.
The abstract syntax used in OpenModelica has been designed with several goals in mind:
- Complete representation of all Modelica language constructs.
- Reconstruction of the source code from the AST.
- Use for semantic specification, type checking, and compilation.
Syntax type classes are defined using the uniontype construct. A union type is the union of all the record types it contains. Recursive references to a union type are allowed. Components with optional values are declared at instances of the Option<...> parametrized type constructor. In a few cases the tuple<type1,type2,...> type constructor is used. A tuple type can be described as an anonymous record type, where the record type name and the field names are not defined.
In the following all MetaModelica classes (including a short textual description) are listed (version Oct.2009[1] from the OpenModelica SVN). This definition is translated into an OMG MOF-based description (see http://www.omg.org/mof/) using the Eclipse EMF (http://www.eclipse.org/emf/) implementation of a subset of the OMG MOF standard. The .ecore and .ecorediag files are attached to this document. Please see the files for details and diagrams. The mapping between the MetaModelica and the Eclipse EMF (ecore) is defined as following:
[1] Note: all MetaModelica specific classes are removed.
- MetaModelica package is translated EPackage
- MetaModelica uniontype is translated to EClass (isAbstract)
- MetaModelica record is translated to EClass which inherits from the respective EClass that represents the uniontype)
- MetaModelica record attributes of primitive type is translated to EClass attributes of primitive type
- MetaModelica record attributes of composite type is translated to EClass EReference to the repsective EClass
- MetaModelica types are expanded and translated into EClasses
- MetaModelica tuples are expanded and translated into EClasses with the prefix “tuple_”
- MetaModelica Option<...> implies the multiplicity 0..1
- MetaModelica list<...> implies the multiplicity 0..*
- MetaModelica type Ident = String; is not translated. EString is used directly.
- In order to avoid name clashes between EClasses representing uniontype or record each EClass that represents a uniontype has a prefix “u”.
- In order to improve the structure and readability for each MetaModelica uniontype an EPackage is created with the same name as the uniontype. This EPackage includes the EClass representing the uniontype and EClasses representing the records of the uniontype.
The following figure shows an example of the translation for the MetaModelica uniontype “program” (see MetaModelica code below).

public uniontype Program
"- Programs, the top level construct
   A program is simply a list of class definitions declared at top
   level in the source file, combined with a within statement that
   indicates the hierarchical position of the program."
  record PROGRAM "PROGRAM, the top level construct"
    list<Class> classes "List of classes" ;
    Within within_ "Within clause" ;
    TimeStamp globalBuildTimes "";
  end PROGRAM;
end Program;

public uniontype Within "Within Clauses"
  record WITHIN "the within clause"
    Path path "the path for within";
  end WITHIN;

  record TOP end TOP;

end Within;

uniontype TimeStamp
 record TIMESTAMP
   Real lastBuildTime "Last Build Time";
   Real lastEditTime "Last Edit Time";
  end TIMESTAMP;
end TimeStamp;

public uniontype Class
 "A class definition consists of a name, a flag to indicate
  if this class is declared as partial, the declared class restriction,
  and the body of the declaration."
 record CLASS
    Ident name;
    Boolean partialPrefix "true if partial" ;
    Boolean finalPrefix "true if final" ;
    Boolean encapsulatedPrefix "true if encapsulated" ;
    Restriction restriction "Restriction" ;
    ClassDef body;
  end CLASS;

end Class;

public uniontype ClassDef
"The ClassDef type contains the definition part of a class declaration.
 The definition is either explicit, with a list of parts
 (public, protected, equation, and algorithm), or it is a definition
 derived from another class or an enumeration type.
 For a derived type, the type contains the name of the derived class
 and an optional array dimension and a list of modifications."

  record PARTS
    list<ClassPart> classParts;
    Option<String> comment;
  end PARTS;

  record DERIVED
    TypeSpec typeSpec "typeSpec specification includes array dimensions" ;
    ElementAttributes attributes;
    list<ElementArg> arguments;
    Option<Comment> comment;
  end DERIVED;

  record ENUMERATION
    EnumDef enumLiterals;
    Option<Comment> comment;
  end ENUMERATION;

  record OVERLOAD
    list<Path> functionNames;
    Option<Comment> comment;
  end OVERLOAD;

  record CLASS_EXTENDS
    Ident baseClassName "name of class to extend" ;
    list<ElementArg> modifications "modifications to be applied to the base class";
    Option<String> comment "comment";
    list<ClassPart> parts "class parts";
  end CLASS_EXTENDS;

  record PDER
    Path functionName;
    list<Ident> vars "derived variables" ;
  end PDER;

end ClassDef;

public uniontype TypeSpec "ModExtension: new MetaModelica type specification!"
  record TPATH
    Path path;
    Option<ArrayDim> arrayDim;
  end TPATH;

  record TCOMPLEX
    Path path;
    list<TypeSpec> typeSpecs;
    Option<ArrayDim> arrayDim;
  end TCOMPLEX;

end TypeSpec;

public uniontype EnumDef
  "The definition of an enumeration is either a list of literals
     or a colon, \':\', which defines a supertype of all enumerations"
  record ENUMLITERALS
    list<EnumLiteral> enumLiterals;
  end ENUMLITERALS;

  record ENUM_COLON end ENUM_COLON;

end EnumDef;

public uniontype EnumLiteral "EnumLiteral, which is a name in an enumeration and an optional
   Comment."
  record ENUMLITERAL
    Ident literal;
    Option<Comment> comment;
  end ENUMLITERAL;

end EnumLiteral;

public uniontype ClassPart "A class definition contains several parts. There are public and
  protected component declarations, type definitions and `extends\'
  clauses, collectively called elements. There are also equation
  sections and algorithm sections. The EXTERNAL part is used only by functions
  which can be declared as external C or FORTRAN functions."
  record PUBLIC
    list<ElementItem> contents ;
  end PUBLIC;

  record PROTECTED
    list<ElementItem> contents;
  end PROTECTED;

  record EQUATIONS
    list<EquationItem> contents;
  end EQUATIONS;

  record INITIALEQUATIONS
    list<EquationItem> contents;
  end INITIALEQUATIONS;

  record ALGORITHMS
    list<AlgorithmItem> contents;
  end ALGORITHMS;

  record INITIALALGORITHMS
    list<AlgorithmItem> contents;
  end INITIALALGORITHMS;

  record EXTERNAL
    ExternalDecl externalDecl "externalDecl" ;
    Option<Annotation> annotation_ "annotation" ;
  end EXTERNAL;

end ClassPart;

public uniontype ElementItem "An element item is either an element or an annotation"
  record ELEMENTITEM
    Element element;
  end ELEMENTITEM;

  record ANNOTATIONITEM
    Annotation annotation_ ;
  end ANNOTATIONITEM;

end ElementItem;

public uniontype Element "Elements
  The basic element type in Modelica"
  record ELEMENT
    Boolean finalPrefix;
    Option<RedeclareKeywords> redeclareKeywords "replaceable, redeclare" ;
    InnerOuter innerOuter "inner/outer" ;
    Ident name;
    ElementSpec specification "Actual element specification" ;
    Info info "File name the class is defined in + line no + column no" ;
    Option<ConstrainClass> constrainClass "constrainClass ; only valid for classdef and component" ;
  end ELEMENT;

  record DEFINEUNIT
    Ident name;
    list<NamedArg> args;
  end DEFINEUNIT;

  record TEXT
    Option<Ident> optName "optName : optional name of text, e.g. model with syntax error. We need the name to be able to browse it..." ;
    String string;
    Info info;
  end TEXT;

end Element;

public uniontype ConstrainClass "Constraining type, must be extends"
  record CONSTRAINCLASS
    ElementSpec elementSpec "elementSpec ; must be extends" ;
    Option<Comment> comment "comment" ;
  end CONSTRAINCLASS;

end ConstrainClass;

public uniontype ElementSpec "An element is something that occurs in a public or protected section in a class definition. There is one constructor in the
    `ElementSpec\' type for each possible element type. There are
    class definitions (`CLASSDEF\'), `extends\' clauses (`EXTENDS\')
    and component declarations (`COMPONENTS\').

    As an example, if the element `extends TwoPin;\' appears
    in the source, it is represented in the AST as
    `EXTENDS(IDENT(\"TwoPin\"),{})\'."

  record CLASSDEF
    Boolean replaceable_ "replaceable" ;
    Class class_ "class" ;
  end CLASSDEF;

  record EXTENDS
    Path path "path" ;
    list<ElementArg> elementArg "elementArg" ;
    Option<Annotation> annotationOpt "optional annotation";
  end EXTENDS;

  record IMPORT
    Import import_ "import" ;
    Option<Comment> comment "comment" ;
  end IMPORT;

  record COMPONENTS
    ElementAttributes attributes "attributes" ;
    TypeSpec typeSpec "typeSpec" ;
    list<ComponentItem> components "components" ;
  end COMPONENTS;

end ElementSpec;

public uniontype InnerOuter "One of the keyword inner and outer CAN be given to reference an inner or
      outer component. Thus there are three disjoint possibilities."
  record INNER end INNER;

  record OUTER end OUTER;

  record INNEROUTER end INNEROUTER;

  record UNSPECIFIED end UNSPECIFIED;

end InnerOuter;

public uniontype Import "Import statements, different kinds"
  // A named import is a import statement to a variable ex;
  // NAMED_IMPORT("SI",Absyn.QUALIFIED("Modelica",Absyn.IDENT("SIunits")));
  record NAMED_IMPORT
    Ident name "name" ;
    Path path "path" ;
  end NAMED_IMPORT;

  record QUAL_IMPORT
    Path path "path" ;
  end QUAL_IMPORT;

  record UNQUAL_IMPORT
    Path path "path" ;
  end UNQUAL_IMPORT;

end Import;

public uniontype ComponentItem "Collection of component and an optional comment"
  record COMPONENTITEM
    Component component "component" ;
    Option<ComponentCondition> condition "condition" ;
    Option<Comment> comment "comment" ;
  end COMPONENTITEM;

end ComponentItem;

public type ComponentCondition = Exp "A componentItem can have a condition that must be fulfilled if the component should be instantiated." ;

public uniontype Component "Some kind of Modelica entity (object or variable)"
  record COMPONENT
    Ident name "name" ;
    ArrayDim arrayDim "arrayDim ; Array dimensions, if any" ;
    Option<Modification> modification "modification ; Optional modification" ;
  end COMPONENT;

end Component;

public uniontype EquationItem "Several component declarations can be grouped together in one
  `ElementSpec\' by writing them on the same line in the source.
  This type contains the information specific to one component."
  record EQUATIONITEM
    Equation equation_ "equation" ;
    Option<Comment> comment "comment" ;
  end EQUATIONITEM;

  record EQUATIONITEMANN
    Annotation annotation_ "annotation" ;
  end EQUATIONITEMANN;

end EquationItem;

public uniontype AlgorithmItem "Info specific for an algorithm item."
  record ALGORITHMITEM
    Algorithm algorithm_ "algorithm" ;
    Option<Comment> comment "comment" ;
  end ALGORITHMITEM;

  record ALGORITHMITEMANN
    Annotation annotation_ "annotation" ;
  end ALGORITHMITEMANN;

end AlgorithmItem;

public uniontype Equation "Information on one (kind) of equation, different constructors for different
     kinds of equations"
  record EQ_IF
    Exp ifExp "ifExp ; Conditional expression" ;
    list<EquationItem> equationTrueItems "equationTrueItems ; true branch" ;
    list<tuple<Exp, list<EquationItem>>> elseIfBranches "elseIfBranches" ;
    list<EquationItem> equationElseItems "equationElseItems Standard 2-side eqn" ;
  end EQ_IF;

  record EQ_EQUALS
    Exp leftSide "leftSide" ;
    Exp rightSide "rightSide Connect stmt" ;
  end EQ_EQUALS;

  record EQ_CONNECT
    ComponentRef connector1 "connector1" ;
    ComponentRef connector2 "connector2" ;
  end EQ_CONNECT;

  record EQ_FOR
    ForIterators iterators;
    list<EquationItem> forEquations "forEquations" ;
  end EQ_FOR;

  record EQ_WHEN_E
    Exp whenExp "whenExp" ;
    list<EquationItem> whenEquations "whenEquations" ;
    list<tuple<Exp, list<EquationItem>>> elseWhenEquations "elseWhenEquations" ;
  end EQ_WHEN_E;

  record EQ_NORETCALL
    ComponentRef functionName "functionName" ;
    FunctionArgs functionArgs "functionArgs; fcalls without return value" ;
  end EQ_NORETCALL;

  record EQ_FAILURE
    EquationItem equ;
  end EQ_FAILURE;

end Equation;

public uniontype Algorithm "The Algorithm type describes one algorithm statement in an
  algorithm section. It does not describe a whole algorithm. The
  reason this type is named like this is that the name of the
  grammar rule for algorithm statements is `algorithm\'."
  record ALG_ASSIGN
    Exp assignComponent "assignComponent" ;
    Exp value "value" ;
  end ALG_ASSIGN;

  record ALG_IF
    Exp ifExp "ifExp" ;
    list<AlgorithmItem> trueBranch "trueBranch" ;
    list<tuple<Exp, list<AlgorithmItem>>> elseIfAlgorithmBranch "elseIfAlgorithmBranch" ;
    list<AlgorithmItem> elseBranch "elseBranch" ;
  end ALG_IF;

  record ALG_FOR
    ForIterators iterators;
    list<AlgorithmItem> forBody "forBody" ;
  end ALG_FOR;

  record ALG_WHILE
    Exp boolExpr "boolExpr" ;
    list<AlgorithmItem> whileBody "whileBody" ;
  end ALG_WHILE;

  record ALG_WHEN_A
    Exp boolExpr "boolExpr" ;
    list<AlgorithmItem> whenBody "whenBody" ;
    list<tuple<Exp, list<AlgorithmItem>>> elseWhenAlgorithmBranch "elseWhenAlgorithmBranch" ;
  end ALG_WHEN_A;

  record ALG_NORETCALL
    ComponentRef functionCall "functionCall" ;
    FunctionArgs functionArgs "functionArgs; general fcalls without return value" ;
  end ALG_NORETCALL;

  record ALG_RETURN
  end ALG_RETURN;

  record ALG_BREAK
  end ALG_BREAK;

  // Part of MetaModelica extension. KS
  record ALG_TRY
    list<AlgorithmItem> tryBody;
  end ALG_TRY;

  record ALG_CATCH
    list<AlgorithmItem> catchBody;
  end ALG_CATCH;

  record ALG_THROW
  end ALG_THROW;

  record ALG_MATCHCASES
    list<Exp> switchCases;
  end ALG_MATCHCASES;

  record ALG_GOTO
    String labelName;
  end ALG_GOTO;

  record ALG_LABEL
    String labelName;
  end ALG_LABEL;
  //-------------------------------

end Algorithm;

public uniontype Modification "Modifications are described by the `Modification\' type. There
  are two forms of modifications: redeclarations and component
  modifications.
  - Modifications"
  record CLASSMOD
    list<ElementArg> elementArgLst;
    Option<Exp> expOption;
  end CLASSMOD;

end Modification;

public uniontype ElementArg "Wrapper for things that modify elements, modifications and redeclarations"
  record MODIFICATION
    Boolean finalItem "finalItem" ;
    Each each_ "each" ;
    ComponentRef componentReg "componentReg" ;
    Option<Modification> modification "modification" ;
    Option<String> comment "comment" ;
  end MODIFICATION;

  record REDECLARATION
    Boolean finalItem "finalItem" ;
    RedeclareKeywords redeclareKeywords "redeclare or replaceable " ;
    Each each_ "each" ;
    ElementSpec elementSpec "elementSpec" ;
    Option<ConstrainClass> constrainClass "class definition or declaration" ;
  end REDECLARATION;

end ElementArg;

public uniontype RedeclareKeywords "The keywords redeclare and replacable can be given in three different kombinations, each one by themself or the both combined."
  record REDECLARE end REDECLARE;

  record REPLACEABLE end REPLACEABLE;

  record REDECLARE_REPLACEABLE end REDECLARE_REPLACEABLE;

end RedeclareKeywords;

public uniontype Each "The each keyword can be present in both MODIFICATION\'s and REDECLARATION\'s.
  - Each attribute"
  record EACH end EACH;

  record NON_EACH end NON_EACH;

end Each;

public uniontype ElementAttributes "- Component attributes"
  record ATTR
    Boolean flowPrefix "flow" ;
    Boolean streamPrefix "stream" ;
// Boolean inner_ "inner";
// Boolean outer_ "outer";
    Variability variability "variability ; parameter, constant etc." ;
    Direction direction "direction" ;
    ArrayDim arrayDim "arrayDim" ;
  end ATTR;

end ElementAttributes;

public uniontype Variability "Variability"
  record VAR end VAR;
  record DISCRETE end DISCRETE;
  record PARAM end PARAM;
  record CONST end CONST;

end Variability;

public uniontype Direction "Direction"
  record INPUT end INPUT;
  record OUTPUT end OUTPUT;
  record BIDIR end BIDIR;

end Direction;

public type ArrayDim = list<Subscript> "Component attributes are
  properties of components which are applied by type prefixes.
  As an example, declaring a component as `input Real x;\' will
  give the attributes `ATTR({},false,VAR,INPUT)\'.
  Components in Modelica can be scalar or arrays with one or more
  dimensions. This type is used to indicate the dimensionality
  of a component or a type definition. Array dimensions" ;

public uniontype Exp "The Exp uniontype is the container of a Modelica expression.
  - Expressions"
  record INTEGER
    Integer value;
  end INTEGER;

  record REAL
    Real value;
  end REAL;

  record CREF
    ComponentRef componentReg;
  end CREF;

  record STRING
    String value;
  end STRING;

  record BOOL
    Boolean value;
  end BOOL;

  record BINARY "Binary operations, e.g. a*b"
    Exp exp1;
    Operator op;
    Exp exp2;
  end BINARY;

  record UNARY "Unary operations, e.g. -(x)"
    Operator op "op" ;
    Exp exp "exp Logical binary operations: and, or" ;
  end UNARY;

  record LBINARY
    Exp exp1 "exp1" ;
    Operator op "op" ;
    Exp exp2 ;
  end LBINARY;

  record LUNARY "Logical unary operations: not"
    Operator op "op" ;
    Exp exp "exp Relations, e.g. a >= 0" ;
  end LUNARY;

  record RELATION
    Exp exp1 "exp1" ;
    Operator op "op" ;
    Exp exp2 ;
  end RELATION;

  record IFEXP "If expressions"
    Exp ifExp "ifExp" ;
    Exp trueBranch "trueBranch" ;
    Exp elseBranch "elseBranch" ;
    list<tuple<Exp, Exp>> elseIfBranch "elseIfBranch Function calls" ;
  end IFEXP;

  record CALL
    ComponentRef function_ "function" ;
    FunctionArgs functionArgs ;
  end CALL;

  // stefan
  record PARTEVALFUNCTION "Partially evaluated function"
    ComponentRef function_ "function" ;
    FunctionArgs functionArgs ;
  end PARTEVALFUNCTION;

  record ARRAY "Array construction using {, }, or array"
    list<Exp> arrayExp ;
  end ARRAY;

  record MATRIX "Matrix construction using {, } "
    list<list<Exp>> matrix ;
  end MATRIX;

  record RANGE "Range expressions, e.g. 1:10 or 1:0.5:10"
    Exp start "start" ;
    Option<Exp> step "step" ;
    Exp stop "stop";
  end RANGE;

  record TUPLE " Tuples used in function calls returning several values"
    list<Exp> expressions "comma-separated expressions" ;
  end TUPLE;

  record END "array access operator for last element, e.g. a{end}:=1;"
  end END;

end Exp;

uniontype FunctionArgs "The FunctionArgs uniontype consists of a list of positional arguments followed by a list of named arguments (Modelica v2.0)"
  record FUNCTIONARGS
    list<Exp> args "args" ;
    list<NamedArg> argNames "argNames" ;
  end FUNCTIONARGS;

  record FOR_ITER_FARG
     Exp exp "iterator expression";
     ForIterators iterators;
  end FOR_ITER_FARG;

end FunctionArgs;

uniontype NamedArg "The NamedArg uniontype consist of an Identifier for the argument and an expression
  giving the value of the argument"
  record NAMEDARG
    Ident argName "argName" ;
    Exp argValue "argValue" ;
  end NAMEDARG;

end NamedArg;

uniontype Operator "Expression operators"
  /* arithmetic operators */
  record ADD "addition" end ADD;
  record SUB "subtraction" end SUB;
  record MUL "multiplication" end MUL;
  record DIV "division" end DIV;
  record POW "power" end POW;
  record UPLUS "unary plus" end UPLUS;
  record UMINUS "unary minus" end UMINUS;
  /* element-wise arithmetic operators */
  record ADD_EW "element-wise addition" end ADD_EW;
  record SUB_EW "element-wise subtraction" end SUB_EW;
  record MUL_EW "element-wise multiplication" end MUL_EW;
  record DIV_EW "element-wise division" end DIV_EW;
  record POW_EW "element-wise power" end POW_EW;
  record UPLUS_EW "element-wise unary minus" end UPLUS_EW;
  record UMINUS_EW "element-wise unary plus" end UMINUS_EW;
  /* logical operators */
  record AND "logical and" end AND;
  record OR "logical or" end OR;
  record NOT "logical not" end NOT;
  /* relational operators */
  record LESS "less than" end LESS;
  record LESSEQ "less than or equal" end LESSEQ;
  record GREATER "greater than" end GREATER;
  record GREATEREQ "greater than or equal" end GREATEREQ;
  record EQUAL "relational equal" end EQUAL;
  record NEQUAL "relational not equal" end NEQUAL;
end Operator;

uniontype Subscript "The Subscript uniontype is used both in array declarations and component references. This might seem strange, but it is inherited from the grammar. The NOSUB constructor means that the dimension size is undefined when used in a declaration, and when it is used in a component reference it means a slice of the whole dimension. - Subscripts"
  record NOSUB end NOSUB;

  record SUBSCRIPT
    Exp subScript "subScript" ;
  end SUBSCRIPT;

end Subscript;

uniontype ComponentRef "A component reference is the fully or partially qualified name of a component. It is represented as a list of identifier- -subscript pairs. - Component references and paths"
  record CREF_QUAL
    Ident name "name" ;
    list<Subscript> subScripts "subScripts" ;
    ComponentRef componentRef "componentRef" ;
  end CREF_QUAL;

  record CREF_IDENT
    Ident name "name" ;
    list<Subscript> subscripts "subscripts" ;
  end CREF_IDENT;

  record WILD end WILD;

end ComponentRef;

uniontype Path "The type `Path\', on the other hand,
  is used to store references to class names, or names inside
  class definitions."
  record QUALIFIED
    Ident name "name" ;
    Path path "path" ;
  end QUALIFIED;

  record IDENT
    Ident name "name" ;
  end IDENT;

  record FULLYQUALIFIED "Used during instantiation for names that are fully qualified, i.e. the names are looked up from top scope directly like for instance Modelica.SIunits.Voltage
Note: Not created during parsing, only during instantation to speedup/simplify lookup."
    Path path;
  end FULLYQUALIFIED;
end Path;

uniontype Restriction "These constructors each correspond to a different kind of class declaration in Modelica, except the last four, which are used for the predefined types. The parser assigns each class declaration one of the restrictions, and the actual class definition is checked for conformance during translation. The predefined types are created in the Builtin module and are assigned special restrictions."

  record R_CLASS end R_CLASS;
  record R_MODEL end R_MODEL;
  record R_RECORD end R_RECORD;
  record R_BLOCK end R_BLOCK;
  record R_CONNECTOR "connector class" end R_CONNECTOR;
  record R_EXP_CONNECTOR "expandable connector class" end R_EXP_CONNECTOR;
  record R_TYPE end R_TYPE;
  record R_PACKAGE end R_PACKAGE;
  record R_FUNCTION end R_FUNCTION;
  record R_ENUMERATION end R_ENUMERATION;
  record R_PREDEFINED_INT end R_PREDEFINED_INT;
  record R_PREDEFINED_REAL end R_PREDEFINED_REAL;
  record R_PREDEFINED_STRING end R_PREDEFINED_STRING;
  record R_PREDEFINED_BOOL end R_PREDEFINED_BOOL;
  record R_PREDEFINED_ENUM end R_PREDEFINED_ENUM;
  record R_UNIONTYPE "MetaModelica uniontype" end R_UNIONTYPE;

end Restriction;

public uniontype Annotation "An Annotation is a class_modification.- Annotation"
  record ANNOTATION
    list<ElementArg> elementArgs "elementArgs" ;
  end ANNOTATION;

end Annotation;

public uniontype Comment "Comment"
  record COMMENT
    Option<Annotation> annotation_ "annotation" ;
    Option<String> comment "comment" ;
  end COMMENT;

end Comment;

public uniontype ExternalDecl "Declaration of an external function call - ExternalDecl"
  record EXTERNALDECL
    Option<Ident> funcName "The name of the external function" ;
    Option<String> lang "Language of the external function" ;
    Option<ComponentRef> output_ "output parameter as return value" ;
    list<Exp> args "only positional arguments, i.e. expression list" ;
    Option<Annotation> annotation_ ;
  end EXTERNALDECL;

end ExternalDecl;

public type ForIterator = tuple<Ident, Option<Exp>>
"For Iterator -
   these are used in:
   * for loops where the expression part can be NONE and then the range
     is taken from an array variable that the iterator is used to index,
     see 3.3.3.2 Several Iterators from Modelica Specification.
   * in array iterators where the expression should always be SOME(Exp),
     see 3.4.4.2 Array constructor with iterators from Specification";

public type ForIterators = list<ForIterator>
"For Iterators -
   these are used in:
   * for loops where the expression part can be NONE and then the range
     is taken from an array variable that the iterator is used to index,
     see 3.3.3.2 Several Iterators from Modelica Specification.
   * in array iterators where the expression should always be SOME(Exp),
     see 3.4.4.2 Array constructor with iterators from Specification";