## Slide 1: Digital Engineering User Stories (DEUS) Model
Modeling Guidelines
Veejay Gorospe
veejay.gorospe@3ds.com

## Slide 2: Agenda
DEUS Model Purpose & Focus
Model Structure & Organization
  Packages Structure
  Element Locations
  Project Usages & Structure
Modeling Guidelines
Modeling Resources

## Slide 3: DEUS Model Objective and Purpose
Digital Engineering User Stories (DEUS) Model
Use case model of digital engineering
The DEUS model is a use case model of digital engineering
  Mostly behavioral activity (SysML) / OV-5b-like (DODAF)
The objective of this modeling effort is NOT to design everything about a Digital Engineering
The objective is to understand:
  The logical inputs and outputs of Digital Engineering as a block box
  The functional dependencies between those inputs and outputs
  With the goal of informing the DVM
Digital Viewpoint Model (DVM)
Information model supporting digital information exchange
<<informs>>

## Slide 4: Model Structure & Organization

## Slide 5: Model Structure & Organization
Package Structure – Top-level Overview
The model is broken up into 3 main sections
  “00 Common” – Contains any elements that are common between use cases
  “01 Use Cases” – Contains the elements specific to each use case
  “02 Use Case Analysis” – Contains element elements for use case analysis
Additionally:
  There is a specific profile for the model’s language customizations (“DEUS Profile”)
  There is a package for any project usages (“_Shared Models”)

## Slide 6: Model Structure & Organization
Package Structure – Common Package Overview
The “00 Common” package currently contains for sub packages for organization
  “Behaviors”
  “Information & Data”
  “Performers”
  “Other Elements”
The “Performers” package contains the main performer of “Digital Engineering Enterprise”

## Slide 7: Model Structure & Organization
Package Structure – Use Case Package Overview
The “01 Use Cases” package contains the main packages for use case information
  Each use case package is labeled as “Use Case ID – Use Case Name”
  Each use case package has its own organization of model elements:
    “Behaviors”
    “Information & Data”
    “Performers”

## Slide 8: Model Structure & Organization
Element Locations – Use Cases
Use Case elements and its corresponding working package should be located in the “01 Use Cases” package
The use case’s package should be named “Use Case ID – Use Case Name” for model organization

## Slide 9: Model Structure & Organization
Element Locations – Activities
The top-level activity for the use case should be located under the use case element
  The normal containment relationship between use case and activity
Any other behaviors related to the use case are located in the “Behaviors” package of the use case’s package
Any common behaviors will be in the “Behaviors” package of the common area

## Slide 10: Model Structure & Organization
Element Locations – Blocks
Blocks should be used for Performers & Information/Data
  Any use case-specific blocks will be located in the appropriate package in the use case’s package
  Any common blocks will be located in the appropriate package in the common area
For now, there’s no stereotype between Performer blocks and Information/Data Blocks
  We’re just going to rely on package organization

## Slide 11: Model Structure & Organization
Element Locations – Other Elements
Any other elements of definition (e.g. signals) should be located in the appropriate “Other Elements” package

## Slide 12: Model Structure & Organization
Project Usages & Structure Overview
Any projects usages in the DEUS model are located in the “_Shared Models”
Right now, there is only one project usage:
  Local usage to the “DEIXWG Common Libraries.mdzip” file
    “DEIXWG Common Libraries.mdzip” must be in the same folder location as the DEUS model file
DEUS Model
<<uses>>
DEIXWG Common Libraries

## Slide 13: Model Structure & Organization
Project Usages & Structure – DEIXWG Common Libraries
The DEIXWG Common Libraries model file is for any common model elements for the DEIXWG effort
Currently is only used by the DEUS model
  Can eventually be used by the DVM
Currently has two glossaries:
  Technical Management Processes Glossary from ISO/IEC/IEEE 15288-2015
  Selected Model Lexicon Glossary (http://markblackburn.com/MBSE/model_lexicon.html)
DEIXWG Common Libraries

## Slide 14: Modeling Guidelines

## Slide 15: Modeling Guidance
# | Guideline | Description
MG1 | Element Location | Elements are located as per the model structure & organization.
MG2 | Element Documentation | Documentation fields of blocks (e.g. Performers, Information, Data, etc.) and other elements (e.g. Signals) are filled out and complete.
MG3 | Use Case Attributes | Use case attributes are filled out and complete
MG4 | Activity Decomposition | Complex activities are grouped together in a containing activity with its own diagram.
MG5 | DEE Swimlane Required | A swimlane that represents the Digital Engineering Enterprise block is in one of the use case’s activities.
MG6 | Information/Data Flow Required | Information and data is represented in a use case as the type on action pins with object flows connecting the pins. At lease one flow in a use case is required.
MG7 | Information/Data Generalization | Information and data blocks are sub-classes of a generic information/data block where possible. Identify generic block classes with the “Is Abstract” attribute.

## Slide 16: Modeling Guidelines
General Guidelines – MG2: Element Documentation
Make sure that all blocks and elements in the “other elements” packages have their documentation filled out and complete
There are tables in these packages to help fill the information out

## Slide 17: Modeling Guidelines
General Guidelines – MG3: Use Case Attributes
Make sure that the use case attributes are filled out and complete
Use case table is located in the “01 Use Cases” package
Attribute | Description
Use Case ID | ID of the use case
Use Case Name | Name of the use case
Author | Author(s) / stakeholder(s) of the use case information (not the modelers).
Goal | Main objective of the use case (i.e. what is achieved when executing these steps).
Assumption | Any expectations that are necessary for the use case to execute.
Pre Condition | Any conditions that are absolutely required in order for the use case to execute.
Post Condition | Any conditions that are asserted upon the completion of the use case.
Notes | Any use case notes.
Model Developer | Model developers of the use case
Applicable Technical Process | Any applicable ISO/IEC/IEEE 15288-2015 Technical Process that the use case applies to.

## Slide 18: Modeling Guidelines
General Guidelines – MG3: Use Case Attributes (Continued)
To better understand the use case’s context in time, we attribute the use case with applicable technical management processes from the ISO/IEC/IEEE 15288-2015

## Slide 19: Modeling Guidelines
General Guidelines – MG4: Activity Decomposition
Make sure to group complex activities into its own containing activity
  Helps to organize use case steps

## Slide 20: Modeling Guidelines
General Guidelines – MG5: DEE Swimlane Required
Make sure that somewhere in a use case’s activities, there is a swimlane that uses the Digital Engineering Enterprise block
  It represents the functional entity that helps to describe the DVM metamodel

## Slide 21: Modeling Guidelines
General Guidelines – MG6: Information/Data Flow Required
Make sure to represent information/data flow on an activity diagram by typing the pins attached to the actions
There needs to be at least one information/data flow on an activity for the use case
  Otherwise, why do we have this use case if it has no information/data flow for the DVM?

## Slide 22: Modeling Guidelines
General Guidelines – MG7: Information/Data Generalization
Make sure to group classes of common information and together using the generalization relationship
Classes that are generic should be marked with the “Is Abstract” attribute
  It makes the block names in italics as per the SysML spec

## Slide 23: Modeling Resources

## Slide 24: Modeling Resources
Use Case Questioning – Use Cases General
Question | Potential Modeling Effect
What are the end goals of the use case? | Updating the “Goal” attribute of the use case
What are the assumptions of the use case? | Updating the “Assumption” attribute of the use case
What are the pre-conditions of the use case? | Updating the “Pre Condition” attribute of the use case
What are the post-conditions of the use case? | Updating the “Post Condition” attribute of the use case
Are the expectations before the start of the use case generalities (assumptions) or absolutes (pre-conditions)? | Moving some assumptions to pre-conditions and vice-versa
Where in a system life cycle does this use case apply to? | Updating the “Applicable Technical Process” attribute of the use case

## Slide 25: Modeling Resources
Use Case Questioning – Performers
Question | Potential Modeling Effect
Who are the performers in the use case? | Determines the performer blocks for the use case
Are specific performers individuals or organizations? | Update names and documentation description for performer blocks (e.g. “Test Engineer” vs “Test Team”)
Which performers are driving the action in the use case (Primary Actors)? | Helps with understanding the sequence of use case steps
Which performers are responding to the action in the use case (Secondary Actors)? | Helps with understanding the sequence of use case steps
How is the Digital Engineering Enterprise (DEE) involved in this use case? | Helps with understanding which steps the DEE will execute in the use case
Are there existing performers that I can reuse? | Helps with model reuse

## Slide 26: Modeling Resources
Use Case Questioning – Information/Data
Question | Potential Modeling Effect
What information/data is required by the use case? | Determines the information/data blocks for the use case
Can some of these information/data be grouped together within the same information class? | Determines any information/data blocks used as abstract classes and generalization
Does this information/data have any properties? | Determines any modeling of value properties within information/data blocks
Do I need to decompose this information/data to accurately represent this information/data within reason? | Determines any composition and structure of information/data blocks
Are there existing information/data elements that I can reuse? | Helps with model reuse

## Slide 27: Modeling Resources
Use Case Questioning – Behavioral Modeling
Question | Potential Modeling Effect
What are the steps to the use case? | Determines the atomic activities and activity sequence for the use case
Can some of these use case steps be grouped together? | Determines the higher level grouping activities for the use case
Which performers are executing the use case step? | Determines where to place activity actions in respect to the swimlanes
Are there any data/information dependencies between two use case steps? | Determines if object flows are needed between activity actions
How many instances of data/information are needed between to use case steps? | Determines the multiplicity of the input and output pins between activity actions
Do any performers need to make a decision in the use case? | Determines if decision nodes are needed and which swimlanes are they located