## Slide 1: Use of Modeling in Hardware Development - Summary of interviews, practice reviews to date for INCOSE Model Management Working Group
8/22/2011

## Slide 2: Approach
Interviewed colleague from IBM legacy Microelectronics Division
Interviewed, reviewed process documentation from BAE Electronic Solutions and Land &Armaments/US Combat Systems
Summary of IBM, BAE ES surveys attached
BAE USCS colleague will review draft working group materials to add additional best practices, provide additional process information to help identify concepts to genericize for MBSE application
8/22/2011

## Slide 3: IBM – System on a chip (SOC) modeling
Utilized for highly complex SoC products
  3.3 billion circuits, 10 miles wire, 5.2 GHz optimized for speed and density
  Modeling employed in two capacities: chip design and verification of chip design
Mature tools
  Synopsys products (chip design, verification), Cadence products (testability, physical layout), IBM internal tools (synthesis, timing, functional verification), various vendor/freeware (design libraries)
  Requirement input parameterized (e.g. technology, frequency, …)
  Library tools and librarians control model versions, enforce naming conventions (e.g. model cannot be check-in w/o proper naming)
  Librarian oversees design set-up/startup, tool updates, design compatibility with tool updates
  Tool vendors compete for entire design lifecycle so integration among them is difficult
  IBM develops tool add-ons in house to address custom design approach and special requirements
Team leads define library structure with librarian for geographically disperse team to access same version of same product during development, test, manufacture
  “Published” by setting up library structure/folders in shared area
  Clear ownership of library set-up, design configuration control : single person or small group
  Build library and its history may be maintained separately to a working library and its history, tool dependent
  Libraries backed up usually automatically and nightly, transparent to design and verification teams
Defined/assigned hierarchy of design elements comprising the system
Library of mature design elements (cores) employed for functionality as needed
Chip design built by integrating elements (“synthesizing”) in bottoms up fashion according to hierarchy
  Model builds are iterative, occurring weekly
  Verification commences as function becomes available
    Verification plan tightly coordinated with design plan
  Generally integrated with verification models at completion of build
Verification comprehensive, tightly coordinated with design plan
    Timing verification done in parallel with synthesis
    Verification includes functional, communication, control, performance, fabrication checkout (good/bad assessment), testability
    Model builds are iterative, occurring weekly
Design and verification teams meet to individually vote go/no go to Fab
  “Go” must be unanimous
8/22/2011

## Slide 4: BAE Electronic Solutions – Mechanical (3D solids/CAD) modeling
Utilized for all 3D solid deliverables
Mature tools
  PTC Pro/Engineer (Pro/E), Pro/INTRALINK, Windchill products, Dassault Enovia Product Data/Lifecycle Managers (PDM/PLM)
  Control versions, revisions, all components, prepare and manage drawings
  Support multiple sources of data (e.g. DOORS, Synopsys, Cadence….)
Library of commonly used components maintained in modeling tools (PTC, Dassault)
  Models meet pre-defined library criteria
Model creation, maintenance, management guidelines and detailed requirements defined, published. Requirements enforced.
Summary of practice, guidance and detailed requirements :
  Ensure proper modeling techniques utilized and modeling consistency by running ModelCHECK (PTC) tool often to analyze parts, assemblies, drawings. Errors must be corrected. Warnings should be corrected
  Demonstrate compliance to part, assembly, drawing, minimum/un-dimensioned drawing requirements prior to release and design drafting checking by running ModelCHECK (PTC) tool
  Include Interface Drawing requirements in Interface Drawing model
  Interface Drawing model(s) must be created, associated with Assembly Top Level model(s)
    Interface Drawing model(s) automatically updates when Top Level Assembly model(s) modified
  State when during design stages Interface Drawing model(s) and Drawing(s) may need to be created or updated
  State Interface Drawing structure, file naming
  Advise to model of placeholder elements
  Define Part or Assembly model elements needed by Operations to extract module data in support of manufacturing documentation and procedures
8/22/2011

## Slide 5: BAE Electronic Solutions – Mechanical (3D solids/CAD) modeling
Summary of practice, guidance and detailed requirements :
  Define common elements for part models: including file name according to prescribed convention, title, material/density, finish, layers (visibility of model items), solid tolerances, surface quality, cage code, part number, START PART which includes default co-ordinate system, layer names, EXPORT, TITLE, NOTES, MATERIAL, FINISH note titles, model parameters and their default values, etc…
  Define common elements for assembly models: including file name according to prescribed convention, title, material/density, finish, layers, solid tolerances, surface quality, cage code, part number, START ASSEMBLY which includes default co-ordinate system, layer names, EXPORT, TITLE, NOTES, MATERIAL, FINISH note titles, model parameters and their default values, etc...
  Define Standard part and assembly configurations
    some options may be over-ridden, others cannot
  Define model window configurations to give all modelers same tool GUI look/feel
  Define supervisory configurations to ensure standard option enforcement for Company sector
  Common tool (INTRALINK) for database management for storage, history, coordination of design objects, baseline management for part and assembly models
  Associate casting models with machining models so that changes to casting model will regenerate machining model
  Utilize standard drawing formats, standard set up files (drawing height, dimensions, note text, text orientation, font properties, drafting standards, etc.), revision history block, title block, views, symbols, BOM tables, etc. for 2D drawings
  Identify common model element for cable/pipe/hardline and their routing
  Create models for procured parts or assemblies and their association to minimally dimensioned drawings, un-dimensioned drawings or no drawings
8/22/2011

## Slide 6: BAE Electronic Solutions – Mechanical (3D solids/CAD) modeling
Summary of practice, guidance and detailed requirements :
  Define file naming conventions for models and drawings. Cannot be changed by the project/engineer
    Restrictions and prescriptives for Company specific part numbers, library part numbers, vendor parts, families of models (e.g. multiple install locations), legacy data
    Model type (e.g. part, assembly) and versions are automatically assigned by the tool
  Define board design model (START BOARD), then communication to Printed Circuit Design colleagues
    Standardized data format standard for translation/incorporation into Mentor Graphics tool
    Reverse translation to ensure intent not lost
  Define characteristics of community library models, how to submit and maintain for those commonly used
    Librarian checklist to ensure new entrant compliance to requirements
  File management of CAD data in concurrent engineering environment using Pro/INTRALINK, including set-up, logging in, folder structure, actions permitted based on user roles, check in/out, specific functions of the tool
8/22/2011