## Slide 1: Infrastructure Bridge Model
Matthew Hause – Atego Chief Consulting Engineer Matthew.Hause@Atego.com

## Slide 2: Introduction
Model Purpose
  Investigate whether MBSE provides benefits to infrastructure projects
  Provide concrete examples of infrastructure issues
  Clarify requirements
  Elicit discussion
Implemented using Atego Artisan Studio
  UPDM for the high level architecture
  SysML for the detailed view
  Explanation and commentary are contained in the notes section of each slide.
For more information contact
  Matthew.Hause@Atego.com

## Slide 3: Problem Statement
1. General Background
  The city of Autoville has just elected a new city council with a mandate to build a drawbridge connecting two points across the Tiger river at Jones Landing. The bridge has to allow for automobile, commuter rail, pedestrian, and bicycle traffic. The bridge must accommodate vessel of a category 4 up to 50 feet in height. After receiving a grant of $1 Billion from the federal government, the council must deliver this bridge by Jan 30, 2018. Construction must start before the next council election.

## Slide 4: Requirements
The requirements specified by the management are:
  Expected daily rail ridership is 100,000 passengers
  AM peak is 6:30 to 9:30 and PM peak is 4:00 to 7:00, and peak unidirectional ridership is 10,000 passengers per hour
  Expected vehicular traffic is 1,000 cars per hour in the inbound direction in the AM peak, and 1,250 cars in the outbound direction in the PM peak. Six lanes of traffic, three in each directions to be provided
  Pedestrian and bicycle traffic across the bridge shall be provided and shall be separated from vehicular traffic
  Manned operations with 10 expected openings per day, with a vertical lift type.
  Height of the bridge to be determined, consistent with size 4 vessel types
  Commercial (ASASHTO HL93) heavy vehicle traffic is allowed throughout the day.

## Slide 5: Requirements
The requirements specified by the management are:
  - Provide access for emergency vehicles
  Provide capability to coordinate vessel movement and drawbridge operations.
  12 hours a day operation provided by an Operator House
  The system has to operate under all weather conditions
  The system must be available 99.99% for all functions when called upon
  - System must meet all applicable federal and state laws and regulations
  - The system shall have an operational life of not less than 50 years.
  - The capital cost of the system shall not exceed $1 Billion.
  - The operations and maintenance cost of the system shall not exceed $10M per year.
  - The system shall be operational by Jan 30th, 2018.

## Slide 6: Requirements Diagram – Can also show traceability
Shows requirements traceability
Can be linked to DOORS and other requirements management tools
Notes: A Requirement Diagram allows you to model relationships between requirements, and model traceability relationships between requirements and items in the model. Requirements can be imported from DOORS or any other requirements management tool.

## Slide 7: Bridge System Capabilities
Notes: A CV-2 defines the taxonomy of Capabilities, that is, the inheritance structure. A Capability is a high-level specification of an ability or capability that achieves specific objectives. An Enterprise will consist of many Capabilities, each used in various combinations with other Capabilities to achieve the declared vision, goals and objectives of the Enterprise. A Capability may evolve over time with regard to how it is delivered but its specific objective typically remains unchanged.
In this diagram we have added the traceability to the requirements defined earlier.

## Slide 8: Requirements Traceability Table
Notes: A Requirement Table presents traceability information in a tabular format. You can specify the Packages that are searched for items. You can add columns to show properties and linked items for the Requirements shown in the table. Note that by default a Requirement Table also shows satisfied items. You can configure a Requirements Table to show items relating to Requirements through other SysML relationship types.

## Slide 9: Goals and Visions
Notes: A CV-1 defines an Enterprise Phase in terms of its goals, visions, enduring tasks and exhibited Capabilities. This gives the high level planning view of the enterprise. It also helps to clearly state the purpose of the project/enterprise.

## Slide 10: Concept Elements in Structural Format
Notes: An OV-1a defines the context of an architecture. It's purpose is to communicate with stakeholders to create a shared understanding of the project. This version contains structured elements (boxes in boxes.) The group felt that the version on the following slide would be more effective in communicating the context.

## Slide 11: Bridge Concept Element Relationships
Notes: This diagram shows the bridge structure in the center and its connecting elements as well as elements connecting to those elements. It illustrates the main concepts in the bridge project. However, the blue boxes would not be effective in communicating with non-experts.

## Slide 12: Concept Elements with added graphics
Notes: This diagram has the exact same set of elements as the previous slide. However, the blue boxes have been replaced with graphics to improve the diagram and help communications.

## Slide 13: Sample Stakeholders and Their Associated Goals Shown in Use Case Format
Notes: Use cases model how the system is going to be used in a given context, giving you an overall picture of the system, from a user's point of view. A Use Case Diagram details the possible ways in which a system can be used, that is, the Use Cases, and the interaction of objects in the system to implement those Use Cases. This type of modeling is now widely accepted as being the best means of establishing functional user requirements and of feeding those along the development lifecycle. In this way, the Use Case Model provides an efficient communication mechanism between users and developers. In this example, we have listed the various stakeholders and the goals that they have in relation to the bridge. The operator house requirement (lower center) has been added to demonstrate how requirements traceability can be added to any diagram.
On a Use Case Diagram you can create Actors and Use Cases, and the relationships between them:
· Inheritance between Actors or Use Cases.
· Interactions between Actors and Use Cases.
· Extend Flows between Use Cases.
· Include Flows between Use Cases.

## Slide 14: Measurement Definitions
Notes: An AV-3 Measurement Definition defines Measurement Sets and Measures. A Measurement Set is a set or collection of Measures and is stereotyped as a SysML Value Type. These measurement sets can be used throughout the model to define quantifiable measures of the system.

## Slide 15: Actual Measurements
Notes: An AV-3 Actual Measurements defines Actual Measurement Sets and Actual Measurements. After creating Measurement Sets and Measures on an AV-3 Measurement Definition, you can create Actual Measurement Sets and Actual Measurements on an AV-3 Actual Measurements diagram. These can be associated with model elements and used to evaluate the system.

## Slide 16: Some Example Exchanges
Notes: An OV-2 defines the internal Needlines and exchanges in the context of the Performer or Logical Architecture that owns the OV-2. It is meant to show a logical view of the system and normally includes the interactions between the main elements in the system. In this case, the east and west locations of the river have been shown as the two elements and the interactions include trains and pedestrians among others. This differs from the traditional version of the diagram which would show only information interactions.

## Slide 17: Organizations
Bridge Organization for Operations
Notes: An OV-4 Organizational Relationships Chart (Typical) defines the typical organizational structures through Organization Types, Person Role Types and Persons. An Organization Type is a group of persons, associated for a particular purpose. A Person Role Type is a type of point of contact or responsible person. The concept also includes a billet or job definition. A Person is a classifier for an Actual Person that can appear on an OV-4 Organizational Relationships Chart (Actual). The diagram is used to define the organizations and roles and command and control structures in the enterprise. These can be used throughout the rest of the model. In this case, we have defined the Autoville Bridge Organization and Traffic Management organizations/departments and their personnel.

## Slide 18: Construction and Inspection Organizations
Notes: A sample of external organizations are shown in the diagram. These include the construction company, bridge inspection, EPA, and coast guard as well as their personnel. The Traffic Control Personnel has a compartment showing the standards to which the person filling the post will need to conform such as headware and high-visibility garments. These are covered in the standards diagrams.

## Slide 19: Users of the Bridge
Notes: The bridge users are listed in this diagram. Some of these such as the Pedestrian will be used as interchange elements as they will cross from one side of the bridge to the other.

## Slide 20: System Components
Notes: An SV-9 defines Materiel, Capabilities, Systems, Skills, Organization Types, Person Role Types and Software. Forecasts can be associated with these elements. It is in class diagram format and the elements defined here can be used throughout the model. A Materiel is a combination of physical elements, energy and data that are combined and used to accomplish a task or function. Software is the software needed for the functioning of the system that is typically included as expected background functionality, such as an operating system. It could also be used to define essential functionality such as the bridge control software. A System is a combination of organizational aspects and equipment that combine to provide a functionality.

## Slide 21: System Context Diagram
Notes: An SV-1/SvcV-1 defines the structure of Resources and the elements that flow between them. In this case the diagram is used to describe the bridge context in terms of the Bridge Structure, the Bridge Control System and its main interfacing systems. Interactions include the passing of Pedestrians, the creation of Dynamic Load, Supply of Electricity, and telemetry information.

## Slide 22: External Interfacing Systems
Notes: The external systems that interface to the Bridge are defined here. These were used in the SV-1 Bridge Context Diagram.

## Slide 23: Using Systems
Systems and users of the bridge
Notes: These are the systems that will use and traverse the bridge. Some of these will be shown as interactions in the structural and context diagrams.

## Slide 24: Signaling Systems
Notes: This diagram uses the same context as the [System] Bridge Context [SV-1 Structure Interaction] diagram. In order to keep the diagrams simple and readable, the signaling systems are shown on this separate diagram. Architects are often tempted to include several levels of detail on these types of diagrams causing them to become extremely busy and unusable. This was partly due to problems in the modeling tools with maintaining a consistent context. The SysML basis of these diagrams provides the means to keep detail to a manageable level and provides separation of concerns normally found in infrastructure projects such as wiring, structure, control, plumbing, etc.

## Slide 25: SV-1 Barriers
Notes: Along similar lines, the Barriers and control systems and signals are shown on this diagram. This also includes the lift mechanism for the bridge.

## Slide 26: Operator Interactions
Notes: The final SV-1 diagram shows the Bridge control systems and the interactions with the Bridge Operator.

## Slide 27: Bridge Control Systems
Notes: The internal elements of the Bridge Control System is shown here demonstrating the required functionality of control and communication.

## Slide 28: Bridge Control Systems
Notes: The internal components of the bridge control system and their interfaces are shown here. In this diagram the standard orange boxes have been replaced with graphics showing typical systems that would be used.

## Slide 29: Supporting Systems
Notes: The Bridge maintainer is a supporting system that needs to be further developed.

## Slide 30: Ship Passing Sequence
Notes: An SV-10c/SvcV-10c defines the behavior of resources through interactions. The vertical bars represent parts of the system and the horizontal arrows are the flows previously defined on the structural diagrams. The large bars are called interaction frames and are references to sub-sequences. This helps reduce the complexity of the diagrams and allows for reuse. The diagram is normally owned by the structural context. This limits the interactions on the diagram to the systems, materiel, etc. and interactions that are found in that context. In this way, multiple contexts can be created and the sequences for them are consistent.

## Slide 31: Open Drawbridge
Notes: The open sequence is the diagram referenced in the previous diagram. It shows the sub-sequence for the open drawbridge interactions. It shows the parallel sequences of the barriers being closed to prevent traffic and pedestrians from crossing the bridge. This ensures safety of the bridge users. Once that has completed, the bridge itself starts to lift.

## Slide 32: Close Drawbridge
Notes: Like the open sequence, this diagram is referenced in the ship passing diagram. It shows the sub-sequence for the close drawbridge interactions. The bridge closes first. Once that has completed, the parallel sequences of the barriers being opened is executed to allow traffic and pedestrians to cross the bridge. This ensures safety of the bridge users.

## Slide 33: Functions of Bridge and Systems
Notes: An Activity (System) defines the behavior of a System in terms of tasks that are performed by the resource. An SV-4/SvcV-4 Systems & Services Functionality Decomposition defines the call tree for Activity (System) elements. It is used to define the functional breakdown of an activity. In this case, it defines the Ship Passing Execution. The diamond represents the functional breakdown of the activities: The Ship Passing Execution activity is made up of Open Bridge, Close Bridge, etc. The Bridge Structure, Ship, and Bridge Operator perform those functions as is shown on the diagram. Although it shows the functional breakdown, it down not show the order of execution. That is shown on the Activity Diagram.

## Slide 34: Ship Passing Sequence Activities
Notes: An SV-4/SvcV-4 Systems & Services Functionality Description defines the actions that are involved with the Activity (System). This diagram describes the Ship Passing Execution activity. Like the Sequence diagram, the activity diagram is used to show a sequence. However, the Sequence Diagram is message based showing messages passing between structural elements and the activity diagram is activity based. It shows the execution order of a set of activities. The vertical columns represent structural elements that have been previously defined and are called swimlanes. The elements representing the swimlanes execute the activities. For example, the Bridge Structure performs the Detect Ship, Open Bridge and Close Bridge activities.

## Slide 35: Open Bridge Activity Sequence
Notes: This activity diagram shows the Open Bridge sequence. It is an initial version as the swimlanes have not yet been added. It shows the initial activation of the warning systems followed by the lowering of the barriers. These will be further decomposed for the various systems. Finally after traffic has been stopped the bridge will be raised.

## Slide 36: Close Bridge Activity Sequence
Notes: This shows the reverse sequence of the Open Bridge sequence. The warning systems are activated, the bridge is lowered, and only after the system is safe does the system allow traffic and trains to pass.

## Slide 37: Functional Hierarchy of Open Bridge Activity
Notes: The SV-4 functional hierarchy documents the functional breakdown of the Open Bridge Activity. It was created by populating the sub-activities created on the Open Bridge activity diagram.

## Slide 38: Functional Hierarchy of Close Bridge Activity
Notes: The SV-4 functional hierarchy documents the functional breakdown of the Close Bridge activity. It was created by populating the sub-activities created on the Close Bridge activity diagram.

## Slide 39: Generated Interface Report (Partial)
Notes: The spreadsheet represents a partial Interface Control Document (ICD) for the Bridge System. This is a standard document that is created for any system of interest. It has been automatically generated from the structural diagrams. The activity columns are currently blank as the structural and functional parts of the model have not yet been linked.

## Slide 40: SV-3 Bridge Systems Interface Matrix
Notes: The SV-3 Bridge Systems Interface Matrix is an automatically generated report that shows the interactions between the various systems. An “X” is inserted at the intersection of the interconnected systems. This is also known as an N2 (N-Squared) diagram.

## Slide 41: Bridge Data
Notes: This diagram is used to define the data or information that is exchanged in the model. This can take the for of specific data formats or simply define the type of data that is to be exchanged.

## Slide 42: Non-Data Interface Definitions
Notes: The elements here represent non-data or system types of exchanges. These are energy exchanges of the type Dynamic Load, Seismic, Electricity and Static Load. These can be used as exchange elements in the structural model.

## Slide 43: Bridge Capabilities and Supporting Systems
Notes: The Capabilities have been updated with their realizing systems. A realizing system is one that accomplishes the desired outcome of the capability. For example, Bridge Control is realized or implemented by the Bridge Operator and the Bridge Control System.

## Slide 44: System to Capabilities Cross Reference Matrix
Notes: The system to capabilities cross reference matrix summarizes the capabilities and the systems that realize those capabilities. It is a useful report to verify that all the required capabilities have systems that implement them.

## Slide 45: Construction and Operational Standards
Notes: The standards views are used to define the different standards to which various parts of the system must conform. A random selection of infrastructure related standards from various countries and states have been assembled to illustrate examples. These standards can be linked to model elements as shown on the referenced diagrams.

## Slide 46: Standards Compliance Matrix
Notes: The standards compliance matrix lists the defined standards and the systems that conform to them. This is automatically generated from the model.

## Slide 47: Standards Conformance Example – Human
Notes: The Traffic Control Personnel has had an additional compartment listing the standards to which personnel must conform.

## Slide 48: Standards Conformance Example – System
Notes: The Bridge Structure and Bicycle Lane have compartments listing their conforming standards.

## Slide 49: System Simulation - Overview
Done with behavior-based diagrams
  State Diagrams
  Activity Diagrams
Useful to:
  Verify system functionality
  Validate user requirements
  Create user interface prototypes
Implementation largely dependent on individual tools
Notes: Simulation can also be added to the model to explore the behavioral parts of the model. This is done using the state and activity diagrams. Capabilities will vary depending on the different tools.

## Slide 50: System Simulation – Simulation Context
The BridgeTest Block defines the context for the simulation
  Made up of a Bridge Controller and Bridge Animator
  Behavior is executed with state diagrams
  A very simple example to elicit further discussion
Notes: This is a simple demonstrator model just to show what is possible. It shows the bridge controller and the animator. It has been included to help get feedback on the model.

## Slide 51: System Simulation – Controller State Diagram
Defines the various states of the system
  In this simple example, the bridge is raised and lowered periodically.
    Time based simulation
  Controls can be added to simulate a user interface
    Event based simulation
Notes: The model shows the states of the bridge being raised and lowered. It can be coordinated with the various lights and other elements of the models as well. There is a time aspect as well as an event based execution of the model.

## Slide 52: System Simulation – Traffic Light State Diagram
Warning light state diagram – also time driven.
Notes: This state machine shows the states of the warning lights on the bridge. If the bridge is raised, traffic is stopped via the red light.

## Slide 53: System Simulation – Main Structures
Notes: The Bridge Test simulation is made up of Red, Amber, and Green Traffic lights, a push button and the bridge lift mechanism modelled as an LED display. Artisan Studio has the ability to create user interfaces as well as animate the state diagrams shown earlier.

## Slide 54: System Simulation – Example Interface
Example Controller simulation block showing the inputs and outputs.
  Interfaces are defined using SysML ports
Notes: This diagram shows more detail of the interfaces on the controller, which was included in the previous slide.

## Slide 55: System Simulation SySim Interface
SySim is designed for systems engineers
  No programming necessary
  Generate and run with a single button
  Provides user interface components using Visual Studio
Notes: This shows the system simulator or SySim interface. The various buttons allow you to generate executables for the model and to animate them.

## Slide 56: System Simulation – Example User Interface
Simple Traffic Light and Bridge Lift Mechanism
Notes: This simple example shows the blue bridge lift mechanism and the traffic light.

## Slide 57: System Simulation – Execution of Simulation
Notes: The example shows the state diagrams being animated while the user interface shows the traffic light and bridge lift mechanism corresponding to the states. The bridge is lifting so the light is red. This was created using minimal effort as an example of the type of simulation that can be done. A more detailed simulation will be created based on feedback from the group.

## Slide 58: Next?
Your feedback on the model would be useful.