## Slide 1
Using MBSE for Operational Analysis
CubeSat Challenge Team
In Affiliation with the Jet Propulsion Laboratory, California Institute of Technology
Notes: Change magicdraw, to nomagic

## Slide 2: CubeSat Challenge Team
JPL
JPL
  Louise Anderson
  Christopher Delp
  Elyse Fosse
  Bjorn Cole
  Leo Cheng
Uni
  Sara Spangelo
  James Cutler
AGI
  David Kaslow
Phoenix Inte
  Grant Soremekun
Int
  Manas Bajaj
  Rose Yntema

## Slide 3: Agenda
MBSE Initiative
Motivation
Radio Explorer Mission (RAX) using SysML
Overview of Analysis Demonstrations
Analysis Demonstrations
  Operations Prediction of State
    Phoenix Integration - ModelCenter
  Spacecraft Control (Flight-Ground)
    Cameo Simulation Toolkit
  Acausal Analysis & Requirements
    Paramagic
  Document Generation and Editing
Results
Future Plans
Notes: First step was building a model and next step these are the kind of analysis you can do, different kind of simulations predictors and how you tie it
Standard inables inter-operation cheaper then in house development

## Slide 4: INCOSE Space Systems Challenge Team
Demonstrate Applicability of MBSE to Space Systems
  Launched and Operational Mission
  Sharable
    INCOSE is an International Organization
Broad Team
  NASA, CSA
  Industry
  Academia (MIT, GIT, Umich)

## Slide 5: INCOSE Space Systems Challenge Team
5 years of MBSE Investigations and Demos
  FireSat Model
    Industry and Academic participation
  Space Systems Library
    Parametric Library based on SMAD (Wertz & Larson)
  CubeSat Application
    Framework
    Integrated Tools

## Slide 6: Better Systems Engineering
Modeling as a Means

## Slide 7: Driving Idea: Systems Engineering Specifications
Systems Engineers in the Space Domain Produce Information
  Functions
    Describing the Problem
    Trades
    System Functional and Behavioral Design
    Specifying System Components and Integrations
    Verification and Validation (V&V)
    Deployment and Fielding
    Operational Support
  Products
    Analysis (Simulation, Tests, etc)
    Reports on Analysis
    Plans
    Design Descriptions
    Interface Descriptions
    Requirements
Relationships are primarily inter-disciplinary
Notes: Model based instead of document centric
How this differs from things done in past

## Slide 8: Challenge: Communication and Consistency
Challenges
  Communicating the system in a world of models
    How do you extract all the rich detail from these simulations into System Specification?
    DOORS? Documents/Slides/Spreadsheets?
    How do you assert mutual consistency between models?
    Meetings? Emails?
Need an equally rich mechanism for expressing the system design
    Human readable
    Machine readable
Notes: * DOORS is a tool used for requirements capture

## Slide 9: Role of Languages in MBSE Enterprise
From multiple points of view
  Capture and express information about the system
  Provide analyzable representations of the system
  Authoritative source of information about the system

## Slide 10: CubeSats?
NanoSatellite (1-10kg)
  Used for Space Research, Technology Demonstrations
1U = 10 cm^3, 2U, and 3U
Ultra Low Cost Missions
  University/Company Training
  COTS Hardware
First CubeSat Launched in 2003
  Over 75+ CubeSats in Operation
ISIS. "CubeSat Concept - Satellite Missions." CubeSat Concept - Satellite Missions. N.p., n.d. Web. 13 Jan. 2013. <https://directory.eoportal.org/web/eoportal/satellite-missions/c-missions/CubeSat-concept>
Notes: Difficulty in CubeSats
Low Cost Missions
Usually not funded at high enough levels, to do conventional systems engineering
Commonly CubeSats are power constrained

## Slide 11: Radio Aurora Explorer (RAX)
Michigan Exploration Lab and SRI International CubeSat mission
Space Weather Missions
  Study plasma irregularities in the ionosphere
  Disturbs Ground-Space Communication and Navigation
Science Experiment
  Bistatic Radar Configuration
  Radar signal transmitted by Incoherent Scatter Radar Site
    Poker Flats, Alaska
Science Data
  Processed on-board and compressed
  Download to a globally distributed network
  Commanded by control center in Ann Arbon, Michigan
Notes: How about changing the remaining points to:
-Space weather mission
-Study plasma irregularities in the ionosphere
- Disturbs ground-space communication and navigation
- Science experiment:
-Bistatic radar configuration
-Radar signal transmitted by Incoherent Scatter Radar site in Poker Flat, Alaska
-Science data:
-processed on-board and compressed
-downloaded to a globally distributed network
-commanded by control center in Ann Arbor, Michigan

## Slide 12: Demonstration Overview
System Model Description
  CubeSat Framework
  RAX Implementation
Power Prediction Analysis
  Power loads analysis driven by operational scenario
Spacecraft Behavior Prediction Analysis
  Spacecraft state analysis driven by operational scenario
Communication Design and Requirements Analysis
  Design criteria and constraints based on design parameters
Document Generation and Reporting
  Document and reports of model and analysis

## Slide 13: Value of Integrated MBEE
Authoritative Source
Standard Based Communication and Description
Relatively Low Cost
Model Repository
System Modeling Tools
View Editor
Docweb
(Document Artifacts)
Analysis Tools
STK
Paramagic
Phoenix ModelCenter
RAX System Model
RAX Analysis Models
Notes: Talk about day in the life of cubesat engineer here…

## Slide 14: CubeSat Framework
Mission Adaptable
Each piece of CubeSat Mission modeled
  Environment, Flight, Ground
Notes: The block definition diagram for the CubeSat mission consists at the highest level of a CubeSat Mission Element and Space Environment. Also shown are the Stakeholder and the Mission Objective.
The process starts with identifying the stakeholders as well as understanding 1) the problems to be solved, 2) the goals the system is intended to support, and 3) the effectiveness measures for evaluating how well the system supports the goals.
The Mission Element is the solution to achieving the Mission Objective.
Modeling of the Space Environment can include its effects on the orbit, communication, and component degradation.
The Mission Element decomposes into a Flight System and Ground System.
We had several discussions as to the use of the word Flight System. The words by themselves could mean just the on-board hardware and software responsible for basic spacecraft operations. To others, the words mean the entire satellite - the bus, solar panels, subsystems, hardware, software, and data. The diagram shows that it is the latter.
There was the same type of discussion on the ground system. It is not just the space - ground communication system. It is everything that needed to operate the satellites and carry-out the mission objective.
We began our work by extending sysML to the specific development domain of cubesats. Having an underlying framework gives a basis for all other cubesats missions to take and build upon a common set of languages.

## Slide 15: Modeling RAX
Notes: Speak both to the modeling patterns and what it tells you about the missions
RAX is an earth science mission, it has a ground system and flight system, it has these subsystems. The model is describing the mission.

## Slide 16: Communication Subsystem
Communication Subsystem – Signal to Noise Ratio Analysis
  SysML Parametrics
Notes: Model showing architecture of the communications subsystem and how it relates to a specific analysis for the communication system, you can see things that the model reflects about rax, such as the communication subsystems components….blah blah

## Slide 17: Power Analysis
Power Subsystem – Power Analysis
  SysML Parametric
Notes: Model showing architecture of the communications subsystem and how it relates to a specific analysis for the communication system, you can see things that the model reflects about rax, such as the communication subsystems components….blah blah

## Slide 18: System Components & Behaviors

## Slide 19: RAX Flight System Behavior
State Machine
Activity Diagram
Flight System States

## Slide 20: RAX Report Generation

## Slide 21: Results & Successes
Effectively described different views of RAX System
Analyzed the RAX Model according to common practices in Space Systems Engineering
Analysis completed with COTS Tools
  Integrated around standard SysML models
Demonstrated capability to generate Documents from models
“Develop With What you Fly With” End to End Integration and Analysis concept

## Slide 22: Summary of Issues and Challenges
Gaps in full integration of Analysis
  Scalable enterprise access to model data
  No master orchestrator controlling timing and coordination for all possible analysis execution
Both SysML and MBSE analysis tools are limited in temporal semantics
  Time is key factor for space systems engineering
  Limited applicability of parametrics to behavior aspects of the model
Notes: Parametrics only allow connections ot values. They cant constrain other objects, behaviors etc.

## Slide 23: Demo Videos

## Slide 24: Affiliation: Jet Propulsion Laboratory, California Institute of Technology Acknowledgments: Part of this research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration Copyright: Copyright 2013. All rights reserved.

## Slide 25: QUESTIONS?

## Slide 26: Backup
Successes and Challenge for each demo

## Slide 27: Power Scenario Demo Overview
Motivation
  “Bringing the model to life”, executing model
  Replaces “hacked” integrated software (e.g. manual/ complex code)
Integrating multiple software tools
  MagicDraw (SysML), Systems Tool Kit (STK), Matlab
  Phoenix ModelCenter (PHX) acts as “glue”
What does this enable?
  “Batch” execution of scenarios (i.e. full time history at once)
  Evaluation if requirements are satisfied/objective
  Test/compare scheduling algorithms (heuristic, optimized, etc.)
  Automatically re-run different scenarios (e.g. vary orbit, network)
  Parametric studies: Sensitivity to vehicle/ network parameters

## Slide 28: Power Scenario: Lessons Learned
Useful things we “figured out” (with vendor support):
Extracting time-dependent parameters (e.g. position in STK)
Passing vectors between simulators was equally useful in PHX
Things to keep in mind for future modeling:
Ensure you have required licenses! (may require vendor support)
Parametric diagrams must inherit inputs/ outputs of PHX models
Exploit existing code/ scenarios as much as possible
Maintain modularity so can re-configure code for different applications

## Slide 29: Document Generation
Models are great, still need to support reviews and presentations
Generate document artifacts from the model
  Leverage ISO 42010 (with some extensions)
Domain Specific Experts and Reviewers should NOT have to go back to the model to do their job
Need a way to present the model-based document artifacts to others without requiring others to understand the model.

## Slide 30: Challenge Team History
2007 – First Challenge Team was Founded
2007-2010
  SysML Model of FireSat (SMAD Textbook)
    SysML Suitability for modeling space missions
2011 – CubeSat Initiative Began
  CubeSat Modeling Framework
  Foundation to model/design many current and future CubeSat missions
2012
  Applying SysML Framework to Operational Mission

## Slide 31: Timeline of Activity
Y1: MIT/GaTech Student FireSat Example
Y2-4: SysML model of FireSat
  Space Analysis Library using SMAD (Space Mission Analysis and Design textbook, Wertz and Larson)
  Basic Model of FireSat
  Solar Panel Trade
  Satellite Toolkit Integration
Y5->: CubeSat: An Architecture Framework and Method for Space Systems MBSE

## Slide 32: FireSat MIT/GaTech Collaboration
Build an integrated model of FireSat
  SubSystems in Matlab, STK, Excel
  Integrated with Phoenix Model Center
  Student Teams Mentored by Industry Experts from INCOSE SSWG
Successes
  executable trade model for FireSat
Challenges
  Difficult to build
  SubSystem models were difficult to integrate
  No architecture of the model integration or key parameters
  Difficult to Audit for completeness correctness

## Slide 33: FireSat SysML Model
Build SysML model of FireSat
  Learn SysML
  Describe FireSat using SysML
  Compare Model Description against typical document representation
Successes
  Models of descriptions from book
  Model views corresponding to documents
Challenges
  Technique of modeling and applying the methodology
  Table representations
  Model Analysis
  Document Production

## Slide 34: SysML Space Analysis Library
Build SysML Space Analysis Library
  Build Library of analysis from SMAD
  Build approach to VnV for Library
Successes
  Libraries for many analysis types
  Useful testing approach
Challenges
  Deep subject – much could not be captured
  Executability (significantly improved since)
  Units and Dimensions (significantly improved since)
  Presentation of equations

## Slide 35: FireSat Solar Panel Trade
Use Library to replicate Solar Panel Sizing Trade
  FireSat Model and Library-> executable trade
Successes
  Successfully built executable trade
  Hard-linked to requirements
  Powerful view of driving systems properties
Challenges
  Executability (improving since)
    Debugging
    Scaling

## Slide 36: FireSat Integrated Modeling
Integrate FireSat SysML Model with Satellite ToolKit
  Exchange Orbit Scenario properties
Successes
  Basic Exchange of Parameters
  Direct comparison of MBSE in SysML and STK
  Explicit link between models and requirements
Challenges
  Integration
    Complicated
    Difficult to Scale

## Slide 37: CubeSat: Framework and Method
Build a Modeling Framework and Method for CubeSats
  CubeSat Domain-Specific Terms
  SE Framework for Modeling CubeSat Missions, Spacecraft, and Ground Systems
  Example Application using RAX Mission
Successes
  First version of Framework
  Early version of multiple executable demos
Challenges
  Resources
  Executability
  Integration

## Slide 38: Consensus of Team
Modeling with SysML
  Everything was hard at first
  Methodology is critical to a model that hangs together
  SysML simplified construction of basic things like functions and properties
  SysML tastes like early CAD apps
  Libraries of model analysis were effective in making solar panel trade
  Integration with STK
Document Comparison
  Model unified properties between views
  Simplified understanding of the System
  The common SysML language improved communication between teams and simplified collaboration
  Automated reports allowed for more time to focus on engineering