## Slide 1
Ontologies and Model-Based Systems Engineering
Steven Jenkins
Principal Engineer
Systems and Software Division
Jet Propulsion Laboratory
California Institute of Technology
Copyright © 2010 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Models Are Information Structures
Every model, whether it’s a differential equation, a simulation, or a SysML drawing, organizes concepts and properties into meaningful relationships.
These concepts, properties, and relationships can be unique to a model, or they can be common to a family of models.
To the degree that they’re common:
  models can be compared, contrasted, and reused.
  engineers can understand what’s communicated by a model without retraining.
  engineers can focus on creating and understanding, not explaining.
Can we come up with a common set of concepts, properties, and relationships for systems engineering? Absolutely.
  That doesn’t mean everyone is saddled with one-size-fits-all.
  The common set is for common things. Unique things are handled by extensions.
These concept, property, and relationship definitions are called an ontology.

## Slide 3: Names vs Classifiers
Suppose we have a thing named “Star Tracker A”.
Without an ontology, what can we infer about this thing?
We just have to “know” that it’s probably
  a piece of hardware with a reference identifier
  a mechanical component with mass properties
  a electronic component with power properties
  a thing with interfaces
Too much of this knowledge is implicit. If we wanted to automate production of a master equipment list, how would the algorithm know to include this thing and not another thing called “flight software”? How would it ask for the thing’s mass?
This is easy to solve if we keep separate
  what the thing is called (to a first order, we don’t care)
  what kind of a thing it is (from a controlled vocabulary of concepts)
A hierarchy of components provides a structure for properties

## Slide 4: An Example Classification Hierarchy
WhizBangMkIVStarTracker
StarTracker
FlightAvionicsComponent
FlightHardwareComponent
HardwareComponent
Component
Each concept is a specialization of the concept above it.
more general

## Slide 5: Some Example Properties
WhizBangMkIVStarTracker
whiz factor
StarTracker
sensitivity
FlightAvionicsComponent
power load
FlightHardwareComponent
mass, center of mass, moments of inertia
HardwareComponent
reference designator
Component
name, id
Each concept has all the properties of all its ancestors, plus its own unique properties.

## Slide 6: Building It Out
FlightAvionicsComponent
power load
FlightHardwareComponent
mass, center of mass, moments of inertia
HardwareComponent
reference designator
Component
name, id
WhizBangMkIVStarTracker
whiz factor
StarTracker
sensitivity
UltraTurboTransponder
turbo boost
Transponder
power output
Single, well-known property name for common properties (e.g., mass, power load)

## Slide 7: Relationships Are Also Properties
Component
Interface
Function
Requirement
presents
performs
specifies

## Slide 8: Putting It To Use
We can express facts in these terms and store them in a repository:
  x has type WhizBangMkIVStarTracker
  x has name “Star Tracker A”
  WhizBangMkIVStarTracker is a subclass of StarTracker
  StarTracker is a subclass of FlightAvionicsComponent
  and so on….
  Facts are expressed in triples of the form (subject, predicate, object).
We can then ask simple questions like “What is the sensitivity of the WhizBangMkIVStarTracker named ‘Star Tracker A’?”
If the repository can draw inferences, then we can ask things like “What is the sensitivity of the StarTracker named ‘Star Tracker A’?”
Then the master equipment list is simple: “Find all FlightHardwareComponents and print their names and masses.”
Note that these are mission-independent (i.e., reusable) procedures.

## Slide 9: The Semantic Web World
Standards
  Resource Description Framework (RDF)
    Statements of the form (subject, predicate, object)
    Simple class hierarchies
  Web Ontology Language (OWL)
    RDF vocabulary for formal logic
  SPARQL Query Language for RDF
    Powerful language for querying RDF/OWL databases
Technology
  Ontology editors (Protégé, TopBraid Composer, etc.)
  Knowledge repositories (Sesame, Oracle Semantic Database, Mulgara, etc.)
  Application frameworks (Sesame, Jena, TopBraid Suite, etc.)
Community
  Journals, conferences, workshops
  W3C standards working groups
  ODM

## Slide 10: Semantic Web Example
OWL information base describing formulation-phase design information for Phoenix mission to Mars
  9583 triples
  Built on multiple ontologies, including rdf, base (JPL), and mission (JPL)
  Stored in an open-source Sesame2 repository
Simple query: find id and name for the component whose name is “Spacecraft System”
SPARQL Query | Result
select distinct ?cid ?cn where { ?c rdf:type mission:Component . ?c base:identifier ?cid . ?c base:canonicalName ?cn . filter (?cn = "Spacecraft System")} | C.2 Spacecraft System

## Slide 11: Semantic Web Example
More complex query: find id and name for all functions performed by the component whose name is “Spacecraft System”
SPARQL Query | Result
select distinct ?fid ?fn where { ?c rdf:type mission:Component . ?c base:canonicalName ?cn . ?c mission:performs ?f . ?f base:identifier ?fid . ?f base:canonicalName ?fn . filter (?cn = "Spacecraft System")} | F.1.1.2.1 Transport Payload to Martian Vicinity F.1.2.2.3 Execute Commands F.1.2.2.4 Maintain Communication F.1.1.2 Transport Payload to Martian Surface F.1.2.2 Maintain Operational State

## Slide 12: Semantic Web Example
Still more complex query: find id and name for all requirements specifying functions performed by the component whose name is “Spacecraft System”
SPARQL Query | Result
select distinct ?rid ?rn where { ?c rdf:type mission:Component . ?c base:canonicalName ?cn . ?c mission:performs ?f . ?r mission:specifies ?f . ?r base:identifier ?rid . ?r base:canonicalName ?rn . filter (?cn = "Spacecraft System")} | L.3.FS.55 Arrival V-Infinities L.3.FS.42 First TCM Time L.3.FS.43 Last TCM Time L.3.FS.147 Command Durations During Cruise L.3.FS.144 Command Processing Capability …

## Slide 13: Some Relative Priorities
Topic | Semantic Web | UML/SysML
Graphics |  | ++
Tooling | + | ++
Querying | ++ | +
Inferences | ++ | 
Interchange | ++ | +
Expression | ++ | 
Description | + | ++

## Slide 14: Ontologies and SysML
SysML has an ontology, if not by that name
  Block, Interface, Activity, Requirement, etc.
An organization seeking to build long-lived, interchangeable models will likely need to build more ontological structure beneath these high-level concepts:
  Work Breakdown Structure, Hardware, Software, Stakeholder, Concern, etc.
  Plus specialized associations (authorizes, represents, specifies, etc.)
JPL is developing its ontologies using OWL2 and translating them to SysML conceptual models and profiles.
  To us, OWL2 (and the interoperability it implies) are more fundamental than SysML
  Model-based engineering includes many domain-specific models and tools, including system models and SysML tools
We expect to exchange model data between SysML and semantic tools for analysis, validation, product generation, etc.