## Slide 1: Feature Space: Integrating Value, Purpose, Mission, Risk, and Variation
Bill Schindel
INCOSE Patterns Working Group
schindel@ictt.com
INCOSE North Texas Chapter Meeting
June 14, 2022 V1.2.2
Copyright 2022, W. D. Schindel Permission granted to use with attribution

## Slide 2: Abstract
Model-based systems engineering offers the possibility of clarity of models that powered the scientific revolution. Among the surprising results of this is realization that, for appropriately structured models, some seemingly separate aspects of engineering can be combined into a simpler integrated representation.
Engineers are accustomed to thinking of mission engineering, stakeholder needs analysis, requirements engineering, optimization of design, performing risk analysis, and engineering of product line variants as a series of related but different subjects that collectively add up to a complex problem. However . . .
In this talk, we will summarize some implications of the question “What is the smallest model of a system?”, for purposes of engineering and science across life cycles. We will take a look at Feature Space, how it reduces degrees of freedom to give a clearer integrated view of system value, purpose risk, and varied configuration, along with SysML realization of this approach.

## Slide 3: Contents
The INCOSE MBSE Patterns Working Group
What is the smallest model of a system?
Stakeholder Value: Introduction to Feature Space
Mission
Risk
System variation, product lines, and configurable families
Mapping into SysML and other languages and tooling
Interested? How to get involved
Conclusions, questions, discussion
References
Speaker background

## Slide 4: The INCOSE MBSE Patterns Working Group
MBSE Patterns Working Group will meet at IS2022 on Sunday, June 26, at 1:30 ET—if you are not on site, you can join virtually: https://www.incose.org/symp2022/symposium/event-schedule
Originated in 2013 as one of the INCOSE-OMG MBSE Initiative challenge teams, advancing in 2016 to INCOSE Working Group.
Focused on model-based representation of recurring, configurable system-level patterns.
History of projects emphasizing collaboration with other technical societies & INCOSE Working Groups.
Numerous publications and resources available for download from Patterns Working Group web site-- https://www.omgwiki.org/MBSE/doku.php?id=mbse:patterns:patterns (Note this is on OMG Wiki!)
You are invited to participate!

## Slide 5: What is the smallest model of a system?
The use of model-based recurring patterns is at the center of the explosive success of science, engineering, and mathematics in transforming the human-experienced world over the last 300 years.
In pursuing the use of model-based patterns for systems engineering, we soon realized that the underlying theory supporting MBSE would need to be strengthened to include the model-centric lessons those 300 years--if MBSE is to have the kind of transformative impact in practice that STEM has had.
The beginning of that process, twenty years ago, was to ask the question:
  “What is the smallest model of a system, for purposes of science and engineering, over the life cycles of systems?”
Our program this evening is about a few aspects of where that led.

## Slide 6: Formalizing a Few Representational Concepts
Definition: In the perspective described here, by “System” we mean a collection of interacting system components:
By “interacting” we mean the exchange of energy, force, material, or information (all of these are “input-outputs”) between system components, . . .
. . . through which one component impacts the state of another component.
By “state” we mean a property of a component that impacts its input-output behavior during interactions. (Note the circular cause-effect definition chain here.)
So, a component’s “behavior model” describes input-output-state relationships during interaction—there is no “naked behavior” in the absence of interaction.*
The behavior of a system involves emergent states of the system as a whole, exhibited in its behavior during its own external interactions, resulting in observable holistic aspects.
(* This means that if you are trying to model system behavior outside of Interactions, you may be fooling yourself.)

## Slide 7: What have we learned in 300 years?
The history of science and engineering offers plenty of insight about this subject, which is much older and deeper than what we today call “MBSE”.
What is the practical significance of this to SE practice?
Important because contemporary MBSE models often:
  Are missing key aspects (are too small)
  Contain redundant conflicting aspects (are too big)
  At the same time!
  We will be discussing prominent examples of both.
The S*Metamodel is a formalization of that minimal content—much of which is familiar, but some of which is less visible in current practices we observe.
This is not about an alternative modeling language or tooling—the agnostic S*Metamodel has been mapped to contemporary languages and tooling (including OMG SysML) for a number of years, and works just fine in current COTS modeling tool environments.
Informal pedagogical S*Metamodel subset
Formal S*Metamodel (~100 pages UML & prose)
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:systematica_5_metamodel_v7.1.6a.pdf

## Slide 8
An S*Model is any model (descriptive information construct) of a system (in any modeling language, views, or tooling) which conforms to (maps to) the S*Metamodel:
Some of the types of information found in S*Models (independent of language or tooling).
S* is short for Systematica

## Slide 9: What lessons of 300 years? One Aspect is External Behavior as Interaction
Informal pedagogical S*Metamodel subset
Interaction/Behavior Space: Describes Behavior as Interactions with Environmental Actors. An objective description more familiar to scientist and engineers—exchanges of forces, energy flows, material flows, information, causing changes of state.
Example: Travel Over Terrain
The world of the physical sciences—all the known laws of mechanics, electrical science, etc. are in the context of Interactions.

## Slide 10: Example: Vehicle Interactions with External Actors
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_tutorial_glrc_2016_v1.7.4.pdf

## Slide 11: Another Aspect, and a subject of this talk, is Stakeholder Value: Introduction to Feature Space
Informal pedagogical S*Metamodel subset
Feature Space: Describes Stakeholder Value Space. This description frequently includes subjective aspects, and is describing stakeholders as much as it is describing the system of interest.
Scoreboard/tradespace for optimization.
The structure & semantics (not just quantitative) of value.
The world of Stakeholder Needs, Customer Requirements, Capabilities, Preferences & Priorities, Release Trains.
Connecting models to the C-Suite.
What have we learned in 300 years?

## Slide 12
Example: Vehicle Features Model (in a SysML Features Package)

## Slide 13: System Behavior is Modeled Twice (Features and Interactions) Objective-Subjective Link & The Value Selection Phenomenon
Engineers know that value is essential to their practice, but its “soft” or subjective nature seems challenging to connect to hard science and engineering phenomena.
System engineers currently learn to seek out and represent (may model in detail) stakeholder needs, measures of effectiveness (MOEs), objective functions connected to derived requirements and technical performance, etc. to answer: what value does your system contribute?
This nearly always includes “conflicting” dimensions of value, when “trade space” value dimensions appear to trade against each other—as in performance vs. cost. The resulting balancing act led to notions of Pareto Frontiers and other multi-variate forms, Arrow’s Impossibility Theorem, and other formulations and insights about the dimensions of value.
For many systems, lack of good knowledge (by even the customer) about value has changed engineering into a discovery project, as in Agile Methods, Minimum Viable Products, Pivoting, Hypothesis Experiments, and similar approaches.
Meanwhile, what are the phenomena associated with value, what is the bridge between subjective value and objective science, where are the related mathematics and recurring patterns, and what are the impacts on future SE practice?
What follows is not the same as simply “modeling idealized value”, which might seem natural but which has some challenges for direct observation.

## Slide 14: What is the distinction we are making here?
This is where the “objective science” comes in!
We are interested in models that can be tested in actual experiments with real selection agents.
Systems engineering needs to catch up with what business has discovered and put into practice in recent years—driving discovery with real experiments that test the validity of hypothesized value, in a dynamic, pivoting enterprise.
We are interested in what actual selection behavior tells us about value—not just what isolated offerings of opinion about value or statements of preference. What really gets selected?
That is the distinction of the Value Selection Phenomenon.
It is a real phenomenon that always occurs and can be observed.
It also can be influenced by advertising, culture, context, bias.
It can also help us engage the “multi-variate” value challenge.
“Modeling Value” in the traditional sense (e.g., MOEs/Measures of Effectiveness, etc.) sounds a lot like “Modeling Value Selection”—so what distinction we are making?

## Slide 15
Even if value (both human-based and otherwise) seems elusive or subjective, the expression of value in the real world is always via selection, and selection itself is an observable interaction-based phenomenon: The Value Selection Phenomenon:
Settings | Types of Selection | Selection Agents | 
Consumer Market | Retail purchase selection | Individual Consumer; Overall Market | 
Operational Use | Decision to use product A or use product B | User | 
Military Conflict | Direct conflict outcome; threat assessment | Military Engagement | X
Product design | Design trades | Designer | 
Commercial Market | Performance, cost, support | Buyer | 
Biological Evolution | Natural selection | Environmental Competition | X
Product Planning | Opportunity selection | Product Manager | 
Market Launch | Optimize choice across alternatives | Review Board | 
Securities Investing | What to buy, what to sell, acceptable price | Individual Investor; Overall Market | 
College-Student “Matching Market” | Selection of individuals, selection of class profile, selection of school | Admissions Committee; Student & Family | 
Life choices | Ethical, moral, religious, curiosities, interests | Individual | 
Democratic election | Voting | Voters; Voting Blocks | 
Business | Risk Management, Decision Theory | Risk Manager, Decision Maker | 
Not all selection is by human agents

## Slide 16: Mission; Mission Features; Mission Engineering
The Defense community in particular has increased emphasis (especially the last ~5 years) on “Mission Engineering”-- this includes explicitly representing Mission in system models.
This healthy trend could be viewed as catching up with some commercial systems engineering—improving the representation of what holistic engineered domain systems are intended to accomplish.
Mission Space is a subset of Feature Space, concerned with primary purpose of either an engineering Systems of Interest (e.g., an Aircraft) or the larger domain systems of which they are a part (e.g., a Task Force):
  Example: A10 Aircraft Close Air Support Mission.
  Some models show multiple levels of systems, so we can think about their respective Missions.
Not all important stakeholder Features or capabilities are Mission or Primary Purpose level Features:
  Remember the “-ilities”? (e.g., the Maintainability Feature)
  Remember system management functional areas (SMFAs) “FCAPS”? (e.g., the Security Management Feature)
Configurable patterns (Mission Packages) of Mission Features are encouraged for common understanding, sharing across subsystems, programs, suppliers, rapid response, for common language, ontology.
https://ndiastorage.blob.core.usgovcloudapi.net/ndia/2016/systems/18950_RobertGold.pdf

## Slide 17: Models of risk: What do we need to represent?
Traditional systems engineering example risk analysis representations are well-established, and can be found in:
  Failure Modes and Effects Analysis (FMEA) or Failure Modes, Effects, and Criticality Analysis (FEMCA).
  Special cases for risks of designs, risks of production and other processes, risks introduced by human operators (D-FMEA, P-FMEA, A-FMEA).
  Fault Tree Analysis (FTA).
  Preliminary Hazard Analysis (PHA).
  Reliability Centered Maintenance (RCM) analysis.
  Hazards and Operability Analysis (HAZOP).
  Safety and Cybersecurity Analysis variations on the above.
Some are used as part of review of a candidate system design, others to analyze an existing system, as in the case of RCM planning of preventive maintenance, etc.

## Slide 18: Models of risk: What do we need to represent?
Most systems engineering relevant definitions of risk include these ideas:
  Potential, threat, or hazard of some future harm, injury, death, setback, economic or market loss, impacted assets, loss of advantage, etc.
    (Sometimes we alternatively model “risk” of a more positive “opportunity” for gains of various kinds--not our current focus in this session.)
  One or more causal “modes” which can lead to the negative outcome.
  A degree of uncertainty as to that occurrence, whether expressed as likelihood, probability distribution, or otherwise.
  Some idea of the severity of impact of such a negative outcome, were it to occur, and what parties would be impacted.
  Ability (or inability) to detect whether the negative situation has occurred or is occurring.
  Ability (or inability) to mitigate or work around or otherwise tolerate the negative situation, were it to occur.
  In some cases, a time evolutionary aspect representing when in time these ideas might apply.
  Means of assembling a relatively complete (and potentially large) collection of the above possibilities, and weighing them relative to each other so that attention and resources can be assembled, focused, and allocated to their prevention, mitigation, planning, or other disposition. (“Risk Priority Number” (RPN) scores are common: RPN = Probability x Severity x Detectability.)

## Slide 19: Risk: Failure Impacts
A pleasant surprise is the discovery that a solid MBSE model of a system’s Stakeholder S*Features brings us very close to having a model of all the potential negative Effects (the “E” part of FMEA) that a system may present (even if some are not realizable):
  Even if we don’t yet know the system’s design (!), a fully-modeled Feature Space is a direct path to the Failure Effect Space, because . . .
All risk is risk to Stakeholder Features:
  Why? If you ever discover a risk that is not represented in the modeled Feature space of a system, then you have just found a missing part of the positive Feature model. (Add it.)
  So, it turns out that the negative FMEA model part improves the positive part of the model, and the positive part of the model improves the negative FMEA part of the model . . .

## Slide 20: All Risk is Risk to Stakeholder Features
Therefore we can view each Stakeholder Feature in the model as having one or more associated Failure Impacts that are about risks (at least in principle) to stakeholders (should they ever occur).
Example:
  Feature = Telephone Voice Communication Service
  Failure Impact = Loss of Voice Communication Service
What we mean by these are the “E” part of an FMECA: The “Effect” or consequence of the risk realization.
Note that one Feature may be associated with multiple Failure Impacts.

## Slide 21: Simple FMEA, Generated from Configurable System Pattern
Feature | Effect (Failure Impact) | Severity | Functional Failure (Counter Requirement) | Component | Failure Mode | Probability | Mitigation (Control)
Navigation Feature [GPS-based Location Sensing] | No Confidence in Displayed Position | Serious (4) | The system displays a location that is not accurate to 10 feet. | Vehicle ECM | Erratic ECM | 0.0015 | Nav Backup Mode: External Nav Module
Navigation Feature [GPS-based Location Sensing] | False Confidence in High Error Displayed Position | Critical (5) | The system displays a location confidence indicator that is not correct. | Vehicle ECM | Erratic ECM | 0.0015 | None
Navigation Feature [GPS-based Location Sensing] | No Displayed Location | Serious (4) | The system does not display the graphic map presentation. | Panel Display | Fractured Display | 0.0003 | Nav Backup Mode: External Nav Module
21
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_tutorial_glrc_2016_v1.7.4.pdf

## Slide 22: To find out more about integrated FMECA
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:improving_failure_analysis_using_mbse_v1.3.2.pdf

## Slide 23: S*Patterns are Configurable MBSE Models of Families
S*Patterns are configurable S*Models of generalized systems or system families.
They are intended to be re-configurable, re-usable, and accumulate learning.
They are often patterns of “whole systems”, as opposed to components.
They are model-based patterns (there is a long history of other patterns).
As S*Models, they are based on the S*Metamodel.
Closely related to: Models of Product Platforms, Architectural Frameworks, Ontologies, Configurable Product Line Engineering Models, Domain Specific Modeling Languages

## Slide 24: S*Pattern Configuration: Driven from Feature Space
Engineers and other subject matter experts are familiar with extensive lists of detail configuration variables at many levels:
  holistic system capability options
  large subsystem assemblies options
  small hardware components choices
  software component variations
  configurable datasets, option switches, and other managed options
Most of these points of variation tend to be in the more detailed level lists of numerous smaller elements.
Collectively, these choices roll up to overall capabilities visible to system stakeholders—those also vary accordingly, but are fewer in number.

## Slide 25: S*Pattern Configuration: Driven from Feature Space
With that in mind, it can be somewhat surprising to realize that all configurability at any “level” is for Stakeholder Feature level reasons.
Obvious question: What about a small component level variant that you say has no effect significant to any stakeholder?
  Answer: We can eliminate that component option choice, and no one will care!
Obvious objection: But, what about option choices made to optimize supply chain robustness, or minor behaviors like minor parasitics (e.g., noise).
  Answer: But you said that no stakeholder cared!
Our point here: Stakeholder Feature Space is supposed to be large enough to cover the life cycle stakeholders who “count”, including production, support, shareholders, etc.
Implied warning: So, the term “non functional requirement” can be misleading.

## Slide 26: Propagation of configuration population is inherent to the nature of all engineered systems
S*Feature Space drives configuration from a smaller set of (stakeholder based) degrees of freedom / points of variation.
Simplifies Product Line Engineering (PLE) model configuration rule-making and integrates PLE.
Inherent PLE degrees of freedom configuration propagation:

## Slide 27: Relationship to Feature-Based PLE ala’ ISO 26580
Very similar in the PLE aspects, with a few differences:
ISO26580 PLE specifies modeling what changes, but specifies omitting what does not change; S*Feature models include baseline capabilities.
ISO26580 refers to all the points of variation as “Features”, with rules to be established between them; S*Patterns begins with a smaller set of “Stakeholder Features” degrees of freedom in stakeholder value space, then recognizes all the other points of variation throughout the model but connects them with each other up to the Stakeholder Features points of variation.
This shows that the number of real degrees of freedom, after considering constraints, is smaller.
Effectively complies with ISO26580 while making its use simpler and more integrated.

## Slide 28: How to find out more about configurable model-based patterns
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_extension_of_mbse--methodology_summary_v1.6.1.pdf
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:glrc_2018_tutorial--mbse_emerging_issues_v1.4.2.pdf
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_tutorial_glrc_2016_v1.7.4.pdf

## Slide 29: Existing mappings into OMG SysML, other languages, and your tooling
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:systematica_mapping_for_magicdraw_csm_v1.9.1a.pdf

## Slide 30: Interested? How to get involved
INCOSE Patterns Working Group will meet (on site and virtually) at IS2022 on June 26, 1:30-4:30 PM ET: https://www.incose.org/symp2022/symposium/event-schedule
Or, just contact Bill Schindel schindel@ictt.com
Current working group projects: https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:iw22_mbse_workshop_round_robin--mbse_patterns_wg_schindel_v1.2.2.pdf

## Slide 31: Conclusion, questions, and discussion
Conclusion: Modeling and management of System Value, Mission, Purpose, Risk, and Configurability are deeply connected by Feature Space.
Examples include: Configurability of Mission; Risk to Mission.
Discussion:

## Slide 32: Thank you!

## Slide 33: References
Integrated Examples:
Oil Filter “S*MBSE Patterns: A Small Scale Example”, https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:oil_filter_example_v1.6.2.pdf
Feature / Capability Space of the System of Innovation: “The Innovation Ecosystem: Introduction to the INCOSE ASELCM Pattern”, INCOSE North Texas Chapter, December, 2021. https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:incose_north_texas_pgm_12.14.2021_v1.2.2.pdf
Terrestrial Vehicle: https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_tutorial_glrc_2016_v1.7.4.pdf
Mission Engineering:
R. Gold, “Mission Engineering”, MDIA SE Conference Oct 2015. https://ndiastorage.blob.core.usgovcloudapi.net/ndia/2016/systems/18950_RobertGold.pdf
R. Giachetti, A. Hernandez, “Mission Engineering”, SEBoK. https://www.sebokwiki.org/wiki/Mission_Engineering
Example defense mission: CV-22 Variant Osprey Aircraft: https://www.af.mil/About-Us/Fact-Sheets/Display/Article/104531/cv-22-osprey/#:~:text=The%20mission%20of%20the%20CV,missions%20for%20special%20operations%20forces
Example defense mission: Special Operations Wing: https://www.hurlburt.af.mil/About-Us/Fact-Sheets/Fact-Sheets/Article/204524/1st-special-operations-wing/
Integrating Risk Analysis into Feature Space:
FMECA Slides and paper “Failure Risk Analysis: Insights from Model-Based Systems Engineering” Proc. of INCOSE 2010 International Symposium”. https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:improving_failure_analysis_using_mbse_v1.3.2.pdf and https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:impact_of_mbse_on_failure_analysis_v1.2.1.pdf
Integrating Configurability into Feature Space:
Tutorial: “Introduction to Pattern-Based Systems Engineering(PBSE): Leveraging MBSE Techniques”, INCOSE Great Lakes Symposium, 2016. Retrieve from-- https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_tutorial_glrc_2016_v1.7.4.pdf
ISO26580 (2021) “Software and systems engineering — Methods and tools for the feature-based approach to software and systems product line engineering”, ISO, 2021. https://www.iso.org/obp/ui/#iso:std:iso-iec:26580:ed-1:v1:en

## Slide 34
Value:
Schrage, M., The Innovator's Hypothesis: How Cheap Experiments Are Worth More than Good Ideas (MIT Press) Hardcover – September, 2014
The Value Selection Phenomenon: “Discussion Inputs to INCOSE Vision 2035 Theoretical Foundations Section”. https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:science_math_foundations_for_systems_and_systems_engineering--1_hr_awareness_v2.3.2a.pdf
“Value Engineering and Body of Knowledge”, SAVE International, 2007. Retrieve from http://www.value-eng.org/pdf_docs/monographs/vmstd.pdf
Pattern-Based MBSE:
INCOSE MBSE Patterns Working Group Web Site: https://www.omgwiki.org/MBSE/doku.php?id=mbse:patterns:patterns
PBSE Methodology Reference: “Methodology Summary: Pattern-Based Systems Engineering (PBSE), Based On S*MBSE Models” https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:pbse_extension_of_mbse--methodology_summary_v1.6.1.pdf
S*Metamodel: https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:systematica_5_metamodel_v7.1.6a.pdf
S*Metamodel Mapping to OMG SysML Third Party COTS Tooling: https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:systematica_mapping_for_magicdraw_csm_v1.9.1a.pdf
References, continued

## Slide 35: Speaker background
Bill Schindel is president of ICTT System Sciences. His engineering career began in mil/aero systems with IBM Federal Systems, included faculty service at Rose-Hulman Institute of Technology, and founding of three systems enterprises.
He chairs the INCOSE MBSE Patterns Working Group, and served on the lead team of the INCOSE Agile Systems Engineering Life Cycle Discovery Project. He is an active member of the ASME VV50 working group on model credibility in advance manufacturing, and the AIAA digital thread and digital twin case study teams.
Schindel is an INCOSE Fellow and CSEP, and is a director and past president of the INCOSE Crossroads of America Chapter.
schindel@ictt.com

## Slide 36: Supplemental backup

## Slide 37: Oil Filter Family: Feature Space Across Domains
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:oil_filter_example_v1.6.2.pdf

## Slide 38: Three integrated model classes
In the “smallest model” sense, the positive side of a system model is directly integrated with, and testable against, the negative side of the system model.
Three classes of information are implied, which are commonly seen in FMECAs and other risk analysis (under various names) but not always integrated with their positive counterparts:
Failure Mode: An abnormal state of a subsystem or component that results in abnormal (out of spec) behavior of that subsystem or component. (Part of State Space)
  Example: Bearing Fracture (Note that you can also model causes, mitigations, detection, etc.)
Counter-Requirement: A requirements-like statement that describes the abnormal (out of spec) behavior of a subsystem or component. (The Functional Failure part of a FMECA; Counter Requirements are a part of Requirements Space)
  Example: The system fails to transmit rotary torque.
Failure Impact: The effect or consequence impacting a stakeholder, associated with the Feature that is impacted. (The “E” part of a FMECA; part of Feature Space.)
  Example: Vehicle Transportation Services Not Available
Failure Impact
Failure Mode
Counter Requirement

## Slide 39
https://www.omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:patterns:incose_north_texas_pgm_12.14.2021_v1.2.2.pdf