## Slide 1: How to verify system design against requirements ? The Thirty Meter Telescope Case Study
January 11, 2018, OMG-SST
Robert Karban
JPL, California Institute of Technology
An Executable MBSE Method (ESEM) to
Support Requirements Analysis and Verification
Notes: 25+5 minutes presentation
An Executable MBSE Method (ESEM) to Support Requirements Analysis and Verification

## Slide 2: Outline
Introduction to Thirty-Meter Telescope (TMT)
(MB)SE approach in TMT project
System design and requirements verification approach
Infrastructure and Modeling Guidance
OpenMBEE public server
OMG SysML specification

## Slide 3: Complexity of TMT
The Thirty Meter Telescope (TMT) is no different than other complex systems of systems
We still need to apply core SE processes
Difference: telescope community is historically unfamiliar with formal Systems Engineering

## Slide 4: TMT Key Science
Nature and composition of the Universe
Formation of the first stars and galaxies
Evolution of galaxies
Relationship between black holes and their galaxies
Formation of stars and planets
Nature of extra-solar planets
Potential of life elsewhere in the Universe
Unforeseen discoveries…

## Slide 5: TMT Project
TMT Project formed in 2004
TMT international partnership grew
  US (Caltech & UC), Canada, China, India, Japan
2004 – 2008 site studies
  Chile, Mexico, Hawaii
Mauna Kea, Hawaii selected in 2009
2014 start of TMT Construction Phase
Notes:   Formation: Association of Canadian Universities for Research in Astronomy (ACURA), Caltech, UC, AURA (associate)

## Slide 6: Primary Mirror (M1)
Segmented primary mirror
  492 hexagonal segments
  1.44 m across corners
  2.5 mm gaps (0.1 in, 0.6% lost area)
  Thin glass (~2 in) reduces mass and thermal inertia
Reduces difficulties:
  Fabrication
  Testing
  Transportation
Reduces risks:
  Breakage of single segment is less catastrophic
Moderate cost and complexity
Notes: Glass temperature can follow changing ambient temp to minimize mirror seeing effects
Segment blanks: Japan (Ohara)

## Slide 7: Alignment and Phasing System (APS)
Alignment and diagnostic instrument located on a Nasmyth platform
Modified Shack-Hartmann wavefront sensor
Responsible for pre-adaptive optics wavefront quality
Uses starlight to measure wavefront errors and determine commands to send for aligning optics

## Slide 8: Typical TMT SE Activities using modeling techniques
Capture operational use cases with estimated durations of actions, e.g.
  Post segment-exchange alignment: requirement: 2h; CBE 1h19m
Capture power and mass characteristics of components
Identify involved subsystems, e.g. Telescope Control System (TCS), M1 Control System (M1CS)
Identify interfaces and interactions among subsystems
Analyze associated scenarios
Automatically verify system requirements are satisfied
Derive requirements for TMT subsystems
Develop/refine timing requirements for algorithms, internal and external interface commands
Monte Carlo simulation of expected timings and variants for operational scenarios
Notes: Capture relevant information in a SysML model (system database) using ESEM (Executable Systems Engineering Method)
Used SysML constructs
  Block diagrams, State Machines, Activity Diagrams, Sequence diagrams
Simulate system level scenarios
Verify correctness by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
Automatically verify timing against formal constraints (requirements)
Follow ESEM to define two white box specifications that specialize the black box specification
  Conceptual Specification
  Realizations Specification
Decompose the white box specifications into elements representing the subsystems

## Slide 9: Analysis of Architecture and Design
Max duration Post-segment exchange: 7200s 5000s
Number of exposures of 45s 4 6
Max peak power consumption in dome: 8.5kw 8.1kw Number of motors with 50W 10 12
Update Requirements
Analyze Conceptual Design
Analyze Realization Design/Specification
OCD, Requirements, ICD, DDD
Pass/fail
1
2
3
4
5
6
Notes: Touches on all modeling capabilities: construction, visualization, analysis, management, exchange and integration, collaboration and workflow

## Slide 11: Operational Scenarios

## Slide 12: Characterize Component Structure & Behavior with different View Points
Operational behavior captured with
state machines and activity models
1
2

## Slide 13: Characterize Components
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration
1
2
3
4

## Slide 14: Timeline of component states

## Slide 15: Interfaces between components
Provides information for ICD from behavioral model
and in the context of the system structure

## Slide 16: Power Analysis in the Context of Structure and Interfaces

## Slide 17: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 18: System Level Analysis

## Slide 19: TMT MBSE Objectives
Uses standard languages and techniques where practical to avoid custom software development
Use MBSE to define executable SysML model that captures requirements, operational scenarios, behavior, system decomposition, relationships and between subsystems, etc.
Use the model to analyze the system design for
  Power consumption, mass, and duration/timing
  Error budgets (e.g. wave front error)
Produce engineering documents
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents

## Slide 20: TMT MBSE Application
SysML as common language
TMT SysML Model does not model the entire telescope
Main objective is to model operational scenarios and demonstrate that requirements are satisfied by the design
Motivator for TMT MBSE = optimization
Ex: JPL modeling of APS subsystem
  Use Case: Post segment-exchange alignment, 2h requirement
  Component characteristics (power, mass)
  Relationships (TCS, M1CS)
Ex: Monte Carlo simulations for acquisition and slew time
  To minimize loss of observing time, TMT should be able to move from one target to another and acquire it in 3 min or less

## Slide 21: TMT Hybrid Approach
Traditional SE
  Clear, defined deliverables
  Easily accessible
  Shallow learning curve
  Simple traceability
MBSE
  Understanding behaviors of a system
  “Rich” capability to represent complex systems
Exploit the advantages of each approach

## Slide 22: Approach to Automate Requirements Verification
Next phase of system modeling emphasizes executable models to enhance understanding , precision, and verification of requirements
Executable Systems Engineering Method (ESEM) augments the OOSEM activities by enabling executable models
  ESEM produces executable SysML models that verify requirements
  Includes a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams
  Enables integration of supplier/customer models

## Slide 23: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 24: Object Oriented System Engineering Method
Defines the architecture in terms of:
Domain: the context of the solution
  Enterprise: the ecosystem of the solution
    System of Interest: the solution being specified
      Black Box: externally visible specification
      Conceptual: white box functional specification
      Physical: white box realization specification

## Slide 25: Model Organization & Package Structure
Organizing principles
  Customer/Supplier relationship
  Work Breakdown Structure
  OOSEM/ESEM abstraction layers – Methodology
  Domain specific organization

## Slide 26: Building the Viewpoint Model
Viewpoint Model
  Purpose informed by Stakeholder Concerns
  Methods and Analysis for constructing the View from the Model
  Presentation Rules
Docgen as query language https://github.com/Open-MBEE/mdk/tree/mdk-manual/src/main/dist/manual

## Slide 28: Black Box Design Model
Project level components communicate with APS black box block
APS Black Box
TCS
M1CS
ESW
CS
Operator

## Slide 29: Conceptual Design Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 30: Duration Analysis results

## Slide 31: Realization Design Model
System Decomposition Hierarchy

## Slide 32: Realization Design Model
System Decomposition Hierarchy

## Slide 33: Power Analysis Results

## Slide 34: References
http://omgwiki.org/MBSE/doku.php?id=mbse:telescope
Open Source TMT model: https://github.com/Open-MBEE/TMT-SysML-Model
Open Source Engineering Environment: https://open-mbee.github.io/
Docgen, View&ViewPoints: https://github.com/Open-MBEE/mdk/tree/mdk-manual/src/main/dist/manual
Model-Based Systems Engineering Case Study: http://omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:incose_mbse_iw_2017:iw_2017_open_mbee.pdf
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban R., Dekens F., Herzig S., Elaasar M, Jankevičius N., “Creating systems engineering products with executable models in a model-based engineering environment”, SPIE, Edinburgh, Scotland, 2016
Karban, R., “Using Executable SysML Models to Generate Systems Engineering Products”, NoMagic World Symposium, Allen, TX, 2016
A Practical Guide to SysML, 3rd Edition, Chapter 17 by Friedenthal, Moore, and Steiner
Zwemer, D., “Connecting SysML with PLM/ALM, CAD, Simulation, Requirements, and Project Management Tools”, May 2016

## Slide 35: Backup slides

## Slide 36: Integrated Document Generation And Simulation

## Slide 37: Model Organization & Package Structure
Organizing principles
  Customer/Supplier relationship
  Work Breakdown Structure
  OOSEM abstraction layers

## Slide 38: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 39: Step 1: Formalize Requirements
Requirement Pattern
  Customer Side
    Define the textual requirement with a Requirement
    Optionally define a design black box specification with a Block with relevant value properties
    Optionally refine the Requirement with a Constraint Block on the black box design Block
  Supplier Side
    Define a design black box specification with a Block (that refines the customer’s black box Block if any and provides tighter property values)
    Refine the textual Requirement by a Constraint Block (if not already defined by the customer)

## Slide 40: Step 1: Formalize Requirements

## Slide 42: Step 2: Specify Design
Follow OOSEM to define two white box designs which specialize the black box design
  Conceptual Specification
  Realization Specification
Decompose the white box designs into Blocks representing the subsystems

## Slide 43: Black Box Design Model
Project level components communicate with APS black box block
APS Black Box
TCS
M1CS
ESW
CS
Operator

## Slide 44: Step 2: Conceptual Design Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 45: Step 2: Realization Design Model
System Decomposition Hierarchy

## Slide 46: Step 2: Realization Design Model
System Decomposition Hierarchy

## Slide 47: Step 3: Characterize Components & Specify Behavior
Specify behavior of components
  E.g., using SysML state machines for lifecycle behavior
  E.g., using SysML activity diagrams for functional flow
Characterize Components, e.g., Using Patterns
Example: Roll-up Pattern
  Constrained value represents an aggregate value that is propagating up a hierarchy of subcomponents
  Static roll-up (e.g., mass roll-up)
  Dynamic roll-up (e.g., power roll-up)

## Slide 48: Step 3: Characterize Conceptual Components
Operational behavior captured with
state machines and activity models
1
2

## Slide 49: Step 3: Characterize Conceptual Components
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration
1
2
3
4

## Slide 50: Interfaces between components
Provides information for ICD from behavioral model

## Slide 51: Step 3: Characterize Realization Components
Power Roll-up Pattern Application

## Slide 52: Step 3: Characterize Realization Components
Power Rollup Pattern
State constraints

## Slide 53: Step 4: Specify Analysis Context
Analysis Context Pattern
  Abstract analysis context Block composes both the design black box Block and white box Block
  Analysis properties defined on the analysis context Block (e.g., peak power, power margin)
  Analysis parametric model on the analysis context that computes and binds analysis values

## Slide 54: Step 4: Specify Analysis Context
Analysis Context Pattern

## Slide 55: Step 5: Specify Operational Scenarios
  Operational Scenario Pattern
    Concrete analysis context Block which
      Represents one operational scenario (e.g., power configuration)
      Specializes the abstract analysis context Block
      Redefines context’s properties with scenario-specific values
      Defines an owned behavior (sequence diagram) as scenario driver
        Changes the states of the different components, by sending them signals, causing the rolling-up to occur automatically
        Can specify duration constraints to time the injection of signals thus controlling time spent in a certain state
        Can use state constraints (on components) to verify during execution if a component is actually in expected state

## Slide 56: Step 5: Specify Operational Scenarios
Operational Scenario Pattern

## Slide 57: Step 5: Specify Operational Scenarios
Operational Scenario Driver

## Slide 58: Step 6: Specify Scenario Configurations
Scenario Condition Pattern
  A decomposition tree of instance specifications representing the state of the scenario
    Can be presented in tabular form
      Rows represent the instance specifications (e.g., component)
      Columns represent values (e.g., operating power) from the instance specifications
Issues
  Hard to keep instance specifications in sync with Block hierarchy
    Mitigation: tool automation

## Slide 59: Step 6: Specify Analysis Configurations
Scenario Initial Condition Pattern

## Slide 60: Step 7: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 61: Timeline of component states

## Slide 62: Duration Analysis results

## Slide 63: Power Analysis

## Slide 64: Power Analysis Results

## Slide 65: Acknowledgments
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration and NoMagic.
The TMT Project gratefully acknowledges the support of the TMT collaborating institutions. They are the Association of Canadian Universities for Research in Astronomy (ACURA), the California Institute of Technology, the University of California, the National Astronomical Observatory of Japan, the National Astronomical Observatories of China and their consortium partners, and the Department of Science and Technology of India and their supported institutes. This work was supported as well by the Gordon and Betty Moore Foundation, the Canada Foundation for Innovation, the Ontario Ministry of Research and Innovation, the National Research Council of Canada, the Natural Sciences and Engineering Research Council of Canada, the British Columbia Knowledge Development Fund, the Association of Universities for Research in Astronomy (AURA) and the U.S. National Science Foundation.