## Slide 1: MBSE Implementation Across Diverse Domains at The Boeing Company
INCOSE MBSE Working Group
25-26 January 2014
Barbara Sheeley, Robert Malone, John Palmer, Ron Carson (ronald.s.carson@boeing.com )

## Slide 2: Topics
Boeing diverse product lines
Boeing approach to MBSE
Boeing MBSE challenges
Boeing MBSE needs from industry

## Slide 3: Boeing at a Glance
Customers and customer support in 150 countries
    Total revenue in 2012: $81.7 billion
    70 percent of commercial airplane revenue from customers outside the United States
Manufacturing, service & technology partnerships with companies around the world
    Contracts with 22,000 suppliers and partners globally
Research, design & technology-development centers & programs in multiple countries
More than 170,000 Boeing employees in 50 states and 70 countries
Notes: 3

## Slide 4: A Sample of Diverse Boeing Products
Maintenance, Modifications & Upgrades
C-17 GSP
FUTURE PROGRAMS
P-8A
Apache
C-17
Weapons
AWACS
PAC-3
CH-47
GMD
ISS
ABL
BCTM
FAB-T
JTRS
Shuttle
Satellites
F-18
F-15
737
747
747-8
777
787
Tankers
Boeing’s 80 Year Heritage of Systems Engineering
Sea Launch
B-52
SBI
Copyright © 2014 Boeing. All rights reserved.
Notes: 4

## Slide 5: Diverse Boeing Product Domains
Commercial Airplanes and Aviation Services
Defense, Space & Security includes:
  Boeing Military Aircraft
  Network & Space Systems
  Global Services & Support
  Phantom Works
Components to systems-of-systems
Highly networked and high-integrity performance demands
Product and Organizational Diversity Yields MBSE Challenges and a Need for Diversity of MBSE Solutions

## Slide 6: Topics
Boeing diverse product lines
Boeing approach to MBSE
Boeing MBSE challenges
Boeing MBSE needs from industry

## Slide 7: Boeing Enterprise Approach to MBSE Implementation
Education on the topic of MBSE
  Reestablishment of basic SE beyond requirements management
  Importance of functional models (Carson & Sheeley, INCOSE 2013)
Development of MBSE capability for programs to use
Development of guidance for how to use the MBSE developed capability
A core group that provides support to all programs
Means to capture and share successes and lessons learned

## Slide 8: Boeing Approach to MBSE Capability Development
A unified enterprise approach
  Common process
  Common set of tools
MBSE will be accomplished thru capturing information in an integrated architecting environment, in 3 major architecture pieces
  Functions and interfaces
  Requirements
  Logical elements and interfaces
Architecture data extended / used to perform integration, verification and validation efforts

## Slide 9: Integrated Product Architectures at The Boeing Company
  IPA is a enterprise effort to develop and deploy a common capability to enable Boeing engineers to integrate requirements, architectures, and analyses
  IPA uses a model based systems engineering (MBSE) approach in an integrated data environment
  The integrated architecture environment enables consistent, seamless generation of SE artifacts and enables more effective system trades
Requirements Architecture
Functional Architecture
Logical Architecture
Requirements Allocation
Functional Allocation
ICDs
Specs
DoDAF views
Verification
Logic
Networks
Functional Timelines
Logical product structures
Control and data flows
Architecture Data Captured and Managed in a Single Data Environment Ensures Product Quality and Enables Affordability
Specialty development perspectives

## Slide 10: Getting it Right
MBSE can improve probability of “getting it right” the first time
Right Components
Right Interfaces
Right Requirements
Right System
Simulated System
Models of Requirements
Models of Interfaces
Models of Components
\
Requirements
Functional
Architecture
(
What Has to Be
Done
)
Logical
Architecture
(
How It Is Done
)
Physical
Architecture
(
How It Is
Implemented
)
Product Definition
Verification and Validation
All Information is Connected in a Single Data Model
Notes: Products comprise components produced by multiple suppliers
Components are procured through contracts imposing specifications
  Specifications include interface definitions
The more “right” the specifications are, the better the components integrate when delivered, reducing the cost and schedule impacts of rework, and reducing test costs
Models enable getting the specifications “right” to a degree not possible in document-based systems engineering
  Because the individual components are integrated into an overall system functional model
Models also enable emulation, since not all components are delivered concurrently

## Slide 11: Getting the Specifications Right
Requirements
Architecture
Functional
Architecture
Logical
Architecture
Do the functions and requirements included in the specification completely and accurately specify the logical architecture model?
Are the individual specifications, especially regarding interfaces, consistent with each other?

## Slide 12: Boeing Approach to MBSE Tools
Structured MBSE approach
    Siemens® Teamcenter® for SE  Teamcenter® Unified
Object-oriented MBSE approach using SysML™
    IBM® Rational® Rhapsody®

## Slide 13: Boeing Approach to MBSE Deployment
Legacy programs
  Apply MBSE to the increment or change (Herzog et al., INCOSE 2010)
  “Come along side” to train new approach, tools
    “Tell, show, do, apply”
New programs
  Gain adoption during program definition phase
  Provide training, support, expertise, assistance, tools, help, troubleshooting, tailoring – “service-ready solution”
Ensure persistence – embed the new ways of thinking in the organizational culture

## Slide 14: Topics
Boeing diverse product lines
Boeing approach to MBSE
Boeing MBSE challenges
Boeing MBSE needs from industry

## Slide 15: Challenges
Legacy and new products
Process definition/adoption
Transition to downstream phases and tools
  Integration, Verification, Manufacturing, PLM, Support
Product complexity
Quantity of engineering data
Process/tool training and skills
Use of diagramming
Notes: Continuing support of legacy products (up to 50+ years old)
Complexity of new products
Small programs and very large scale programs
Overcoming a variety of past SE / product architecting approaches
  “Requirements only” approach
  Architectures developed only for detailed subsystems
  Data captured only in powerpoint, word, excel and visio
Communication / understanding of the motivation to use MBSE
Use of MBSE information in downstream product definition lifecycle (detailed HW and SW design, test, certification)
  Moving / using the data in a host of many other tools
Adequate skill / knowledge level

## Slide 16: Size/Complexity Challenges
Increased Systems Complexity/Integration Drives Need for MBSE
Number of signals versus introduction date of the commercial transport aircraft.
Lines of Software code versus commercial transport aircraft.

## Slide 17: Quantity of Engineering Data
Example Boeing Commercial Airplane System Architecture Model Volume (~14 GB)
  ~2,300 functions
  ~10,000 data flows
  ~5266 equipment installations with data interfaces
  ~1,000,000 data parameters
  ~9490 electrical connections
  ~ 60,000,000 objects in data base (~ 3 relationships (links) per object)
~1300 users are required to produce this dataset

## Slide 18: Training & Skill Challenges
Programs need a combination of 4 skill sets:
  SE knowledge and experience
  Product domain knowledge
  Tool user skills
  Modeling skills
Acquiring modeling skills is the most difficult to achieve
  Knowing what to model at what level of detail based on the questions to be answered
  Knowing what modeled data to analyze & how to analyze it
SE
Tool
Modeling
Knowledge
Experience
Skill
Product

## Slide 19: Diagramming Challenges
  Diagramming is a starting point for stakeholder discussions and model review
A diagramming interface is inadequate for creating millions of objects and relationships
  Also use bulk import utilities, spreadsheets, documents, and database objects
A diagramming interface is impractical for analyzing millions of objects and relationships for integrity
  Also need query and presentation of results in a report format
A diagramming interface is a necessary component of an MBSE environment to allow human comprehension of the model, but is not sufficient, in itself, to define and analyze the model

## Slide 20: Topics
Boeing diverse product lines
Boeing approach to MBSE
Boeing MBSE challenges
Boeing MBSE needs from industry

## Slide 21: MBSE Process Needs
Success stories – to help promote the benefits
Methods to measure impact of MBSE
Training to develop good “modelers”
Methods to ensure persistence of MBSE after the advocates move on
Notes: Matthew Hause request from last IS and IW
Similar – but quantified to help promote MBSE to management
How to train individuals so that the model is “fit for use” – much more than tool training
How to ensure that the work survives/persists after the leader/advocate has moved on – eliminate single point organizational failures

## Slide 22: MBSE Tool Needs
Lower user ‘entry barriers’ – more intuitive user interfaces
Support for hundreds of globally distributed users
Size scaling – consistent performance when managing large quantities of data and users
Each diagram object is a database object
Exchange and synchronization of federated engineering data (different databases)
  Other Engineering disciplines (SWE, EE, etc.)
  Transition to Manufacturing and PLM
  Tool vendors working together!
Support for data reference libraries and data reuse
Configuration and version control of all objects
Bulk import / export / update capability

## Slide 23: Summary
Boeing diverse product lines, customer bases, and legacy programs require a balanced effort to implement MBSE
Success has been seen on a variety of programs
Boeing is committed to moving forward with MBSE
Help needed with integrating data among different tools