## Slide 1: Transition to Model Based Embedded System Development
Jim Ross – John Deere
January 2012

## Slide 2: A Look Inside an ECU
Calibration
Engineer
PV&V
Engineer
System
Engineer
Hardware
Engineer
Software
Engineer

## Slide 3: Model-Based System Development
Final Product
Virtual
Physical
Systems &
Interface Specs
Initial Model Cal
Performance
Verification
Rough Product
Time
System Architecture & Requirements
Design Updates
Model Validation
Virtual System
Modeling & Simulation
Algorithm
Updates
More Model Cal
Controller Cal
and Gain Tuning
Virtual system model
also used for
First Line Support
after production launch
Product Maturity
Physical System
Development & Testing
Concurrent & Iterative System Engineering
Develop physical system from virtual system model
Validate and refine virtual system model from physical system testing
Model Based Software Development
Notes: System vs. Software
MBSD – both System and Software
This slide paints a picture of System View
Identifies Software within it
MB Software Development
- Certainly value here
- Also significant effort invested in models
- Use for only SW leaves value “on the table”
- Extension of MathWorks’ “Rule of Twos”
The key is that the whole is greater than the sum of the parts. - Optimizing the parts is good – there is value there.
- Optimizing the whole is much, much better.
This is true when designing a product
- a vehicle or a building or a spacecraft.
- It is also true when designing a development process.
It all comes down to taking your blinders off and realizing there is more out there.

## Slide 4: Model-Based Systems Development (MBSD)
Simple Definition
  Design process using mathematical models that describe the logical and physical behavior of a system
In Practice
  Graphical model of embedded software algorithm
  Plant models capturing physical behavior
  Simulate and analyze system behavior and interactions
  Code generation from software algorithm model
Plant Model
Controller Model
Controller
(Software Algorithms)
Actuator
(Driver/Physical)
Plant
(Physical)
Sensor
(Driver/Physical)
Notes: Graphical = Block Diagram, State Diagram
Application Appropriate Plant Models – Right model for the task
Virtual design cycle through simulation/analysis

## Slide 5: Architecture, Design, Implementation
Component A Model
Component B Model
Component C Model
Application Model
Simulation
Rapid Control
Prototyping
Production Code
Generation Platform 2
Björn C. Becker
Production Code
Generation Platform 1
Design
Application model reused throughout the development process.
Architecture
Functionality split into components reused throughout the process and/or for multiple projects.
Implementation
Target variations are handled via the Data Dictionary and Code Generation.
Doubles
Fixed-Point
Singles
Doubles
Fixed-Point
Singles
Notes: Architecture – Reuse - Separate Design from Implementation
Interfaces are key here
Doubles Singles Fixed Point
Simulation x x x
RPC x
PCG 1 x
PCG 2 x
Idealized Process
Design vs. Implementation
Neutral Model – new application/algorithm logic in model form only
Data Dictionary with Implementation Details (Elaboration = Refinement)
Model can be used at any stage with any elaboration needed
Reality
Often stay with elaborated model
Struggle with “partially” elaborated models
Often capture some elaboration in model itself
Hard to go back to a neutral model for future design revisions
Overall, this is a success but there are some difficulties.

## Slide 6: Data Dictionary
Implementation Layer
Data Type – Simulation (optional) & Code Generation
Variable Name, Filenames, Storage Class – Code Generation
Range, Units – Documentation
Value Layer
Values – Simulation, Code Generation, & Production
Notes: Values
Physical Components – Nominal values come from the design
Software Components – Nominal values are part of the software calibration

## Slide 7: Plant Model Classifications
 | Simple | Controls | Analysis
Typical Tools | Simulink & Stateflow | Simulink & Stateflow Transfer Function | AMESim EASY5 Dymola GT-Suite Kuli
Basis | Logic | Dynamics | Physics
Nature | Reactive | Reactive | Predictive
Fidelity | Low | Medium | High
Execution Time | Low | Low | High
Key Business Driver | SIL Testing | MBSD | HW Design
Domain Knowledge | Low | Medium to High | High to Very High
Notes: Nature
Reactive means model is valid under conditions it was created -> Reacts to known conditions
Predictive means model is valid under all conditions -> Predicts response to unknown conditions
Domain Knowledge
  Need for specialized domain knowledge

## Slide 8: In The Loop
Electronic Control Unit
Host PC
Hardware In the Loop (HIL) System
Processor
I / O
I/O Signals
Plant Model
Software In the Loop (SIL) System
Host PC
Processor
ECU Code DLL
Virtual I / O

## Slide 9: Plant Model Usage
Windows
MIL
Plant
Model
SW Model
ECU Model
Sensor Models
System
Plant
SW
ECU
Sensors
HIL
Plant
Model
SW
ECU
Sensor Models
SIL
Plant Model
SW
ECU Model
Sensor Models
RealTime
Notes: MIL Use Cases
Simple – Initial Development
Controls – Final Development, Final Validation, Optimization
Analysis – Virtual Calibration
SIL Use Cases
Simple – Software Test, Integration Test
Controls – Integration Test, Performance Test
HIL Use Cases
Simple – Final Validation
Controls – Regression Test, Performance Test, Fault Behavior Test, Tolerance/Sensitivity Test

## Slide 10: Model in the Loop Usage
Initial Algorithm Development
  Simple Software Model
Final Algorithm Development
  Controls Model
Final Validation
  Additional Interface Models
  Controls Model
Virtual Calibration
  Analysis Model
Optimization
  Controls Model
MIL
Plant
Model
SW Model
ECU Model
Sensor Models
Notes: Note that the appropriate data dictionary can be used for each model based on the current activity
Right fidelity for the task at hand
- Traditional Model Fidelity
- Data Dictionary Implementation Layer

## Slide 11: Software in the Loop Usage
Software Test
  Simple Software Model
Software Integration Test
  Simple Software Model
  Controls Model
Performance Testing
  Controls Model
SIL
Plant
Model
SW
ECU Model
Sensor Models
Notes: Performance Testing is a variation of Virtual Calibration/Optimization performed in MIL

## Slide 12: Hardware in the Loop Usage
Final Validation
  Simple Software Model
Regression Testing
  Controls Model
Performance Testing
  Controls Model
Fault Behavior Testing
  Controls Model
  Fault Insertion Unit
Tolerance/Sensitivity Testing
  Controls Model
HIL
Plant
Model
SW
ECU
Sensor Models
Notes: Tolerance/Sensitivity Testing can be performed in MIL or SIL as well.
- In MIL, an Analysis model can be used for limited iterations.
- Controls model would be used for screening first, then an Analysis model used to look more closely where needed

## Slide 13: Conclusion
Opportunities
  Confidence in models BEFORE hardware availability
  Model Integration
  Requirement Traceability
  User Interface Modeling
  Co-simulation
Reality vs. Vision
  Model Management
  Separation of Design and Implementation
Notes: Model Integration
- Combine component models into system level models
Requirement Traceability
- Very difficult, need automation
Co-Simulation
- Can be very difficult, needs to be easier
Reality vs. Vision
- Vision is solid, reality falls short