## Slide 1: Progress in Modelica Association Project „System Structure and Parameterization"
Summary of Status by Hubertus Tummescheit
Based on presentation at 2015 Modelica conference by project leader Jochen Köhler and Michael Kübler, ZF Friedrichshafen, Germany

## Slide 2: Agenda
1.
2.
3.
4.
5.
6.
7.
8.
Motivation / Planning MAP System Structure and Parameterization
Defined Use-cases
The SSD approach
First prototypes
Use-cases for FMI in the Automotive Industry

## Slide 3: Modularization on cycle-simulations
ICE
BM
Getriebe
E
-
Drive
Leistungs
-
elektronik
Bremse
DC/DC
Batterie
BM
Transmission
EM
Hybrid Unit
VM
Steuerung
Controller
PE
Brake
Battery
Controller
Controller
Controller
Transmission
Control Unit
FMU
FMU
FMU
FMU

## Slide 4: Status of parameterization of FMUs
Realized issues (I):
No separation of parameter data from the FMUs
No possibility to handle intellectual property of parameters
No namespaces in a network of FMUS, no „virtual parameters“
No possibility to change parameters in a unique way independently from the integration environment for single FMUs
No possibility to define what parameters of the FMU are visible before and after the export
Handling of Data types
  Lookup tables, structures etc. are represented only in a flat non-dynamical matter
  Loading time of large lookup tables

## Slide 5: Basic idea
Develop a standard for
  Describing the structure of an executable system model composed of FMUs, and other models
  Parameterization of FMUs, ensembles of FMUs and other models independent from the tool and data format
  Complete separation of the model and the model parameterization (simplify & enable integration with PLM/ALM, version control, configuration control)

## Slide 6: Goals of a standardized parameterization
Dynamic behavior is separated from parameterization
One FMU can be parameterized (in a standardized way)
  Better: One model that is used to generate a FMU, can be parameterized too
Connected FMUs in a network can be parameterized (in a standardized way)
Parameterization is available on all simulation platforms (MiL, SiL, HiL)
FMUs in a network, combined with other models and ECU modules can be parameterized by one „parameter set“
Mechanisms to configure and transform parameters (unit handling)
Structural information (connections and relations between parameters of different FMUs)
Namespaces, using hierarchies/structures / bundling parameters to parameter sets

## Slide 7: Handling different parameter set formats
SSP
SSD
Param-Set1
Std Plugin
Authoring Tool
FMU2
FMU1
Plugin A
Param-Set2
Parameter Tool
Param-Set2
SSD
2

## Slide 8: Handling parameters within an authoring tool
SSD
Authoring Tool
SSP
Param-Set1
Std Plugin
FMU2
FMU1
Plugin A
Param-Set2
Parameter Tool
Param-Set2
SSD
ParamSet1.c=100
ParamSet1.d=0.01
ParamSet2.alfa=0.3
ParamSet2.beta=5.2

## Slide 9: Describing parameter sets for system architecture
SSD
Param-Set1
Std Plugin
Authoring Tool
Integration Tool
FMU2
FMU1
Sys Param-Set
Parameter Tool
Param-Set2
SSP
ParamSet1.c := SysParamSet.c
ParamSet2.alfa := 0.5*SysParamSet.alfa
SSD

## Slide 10: Describing a system structure
Complete SSP
SSD
SSD
Param-Set1
Std Plugin
Authoring Tool
Integration Tool
FMU1
FMU2
SSP
Param-Set2
Sys Param-Set
ParamSet1.c := SysParamSet.c
ParamSet2.alfa := 0.5*SysParamSet.alfa
SSP

## Slide 11: System architectures with signal-adoption-layers
SSP
Param-Set1
Std Plugin
Authoring Tool
Integration Tool
FMU2
FMU1
Sys Param-Set
Param-Set2
FMU2.u := 0.01*FMU1.y
SSP
ParamSet1.c := SysParamSet.c
ParamSet2.alfa := 0.5*SysParamSet.alfa
Complete SSP
FMU1.u1 := pi/30*u1
SSD
FMU1.u2 := u2
y1 := 100*FMU2.y1
y2 := FMU2.y3

## Slide 12: Design Goals and Basic Package
  Design Goals
  Minimize additional semantics, rely on FMI as far as possible
  Fit into FMI world (use FMI-like design choices where reasonable)
  System Structure Package (SSP)
  SSP is a „ZIP“ container with standardized content (System Structure Package)
  ‘SystemStructure.ssd’ is main system structure description file
  Referenced FMUs, SSPs, etc. packaged in resources directory
SSD
FMU
SSP
*.SSP

## Slide 13: Basic Data Model (UML)
https://svn.modelica.org/projects/ssp/trunk/SystemStructureDescription/SystemStructureDescription.xsd

## Slide 14: Questions?