## Slide 1: SysML-Modelica: A Redefinition & Modification Use Case
Alek Kerzhner and Nicolas Rouquette
Jet Propulsion Laboratory, Caltech
September 2012
Copyright 2011, California Institute of Technology
Government Sponsorship Acknowledged

## Slide 2: Overview: Why is improved support for Modelica’s redeclarations & modifications important for the SyM spec?
Currently, Modelica’s redeclarations/modifications are stored as strings
  See: http://www.omg.org/spec/SyM/1.0/Beta3/
Practically, this leads to 2 significant issues:
  #1 (slide 14) Entering this information in text is error-prone
  #2 (slide 17) Duplication is unavoidable
JPL’s proposal to capture Modelica’s redeclarations/modifications (slide 19)
  Cons:
    Definitely an up-scope of SyM 1.0 Beta3
  Pros:
    Increased opportunity for model reuse (as is demonstrated by the use case described in this presentation)
    Reduced opportunity for model inconsistency
Implications for the SyM transformations (slides 20,21)
  Separate concerns that were previously entangled in SyM 1.0 Beta3:
    Modelica’s name resolution semantics (see Chapter 4 scoping, name lookup & flattening)
    Resolved Modelica  SysML (with UML-based specialization) mapping

## Slide 3: Use Case Overview
We want to be able to have a set of “canned” analyses which can be used as-is or modified by experienced users:
  Analyses would be predefined in a Modelica tool where it is more natural to deal with equations, etc..
  Analyses would then be imported into SysML using the M2S transformation
  Users would connect these analyses as-is to descriptive model elements
  Users would use SysML generation/redefinition to modify the analysis models
  The S2M transformation would then create the appropriate Modelica model
Why?
  We cannot anticipate all variations of analyses of complex models a priori
  We need to facilitate exploring different ways to analyze an existing model (and compare them!)
Some examples this could support:
  Analyzing different system variants using the same base analysis
    Could use redefinition to replace the analysis models used for one or more components
  Analyzing the same system during different lifecycle phases
    Could use redefinition to adjust the equations describing broken/damaged components

## Slide 4: Use Case Overview (cont’d)
We want to perform two tests on a car suspension:
  when the suspension is healthy (as-designed)
  when it has been damaged
(As an example, consider a test where we apply an impulse force to the car and understand the effect on the suspension)
We start from the as-designed test (analysis models exist in Modelica, have been imported into SysML):

## Slide 5: Use Case Overview (cont’d)
Reminder: We want to perform two tests on a car suspension:
  when the suspension is healthy (as designed)
  when it has been damaged
On the descriptive side, we can use SysML specializations to define the test for the damaged suspension:

## Slide 6: Use Case Overview (cont’d)
Reminder: We want to perform two tests on a car suspension:
  when the suspension is healthy (as designed)
  when it has been damaged
We want to simulate these tests

## Slide 7: Use Case Overview (cont’d)
Reminder: We want to perform two tests on a car suspension:
  when the suspension is healthy (as designed)
  when it has been damaged
Analysis Models for these already exist in Modelica

## Slide 8: Use Case Overview (cont’d)
Reminder: We want to perform two tests on a car suspension:
  when the suspension is healthy (as designed)
  when it has been damaged
Analysis Models for these need to be created

## Slide 9: Relationship between descriptive and analytical models
Let’s assume for part of the descriptive model there exist appropriate predefined analysis models

## Slide 10: Existing Test Model
The existing models include a model for the test, which contains a Car Suspension model that can be redefined (See SyM Beta 3, Section 10.3 p. 26) . Specializing CarSuspensionModel is precisely what we need to define the damaged car variant for the 2nd test.
The CarSuspensionModel
can be subsequently modified (by specialization)

## Slide 11: Existing Car Model
The internals of the car suspension model:
Modelica's replaceable annotations are very important.
Without them, we couldn't reuse this model to do the damaged suspension test.
(See SyM Beta 3, Section 10.3 p. 26)

## Slide 12: Analysis Contexts
A
A1
A2
A3
The same descriptive model…
…could be analyzed in various ways
Analysis contexts capture the correspondence between a descriptive model and a particular analysis. (See SyM 1.0 Beta3, p. 76)
Analysis contexts are one example where cross-cutting relationships exist between an analysis and the rest of the descriptive model.
Analysis contexts

## Slide 13: Analysis Context for Original Test
For the original test, one can capture the correspondence between a structural/descriptive model and the analysis model
Descriptive:
SysML
Analytical:
Modelica
(See SyM beta 3 p. 67, 75-76.)
Analysis context

## Slide 14: Defining the new models with the current specification
Issues (1/2):
#1 The user needs to manually enter and interpret the information
  There is no way to insure consistency with the model or perform checks on these modifications until compile time
  Not only does the user now need to know a new syntax, they also need to avoid typos and understand the structure of the underlying models
  This includes understanding the appropriate procedure for name lookup, namespaces, and how to parse statements like (mass=mass)
(See SyM Beta 1.3, Section 8.10, p. 17)
Manually entered by user

## Slide 15: Variant Analysis Contexts
A
C1
A1
B1
Variations of a descriptive model…
…could be analyzed in various ways
B
C
For each descriptive variant, an analysis context is also needed
Analysis Context 1
Analysis Context 2
Analysis Context 3

## Slide 16: Analysis Context
With only the tag value strings, the correspondences cannot be captured because the appropriate structural elements are missing
This type has been re-declared, but that is only captured in the text.
Descriptive:
SysML
Analytical:
Modelica
We can’t show the descriptive/analytical correspondences
(redeclaration is only textual!)
Analysis context

## Slide 17: Defining the new models with the current specification
Issues (2/2):
#2: In order to support the definition of references to other parts of the model, the user needs to create the redefinitions anyway!
Manually created by user

## Slide 18: New Analysis Context
Now the correspondences can be captured because a redefined car property is available.
Descriptive:
SysML
Analytical:
Modelica
Analysis context

## Slide 19: Proposed Solution
Avoid duplicating the representation of Modelica’s redeclaration as tag value strings and UML/SysML’s redefinitions
Instead, specify the correspondence between:
  Modelica redeclaration
  UML/SysML redefinition (i.e., the canonical representation of Modelica redeclaration in UML/SysML)

## Slide 20: Impact on the SysML/Modelica Transformations: Currently
The Modelica AST  SysML transformations entangle two aspects in a fragile way:
Modelica’s resolution semantics (See Modelica Chapter 4)
  A Modelica’s class component is “looked up” by name in the corresponding SysML Block
The mapping between Modelica & SysML is fragile
  Modelica’s redeclarations/modifications are stored as strings (Modelica  SysML)
  Errors due to unexpected duplication between String-based Modelica redeclarations/modifications and UML-based specialization (SysML  Modelica)

## Slide 21: Impact on the SysML/Modelica Transformations: Proposed
Resolved
Modelica
(.xmi)
Resolved Modelica Library
(with SysML correspondences)
Modelica
AST model
with some expressions
parsed
(.xmi)

## Slide 22: Modelica Resolution & Modelica/SysML Correspondences
Modelica Resolver
  Currently, a QVT transformation: Modelica => Modelica
    Authoritative reference is Chapter 5 of the Modelica Language Reference
  Modelica Metamodel must be isomorphic to the record-based representation produced by a Modelica compiler implementation (flattener)
    There is currently no agreement among implementation about what this record-based representation
    This makes the implementation of a .mo  .xmi (modelica) converter highly dependent on a particular Modelica compiler implementation
  Augments the SyM 1.0 Beta3 Modelica metamodel
    Adds attributes to represent references to resolved elements
      Example: ComponentRef needs a reference to a Component definition
      (see SyM 1.0 Beta3 section 14.2.12)
Modelica  SysML Correspondences
  Modelica’s redeclarations & modifications are relationships, (not elements)
  To map these relationships to SysML, we need to incrementally maintain element/element correspondences between Modelica & SysML