## Slide 1: Emerging standards facilitating the development of MBSE Environments Experiences from the European space sector
Harald Eisenmann
24th September 2015
OMG Technical Meeting Boston 2015, 21st – 24th September 2015

## Slide 2: Emerging standards facilitating the development of MBSE Environments
ECSS working group ECSS E-TM-10-23 started in 2004 to address the issue of “project database” for European space sector also in the view of the emerging discussion of MBSE
      Sister WG ECSS E-TM-10-25 started in 2006 to specify a conceptual data model for concurrent design in early life-cycle
The concepts delivered by ECSS E-TM-10-23/5 have been the major driver for new solutions along the lifecycle
      Outside the scope of ECSS E-TM-10-23/5 but still strongly driven by a data models was Thales approach for Capella
While the 10-23/25 concepts, strongly contributed to the success of several model-based engineering activities, the approach requires consolidation and standardization
E-TM-10-23 “Space system data repository”
E-TM-10-25 “Engineering design model data exchange

## Slide 3: ECSS working group ECSS E-10-23 – started in 2004 – was to address the issue of “project database” in particular also in the view of the emerging discussion of MBSE

## Slide 4: ECSS-E-TM-10-23 “Space System Data Repository” was started to facilitate transition to MBSE with the following objectives
Cost reduction
for DB
Improve Quality of Data
Timely arrival of DB
Improve Tool Integration
ECSS-E-TM-10-25 adopted the 10-23 ideas for concurrent design facilities

## Slide 5: ECSS-E-10-23 introduces the following main concepts enabling the required interoperability for a improved consistency of data …
Engineering Tool
Data
Data Management
MMI
Conceptual Data Model
Engineering Tool
Data
Data Management
MMI
Engineering Tool
Data
Data Management
MMI
Engineering Tool
Data
Data Management
MMI
Space System Data Repository
Shared Data Management

## Slide 6: … and an adoption of model-driven S/W engineering principles in order to ensure the correct and maintainable implementation
Conceptual Data Model
Implemented Data Model
(Source code)
Logical Data Model
Model Transformation and
Technology binding
Code generation
Implementation
Constraint
Function dependent
Data models
Implemented
Function dependent
Data models
Formal specification of Data with end user meaning
... Considering implementation languages and constraints
Implemented in the target tool, framework
Conceptual issues

## Slide 7: A view on the process, provides the needed basis for the data model
Domain Discipline
Engineering
Customer
Supplier
Systems Engineering
Configuration Control
Change Management
System Architecture
Interdisciplinary Coordination
System Verification
Consideration of Life-Cycle Aspects
Assumption Management
Budgets and Budget Tracking
Concept of Operations
Functional Decomposition
Requirements Engineering
System Trades
Domain Discipline
Engineering
Domain Discipline
Engineering
Analysis / Simulation related data is not shown here!

## Slide 8: The data models is to capture the data needed by the corresponding processes together with a preliminary mapping to tools
Functional Decomposition
Data
Operational Concepts
Data
System Architecture
Data
System Verification Data
Product Structure
Product Tree
Configuration Tree
Assembly Tree
Items
As Built
Interdisciplinary Shared Data
Mechanical Engineering Data
Electrical Engineering Data
Monitoring and Control Data
OBSW Engineering Data
AIT Engineering Data
AOC Engineering Data
Key System Properties (budget, margin, assumptions)
(Meta-) data for configuration management
(Meta-) data for change management
Domain Discipline
Data
Domain Discipline
Data
Domain Discipline
Data
Requirements Data
System Architecture / Specification Tool SysML, Capella, MEGA
Requirements Engineering Tool
MS Excel
Verification Database
Scope of System Data Repository according to ECSS E-TM-10-23 and 25
PDM
PDM

## Slide 9: The concepts delivered by ECSS E-TM-10-23/5 have been the major driver for new solutions along the lifecycle

## Slide 10: The concepts delivered by ECSS E-TM-10-23/5 have been the major driver for new solutions along the lifecycle
Agency
System Prime
Suppliers
0
A
B
C
D
E
F
CDF
EGS-CC
VSD
RangeDB
System
Avionics
Operation
Life Cycle Phase
CDF
CDF supporting conceptual design
VSD as MBSE E2E demonstrator – blue print
  RangeDB is the operational realization
  EGS-CC shared G/S segment component

## Slide 11: ESA TRP “Virtual Spacecraft Design” was to develop a MBSE demonstrator – relying on the concepts of ECSS-E-10-23
Managing the Federation of DB
Definition of the managed data derived from process
Model management technologies
System simulation along the life-cycle
“user friendly” way of data editing

## Slide 12: Key improvement area in VSD was “system design” activities, here some example from related documentation – managed manually
Budgets
Verification Matrix
Integration Procedure
Configuration
Operational Proc
Requirements
Operational Modes
Electrical Interfaces
Functional Architecture

## Slide 13: The Eclipse Modeling Framework facilitates the realization with a powerful development framework
MMI Framework
Model
Management
Kernel
Consistency
Checking
Comparison
Transformation /
Reporting
Merging /
Branching
Ownership
Tracking
Versioning
Consistency
Checking
Comparison
Transformation /
Reporting
Query
Configuration
Control
Merging /
Branching
Versioning
Basic MMI
Ownership
Tracking
System Model Presentation ( Tailored MMI)
Runtime Application
Versioning
…
System Data
Representation
Conceptual Data Model

## Slide 14: … and there the re-hosted information re-engineered and formally modeled, relying on the conceptual foundation of ECSS-E-TM-20-23
17.10.2013
LEGATO - The Digital Engineering initiative of Astrium Satellites
14
Physical Configuration
AIT Flow and Integration Procedures
Verfication Definitions
Functional Architecture
Requirements Engineering
System Topology
Operational Procedures
Operational Concept
videos\Walkthrough.mp4
17.10.2013
LEGATO - The Digital Engineering initiative of Astrium Satellites
14

## Slide 15: Airbus Defence & Space had to go for a new system database development, VSD demonstrator was the blue print for that
Technology Obsolescence
Changed operational context
MBSE trends in engineering
Harmonization and Standardization
Classic SRDB
Monitoring & Control Data
System Product Structure
System Properties
Electrical Interfaces
Monitoring & Control Data
System Parameters
Analysis Properties
Evolved SRDB providing common management of shared data
SRDB: Spacecraft Reference Database
Shared Data Management
Overall Data Model enabling MBSE
Enablers

## Slide 16: The combination of 10-23 CDM with the Eclipse CDM results in a modular runtime framework, allowing incremental evolution
Model Management Kernel
System Data Representation
Domain discipline specific engineering tools
DOORS
E-CAD
M-CAD
Flight S/W Tools
Control Eng.
Tools
AIT
Tools
Functional System Simulator
Monitoring & Control Data
Verification Data
System Product Structure
Req, Data
Product Tree
Configuration Tree
Assembly Tree
As-Built Status
Product Data Management System
System Parameters
System Properties
Functional Electrical Architecture
MMI / Editors
FSS Configuration
Product Structure Editor
F. Electr Interface Editor
System Parameter Editor
System Property Editor
Simulation Configuration Editor
Verification Defintion
Editor
Monitoring & Control Editor
….
…
….

## Slide 17: “Digital Engineering” a industrial consideration of the “Space System Data Repository” – before the arrival of the new System DB….
Budgets
Dynamic Analysis
FV Simulation
[SimTG]
Verification DB […]
FSW Engi.
FEM
TMM
Electrical I/F DB
[…]
Req.-Mgt
[DOORS]
FSW DB […]
SimConf
[…]
SRDB
[…]
M-CAD
DMU
CAD data management
Product Data Management
[…]
Engineering Tools
Model Management
Configuration Control
System Engineering
Avionics
Mechanical Engineering
AIT
AOC DB
[…]
System Architec.
[SysML]
CCS
Performance
Mission Simulation
Power Analysis

## Slide 18: … and after. The current snapshot of the tool integration status, as part of the “Digital Engineering” initiative
Budgets
Dynamic Analysis
Func System Simulation
Verification DB
FSW Engi.
FEM
TMM
Electrical I/F DB
[…]
Req.-Mgt
FSW DB […]
Simulator Config DB [RDB]
SRDB
[RDB]
M-CAD
DMU
CAD data management
Product Data Management
[…]
Engineering Tools
Model Management
Configuration Control
System Engineering
Avionics
Mechanical Engineering
AIT
Avionics Data Management [RDB]
AOC DB
[…]
System Architec.
Central Checkout System
Performance
Power Analysis

## Slide 19: European Ground Segment – Common Core is to develop common building blocks to configure ground systems for AIV and operation
The objective of the EGS-CC Initiative is to developing a common European Monitoring & Control infrastructure that can:
      be applied for all class of missions, including Launchers
      used across all project phases
EGS-CC is a collaboration of European large system integrators and space agencies to develop a common core:
      Airbus Defence & Space (former Astrium Satellites and Astrium ST)
      Thales Alenia Space (France & Italy)
      OHB System
      CNES (French National Agency)
      DLR (German National Agency)
      ESA (ESOC & ESTEC)
      UKSA (UK National Agency)
Central Checkout System (CCS)
Mission Control System
EGS-CC
EGS-CC
Spacecraft
Telecommand / Telemetry

## Slide 20: CDM is required in order to specify the data which is exchange along the EGS-CC application process
CCS / MCS
Organization A
System Database
EGS-CC
Organization B
System Database
EGS-CC Development Scope
EGS-CC
CDM

## Slide 21: Methodology for conceptual data modeling for conceptual data modeling in EGS-CC
Analysis of the Domain
CDM Requirements Definition
Conceptual Data Model Definition
Preliminary validation of CDM
Operational Implementation
Validation
Existing Models
Functional Requirements
System Concept Definition
Sample Data
Requirements
Data Model
Preliminary Validation Set
Validation Data Set
Tool Support in EGS-CC
Informal
Data Model Editor (DME)
Instance Model Editor (IME)
Target Environment

## Slide 22: Analysis was to gather existing models, concepts, issues, …, ideas in order to clarify scope, and content to derive needs
Parameter along the monitoring chain
PUS
Check Concept
Sample Packet153 Packet
Packetization
M&C abstraction

## Slide 23: “CDM Requirements Definition” for baselining the needs of what shall be “express-able” with the model – from a user perspective

## Slide 24: The formal specification data, answering the requirements, is input for the S/W development i.e. for data exchange and management
Monitoring and Control Overview
Monitoring and Control Element
Monitoring and Control Aspects
M&C Parameters
Detailing of Activities

## Slide 25: The pre-validation with direct instance samples of the CDM is a review (and thus risk mitigation) activity prior development activities
MIB Parameter Definition
Variable TM Packet
Fixed TM Packet
Deduced Parameters
MIB Parameter Checks
ISIS Aggregate Parameters

## Slide 26: The CDM is the single source to derive various artefacts – directly depending on the CDM … – automatically
Data Access API
Implementations
DME
CDM 2 IME S/W Design Transformation
CDM 2 API S/W Design Transformation
Native Data Exchange Schema Generator
CDM Document Report Generator
CDM 2 RT S/W DM Design Transformation
CDM Editor
IME
CDM
eCore
Model
Data Access API Design
(UML)
RT S/W Data Model Design
(UML)
Tailoring Data
Editor
Native Data Exchange Serialization
Native
Data Exchange
Schema
External Data Exchange Serialization
CDM
Report
EGS-CC
Data Exchange
ICD
External
Data Exchange
Format
(XTCE)
CDM
RT S/W Design
(UML)
Generated
Products
includes
includes
includes
includes
includes

## Slide 27: While the 10-23/5 concepts, strongly contributed to the success of several activities, the overall approach requires consolidation and standardization

## Slide 28: Where are we in the process in adopting the principles of ECSS-E-TM-10-23 ?
The core concepts delivered by 10-23 are the blue print - from a model / tool perspective - for the needed environment for SE i.e. addressing discipline- integration, supply chain and life-cycle - integration
From the initial draft model various implementation are available along the system life-cycle - preparing digital continuity of data
A key success factor of the approach was the implementation orientation with binding into the needed tools and technologies – in combination with model-driven S/W development
There is a mutual dependency between process and CDM - close interaction with the end users required – the CDM is for users a valuable information, and a map on how to use the tool
A significant effort is needed to maintain the content and separation of the different model layers, from conceptual through logical to implementation, in particular when operational maturity and roll-out increases

## Slide 29: In proceeding the following issues have been identified
A single shared data model couldn’t be maintained, resulted into divergence of different CDM variants
      Main issue are different programs with individual objectives, stakeholder, priorities and schedules
      … but also divergence in different languages, methodologies and tools
       Resulting in increased coordination between efforts, coming down to the comparison of print outs
No commonly agreed conceptual data modelling language, methodology and tool set in the European Space Community
      Implementation driven approaches with UML / Ecore – typically applied for operational implementation
      Richer semantic oriented Fact Based Modeling – with limited application in operational environments
For data modeling, just modeling classes are not sufficient, …
      Modeling of functional dependencies in between concepts, e.g. derivation rules
      Full modeling support of run time extensions, e.g. model / reference data libraries
      Improved logic coherence of models (adopt from ontologies), suitable for automated reasoning
      Full integration with a constraint language, from specification into performant implementation in different technology domains

## Slide 30: In order to succeed in having the a strong semantic CDM behind the tools the following has to be addressed
A widely agreed use of the same language, methodology and tool is mandatory – including shared configuration control of the models
Care for validation on data model on conceptual but also implementation level, with IPR free sample data for conformance check (learn from  Cax-if.org )
Meta model architecture with an overall shared definition of core concepts - allowing the refinement, into the different application domains, organizations and projects
Widely share quite practical, but essential means to make integration happen
      Standardization of features like consistency check, version control, …, viewpoint, view
      Long term stable object identifiers like UUID v4, identifier mapping, …