## Slide 1: Systems Engineering Ontologies and Modeling Patterns at JPL
Daniel Dvorak
Integrated Model Centric Engineering
Engineering Development Office
Systems Engineering and Formulation Division
Jet Propulsion Laboratory
California Institute of Technology
Pasadena, CA

## Slide 2: Introduction
The Integrated Model-Centric Engineering (IMCE) initiative at NASA/JPL seeks to apply a model based engineering style to the development, integration and analysis of models at various level of detail across the full system life cycle
One thrust of IMCE is to develop ontologies for systems engineering and deploy them as SysML profiles
The following slides show some of the concepts and relationships in the ontologies, and how that leads naturally to modeling patterns
The use of well-defined vocabularies (ontologies) and uniform modeling patterns enables development of project-independent checks for consistency, completeness, correctness, etc.
Most of the technical content shown here is due to the work of J. Steven Jenkins
Some of these diagrams may be out of date with respect to the ontologies

## Slide 3: IMCE Technology: Ontologies for SE
Foundation Ontologies
Base, Mission, Project, Physics,
Quantities-Units-Dimensions-Values, Analysis, Artifact, Architecture description
Discipline Ontologies
Mechanical
Electrical
Thermal
Propulsion
ACS, Nav, …
Application Ontologies
Star Tracker, Sun Sensor, Reaction Wheel, Thruster, Antenna, …
uses
uses
uses
Fundamental terms use in all projects, disciplines, and applications
Discipline-specific terms specified and owned by appropriate organizations.
Kinds of items that are modeled in a project
Focus is integration and interoperation
Focus is reuse

## Slide 4: Partial contents of Foundation Ontologies
Mission Ontology: defines concepts and properties for describing missions in terms of their objectives, their constituent components, the functions those components perform, and the requirements that specify them.
Project Ontology: defines concepts and properties for describing a project in terms of its stakeholders, concerns, work breakdown, and deliverables. It provides a basis for specialization by domain experts.
Analysis Ontology: defines general concepts and properties for analyses (e.g., trade studies, driving requirements analysis, etc.). It provides a basis for specialization by domain experts.

## Slide 5: Partial Map of Foundation Ontology Concepts
performs
Think in terms of triples:
“Requirement specifies Component”
“Component performs Function”
“WorkPackage supplies Component”
specifies
Environment
Mission
Component
Interface
presents
contains
influences
deploys
Function
Objective
pursues
Requirement
specifies
invokes
Legend
relationship
a kind of
Mission ontology
Project ontology
Analysis ontology
(animated)
Analysis
analyzes
Characterization
characterizes
characterizes
Project
supplies
Program
authorizes
Concern
Stakeholder
represents
represents
Product
produces
WorkPackage
supplies
Process
executes
produces
Notes: ----- Meeting Notes (9/15/11 11:38) -----
speak about models
ontologies describe sysml model or domain models

## Slide 6: Mission Ontology Scope (partial)
Mission Ontology defines concepts for describing missions in terms of:
  Objectives,
  Constituent components,
  Functions those components perform
  Requirements that specify them
Environment
Mission
Interface
presents
performs
contains
influences
deploys
Function
Objective
pursues
Requirement
specifies
specifies
invokes
induces
aggregates
refines
Junction
joins
Flow
Item
traverses
Message
MaterialItem
Component
sends, receives
emits,
ingests
Requirements refinement
System
breakdown
Functional
decomposition

## Slide 7: Partial Map of Project Ontology
Project
Program
authorizes
WorkPackage
authorizes
Authority
Product
produces
Process
executes
Concern
Stakeholder
represents
DevelopmentState
delivers,
receives
Deliverable
authorizes
produces

## Slide 8: WorkPackages
In exactly the same way that a Program authorizes Projects to supply Missions, a Project may authorize WorkPackages to supply Components.
A WorkPackage is itself an authority, and it can authorize other WorkPackages.
The authorizes relationship between authorities is the basis of the Work Breakdown Structure.
Mission
Project
supplies
Program
authorizes
Component
WorkPackage
supplies
authorizes
Authority
Notes: WBS – perverted by JPL
The way we divide the pieces of work – delegated that way. Not the accounting purposes ( no hijacking).
Otherwise it won’t scale.
We saw in the mission profile that the Obiter Mission deploys a set of Components (including Orbiter Launch System, Orbiter Spacecraft, Orbiter Mission Operations System, and Ground System). We can new express that those things are true because the Kepler 16-b Project authorizes them. We can also say that the Project authorizes WorkPackages to supply these Components.
The general pattern repeats. Each of these supplying WorkPackages has a corresponding realization; each will contain model elements asserted by the authority of its WorkPackage, including structural and functional decomposition and delegation to the next level of supply WorkPackages.

## Slide 9: Concern and Stakeholder
Concern and Stakeholder are used in the sense of ISO/IEC/IEEE 42010 Systems and software engineering – Architecture description
A Stakeholder represents one or more Concerns
In the context of the Project profile one can say that every Objective (Mission profile) is a Concern (a particular type of Concern that is pursued by a Mission)
Objective
Concern
Stakeholder
represents
Notes: All these have authoritative statements

## Slide 10: Scope of Interface Definition Pattern
This diagram shows a partial map of the Mission Ontology and highlights the scope of the Interface Definition Pattern
Environment
Mission
Interface
presents
performs
contains
influences
deploys
Function
Objective
pursues
Requirement
specifies
specifies
invokes
induces
aggregates
refines
Junction
joins
Flow
Item
traverses
Message
MaterialItem
Component
sends, receives
emits,
ingests
Scope of Interface Definition Pattern

## Slide 11: Scope of 3 patterns related to Function and Interchange
Function
F1
emits
joins1
performs
joins2
InterchangePoint
IP1
Flow
X1
interchanges Through
ingests
InterchangePoint
IP2
Function
F2
interchanges
Through
Component
C1
Interface
IF1
presents
Interface
IF2
Junction
J1
Component
C2
presents
performs
traverses
Interchange
IC1
participatesIn
involves1
involves2
This diagram shows a Flow interchange; similar diagram for MaterialItem and Message.
transfersOut
transfersIn
Scope of Functional Interchange Definition Pattern
Scope of Interface Definition Pattern
Scope of Functional Allocation Pattern

## Slide 12: The value of entailments
«Function»
«performs»
«Component»
«Requirement»
«specifies»
Note: The “binds” relationship is deduced by a tool, not entered by modelers, and can then be used in audits.
«binds»
Audit Rule
Every component must be bound by at least one requirement. (Otherwise, there is no justification for the component.)