## Slide 1: Systems Engineering Concept Model (SECM) Update
Status 09/15/2016
John Watson

## Slide 2: System Engineering Concept Model Agenda
Overview
  SECM High Level Approach
  Today’s SECM Content
  SECM – SysML V2 RFP Approach
Status
  Core Teams Launch Status
  SE Needs work in progress Status
    Requirements and Verification
    Element Concept
    Future Efforts
Notes: Over all goal is to tell what we have done, what we are working on now and to say what’s next.

## Slide 3: Systems Engineering Concept Model (SECM) Approach
SECM – 2015 Industry Reference
SECM - SysML V2 RFP
ISO/
IEC/IEEE 15288:
2015
Other Industry Ontologies
UML 4SE RFP
SysML V1.X Spec
V 1.5
SECM – 2003 Industry
Reference
*
INCOSE Systems Engineering Handbook V4
SysML V2 RFP
* Joint INCOSE/AP233/OMG, Led by Dave Oliver
Other
OMG
Specs
SysML V2 Service Requirements
SysML V2 Spec
User Interface
Guidelines
Meta-model
Profile
Libraries
Concrete Syntax
Standardized API
Reference Model

## Slide 4: SECM Model High Level Organization

## Slide 5: SECM – SysML V2 RFP

## Slide 6: “SECM – SysML V2 RFP” Approach
SECM - SysML V2 RFP
UML 4SE RFP
Related Papers
Other Industry Ontologies
SECM – 2015 Industry Reference
Example Models
SE Needs Concept Model
SE Needs Document
Requirements & Concepts
Topic Expert Core
Team
Produce “SE Needs”
Refine with Industry Experts
Notes: Same as a typical SE Process, Needs analysis followed by requirements to drive the solution

## Slide 7: Topic Core Teams
Properties and Expression Concepts Modeling Core Team
  SE Needs Artifacts Available
  Core Team Launched 22 January 2016
  Their status will be provided today
Interface Concepts Modeling Core Team
  SE Needs Artifacts Available
  Core Team Launched 27 May 2016
  Their status will be provided today
Requirements and Verification Concepts Modeling Core Team
  SE Needs Artifacts Near Completion
  Should be available in the next couple of weeks
Structure/Behavior Concepts Modeling Core Team
  SE Needs effort just beginning
  Initiated14 September 2016
Potential Future Core Team Topics
  Variants
  Libraries

## Slide 8: SE Needs Requirements/Verification

## Slide 9: Requirement Needs Concepts Goals
Capture the concepts of a requirement specification, and the relationships to realization and verification
Capture model based specifications that are more precise, analyzable, verifiable, and reduce ambiguity
Enable the ability to automate the validation of requirements within the model
Maximize the ability to reuse requirements
The key validation concepts include:
  A requirement can be applied to any element in the model to specify constraints on that element
  A realization element can be evaluated
  The realized element is verified by determining whether it satisfies the constraint
Notes: Relative to PBR, Any element can be constrained, not just properties, interface, function or state can be constrained

## Slide 10: Requirements/Verification Concepts
Specification
Verification
Realization

## Slide 11: Requirement Traceability Diagram

## Slide 12: Requirement Attribute Concepts

## Slide 13: Requirement Transformation Example – Curb Weight
Original Textual Requirement Statement
  The Vehicle weight shall not exceed 3200 pounds.
Transformed Formal Requirement Statement
  Subject = Vehicle::Required Curb Weight
  Pre conditions
    Context Properties referencing Environment Properties
      Number of Passengers = 0
      Cargo Weight = 0 lbs.
    Context Properties referencing Vehicle as Designed Properties
      Fuel Capacity = 14 gallons (Full)
      Transmission Oil Capacity = 2 quarts (Full)
      Engine Oil Capacity = 5 quarts (Full)
      Coolant Capacity = 5 gallons (Full)
  Constraint = Boundary Expression:
    Vehicle::Required Curb Weight = 3000 lbs.
  Constraint Evaluation:
    Actual Curb Weight <= Required Curb Weight
  Generated Text Statement: With zero passengers, cargo weight of 0 pounds, a fuel capacity of 14 gallons, transmission oil capacity of 2 quarts, engine oil capacity of 5 quarts, and coolant capacity of 5 gallons, the Curb Weight of the vehicle shall be equal to or less than 3000 pounds.
Notes: Supporting information – e.g. Definition of Curb weight

## Slide 14: Vehicle Weight Performance Requirement Example

## Slide 15: Vehicle Curb Weight Requirement Analysis

## Slide 16: Decompose a Compound Requirement Example

## Slide 17: Element Concepts

## Slide 18: Element Concepts

## Slide 19: Questions

## Slide 20: Backup

## Slide 21: ISO/IEC 29148 Functional Requirement Breakdown
ISO/IEC 29148 states that a typical sentence form for a functional requirements is:
  ‘When <condition clause>, the <subject clause> shall <action verb clause> <object clause> <optional qualifying clause>.
The Control Subsystem shall close the Inlet Valve in less than 3 seconds when the temperature of water in the Boiler is greater than 85 °C.
  Subject – Control Subsystem
  Action verb clause – shall close
  Object clause - the Inlet Valve
  Qualifying clause - in less than 3 seconds
  Condition clause - when the temperature of water in the Boiler is greater than 85 °C

## Slide 22: Resources and References
SEBoK
ISO/IEC/IEEE 15288
INCOSE SE Handbook
INCOSE Guide for Writing Requirements – 2015
PBR Working Group Material
SE Use Case Workflow Working Group
UML 4SE RFP
Yves Bernard’s Paper, 2011, Requirements Management within a Full Model-Based Engineering Approach

## Slide 23: SECM-Domain Goals and Overview
Task objective
  Derive a data model that captures the core Systems Engineering concepts and vernacular
  Derive the system modeling language requirements that will be used in the SysML V2 RFP
Use Cases
  Systems engineers and other discipline engineers contribute to the development and maintenance of a system model throughout the lifecycle to support the system specification, design, analysis, and verification activities
MoE
  The SysML V2 RFP requirements are clear and concise, and reflect the core Systems Engineering concepts and vernacular
High Level Intent/Driving Requirement:
  (R1) The next-generation modeling language must express the core systems engineering concepts. This requires definition of a robust data model that reflects these concepts. The requirements that drove SysML derive from the original Systems Engineering Conceptual Model, jointly developed by the INCOSE/OMG/AP233 WG requirements team. Modifications and refinements to this model will occur in light of lessons learned over the last several years, and as necessary to express the core systems engineering concepts.
Notes: SECM captures the SE Concepts and vernacular
UC SE lifecycle development & maintenance , specification design and verification
MoE - Clear consise req