## Slide 1: Experiences from Developing Concurrent Multi-Disciplinary MBSE
Hans Peter de Koning
European Space Agency
European Space Research and Technology Centre (ESTEC)
Noordwijk, The Netherlands

## Slide 2: ESA Concurrent Design Facility (CDF)
For details see http://www.esa.int/cdf
Concurrent engineering of conceptual design of almost all candidate ESA missions
10 to 20 studies per year
~20 domains-of-expertise per study team
including cost, risk, programmatics

## Slide 3: ECSS-E-TM-10-25 Based Model Driven Architecture
Database
Standardized Semantic / Conceptual Data Model
Semantic Data Model
“Master Definition of Concepts”
addresses “what” not “how”
Derived Logical and
Physical Data Models
“Reference Data Libraries (RDLs) “
Runtime loadable
predefined objects,
including QUDV and Categories
Software Implementations
Tool
Tool
Tool X
Database
Database A
Automated transformations
Interoperable tools and databases
(including adapters to enable existing tools)
Generated
Similar to UML / SysML Model Libraries
Used small subset of UML2

## Slide 4: Open Concurrent Design Tool (OCDT) Architectural Overview
PostgreSQL
Protocol
over TCP/IP
Web Services Processor
(nodejs on Google V8)
Persistent Data Store
(PostgreSQL RDBMS)
Firewall
(optional)
http(s) REST protocol
(on standard ports 80 or 443)
GET, POST, content is JSON
ConCORDE
DST
(Domain Specific Tool)
OCDT Server
OCDT Clients
Domain N
ConCORDE
Domain 3
ConCORDE
Domain 2
ConCORDE
Domain 1
OpenLDAP Server
(optional)

## Slide 5: OCDT implements ECSS-E-TM-10-25A through code generation
Annex A
Standard Semantic Data Model
in UML (MagicDraw)
xmi_verter
(OCDT
code generator)
SQL database scripts
JSON meta-model
C# class library
Python class library
XML Schema
Excel workbook
for data model analysis
Annex A at version 2.4.1
(12 Nov 2013)

## Slide 6: ConCORDE Screenshots (1/2)
Use of Excel as front-end UI
with ConCORDE Ribbon Tab
to reduce learning curve
Site Directory Data
(Models, Catalogues,
Persons, Participants, …)
z
Reference Data
(Parameter Types,
Categories,
Units & Scales,
Rules, …)

## Slide 7: ConCORDE Screenshots (2/2)
All team members automatically sync to latest state of model at 30 second intervals
Engineering Model or Catalogue
(Options,
Element Definitions and Usages, Parameters, …)
Excel Workbook

## Slide 8: Community Portal
https://ocdt.esa.int

## Slide 9: Initial list of desirable improvements in a future SysML (1/2)
Significantly better “semantic quality” of SysML meta-model
  Must be founded in formal logic – ideally provide basis for automated reasoning
  Clean up impeding “artificial” UML heritage
Consider a SysML-Light – a pure subset of a SysML-Full
  Help reduce the learning curve for “normal” engineers
  SysML-Light usable for less complex systems, early life-cycle phase
  Fits with web-app / desktop tool?
Support fine-grained ownership of (responsibility for) model elements by domain-of-expertise and/or multi-disciplinary team-member
  Provides solid basis for role-based access rights management
  E-TM-10-25 / OCDT shows it is doable at Block, Usage, Value Property level
Support fine-grained version / revision control
  Enable full revision history
  Could (should?) be an orthogonal concept to rest of meta-model
  At object level? Need to validate potential scaleability issues.
  Learn from success of git and github

## Slide 10: Initial list of desirable improvements in a future SysML (2/2)
Support compound value properties / types
  To represent richer datatypes (records, vectors, matrices, n-dimensional tensors, generic capture of variable length lists, time series data, …)
Upgrade QUDV model with full support for “measurement scales”
  So that more than just ratio scales can be accurately represented: ordinal, interval, logarithmic, cyclic ratio scales …
  This is needed for future automated unit/scale conversion when integrating models coming from many different sources
  Reference implementation available in E-TM-10-25 and OCDT
Support finite-state-dependent value properties
  I.e. allow a different value for each state
  Very useful in early concept design/formulation
Natural language presentation of relationships and their inverse
  Direction / arrow is immediately clear
  e.g. «satisfy» becomes “A «is satisfied by» B” and “B «satisfies» A”
OCDT has a fast REST Web-Services API
  Experience can be shared