## Slide 1: SECM - Requirements Concepts Initial proposal on restricted textual requirement
Tao Yue and Shaukat Ali
Simula Research Laboratory
Oct 19nd, 2016

## Slide 2: Restricted Textual Requirements
Suggested keywords to use:
  REALIZE
  IS GREATER THAN, LESS THAN, EQUAL TO, etc.
    We have defined a list of such keywords for iOCL.
  IF-THEN-ELSE-ELSEIF-THEN-ENDIF, DO UNTIL, MEANWHILE, VALIDATES THAT
    RUCM has a list of keywords defined for conditions, iteration and concurrency
  INCLUDE, EXTENDED BY
Example
  Input
    “IF the boiler water temperature [ContextProperty] IS GREATER THAN the Boiler Water Valve Threshold of 85oC [ContextProperty], THEN Actual Inlet Valve Control Behavior [ConstrainedProperty] of Control Subsystem shall REALIZE INCLUDE Inlet Valve Control Function [ConstrainingProperty] to open the inlet valve [RealizedElement], ELSE close the inlet valve [RealizedElement] ENDIF.”
  Output
    List of properties
    IF Boiler Water Temperature > Boiler Water Threshold, THEN Open Inlet Valve, ELSE Close Inlet Valve ENDIF.
      With this constraint, a Realize Evaluation can be generated automatically when needed.
      Do we need to formalize Open Inlet Valve and Close Inlet Valve?

## Slide 3
Several questions
  Is Inlet Valve an realized element?
  Does the activity diagram specifying Inlet Valve Control Function at the requirements level or design?
  We might need templates to enforce structures if requirements are complicated.
Going from restricted textual requirement statements to formal requirement statements
  (Semi-automatically) Extract properties from noun phrases (one heuristic)
  Automatically extract constraints.
Restricted Textual Requirements

## Slide 4: Suggested Conceptual Model Changes

## Slide 5: Methodologies
Manual free textual requirements statements and manual formal requirements statements
Manual restricted textual requirements statements and automated (mostly) formal requirements statements
Manual restricted textual requirements statements and automatically generated UML diagrams (e.g., activity diagrams)

## Slide 6: Transformations
Input: Restricted requirement statements
Output 1: Formal requirement statement
Output 2: SysML analysis or design diagrams
Output 3: other artifacts such as tests

## Slide 7: Small Demo

## Slide 8: Small Demo