# Precision Time Protocol (PTP)
Return to Glossary
The Precision Time Protocol (PTP), as defined in the IEEE 1588-2019 - Standard for a Precision Clock Synchronization Protocol for Networked Measurement and Control Systems standard, provides a method to precisely synchronize computers over a Local Area Network (LAN). PTP is capable of synchronizing multiple clocks to better than 100 nanoseconds on a network specifically designed for IEEE-1588. A Network Time Server with PTP is typically referred to as an “IEEE-1588 Grandmaster” or “PTP Grandmaster”. This paper describes basic principles of PTP, information on using dual Grandmasters, and the requirements of the network to achieve sub-100 nanosecond time synchronization.
Source: https://endruntechnologies.com/pdf/PTP-1588.pdf