## Slide 1: Review, Update and Pathway for UPR 1.0 Evolution
UPR: UML Profile for ROSETTA
Presented to the ADTFPTF
23rd March 2022
Charles Dickerson Zahir Ismail Siyuan Ji
Formerly of ZTI Systems
OMG Mathematical Formalisms SIG

## Slide 2: Background and Context
Purpose: introduce discuss plans to evolve the UML profile for the modelling and simulation framework called ROSETTA*.
OMG discovered ROSETTA on MARS.
UPR 1.0 is concerned with structuring information in support of model-based analysis for architecture optimization and constraint driven system design.
In the development of the UML profile for ROSETTA [1] the question was asked at MARS: can constraints also be logical?
* ROSETTA: the Relational Oriented Systems Engineering Technology Trade-off and Analysis Framework [2, 3, 4, 5]
OMG Mathematical Formalisms SIG

## Slide 3: Agenda
UPR 1.0
  Constraint Driven Design (CDD)
  Relational Transformation
  Application to commercialisation of EV wireless charging
Relation to Kernel Modeling Language and Predicates
Discussion of Pathway for UPR 1.0 Evolution
OMG Mathematical Formalisms SIG
EV: Electric Vehicle

## Slide 4: UPR 1.0
UPR aims to
  Fill the gaps by accessing, structuring and integrating information across multiple system models for support of CDD
  Identify conflicting and harmonious requirements
  Support optimization and transformation of System Architecture into Detailed Design
UPR 1.0 proposed
  10 stereotypes, and 1 library
  Facilitating annotation of models to identify information
  But the intent is Not to define new analysis techniques

## Slide 5
UPR 1.0 facilitates the modelling of metric constraints for CDD [6]
A Variable is a measurable attribute that represents an element being constrained and can take on a range of real values.
A Constraint is a constant that limits the values of a variable.
A Comparison Operator, such as ‘<‘, is used to model constraints.
A Design Objective is a measurable attribute of a system that the system is intended to have or achieve e.g., a requirement.
A Design Variable is a variable under the design authority of the engineer. It imparts system properties that achieve objectives e.g., a vehicle speed of > 100 mph can be achieved by reduced weight.
OMG Mathematical Formalisms SIG
Constraint Driven Design (CDD) in UPR 1.0

## Slide 6: UPR for CDD Modeling Model annotation for information extraction
Existing System Model
Annotation
UPR Stereotypes
Design
Objective Constraints
DOtoDV
Sensitivities
Design
Variable
Constraints
Design
Variable
Constraints
OMG Mathematical Formalisms SIG
Notes: r

## Slide 7
Design Variables:
x1 : Radar Power
x2 : Radar Aperture
Design Ranges:
S1: x1 > 0
S2: x1 < 40 dBw (10 Kw)
S3: x2 > 0
S4: x2 < 10 dBsm (10 m2)
Design Space is bounded by Design Ranges
x2
x1
Power Aperture2 = PA2 in linear units for bistatic detection
Power Aperture = PA in linear units for radiation safety.
Design Space
Constraint Driven Design
Radar system design with design space
0
10dBsm
40 dBw
OMG Mathematical Formalisms SIG

## Slide 8
Analytic Equations:
y1 = W1(x1, x2) = x1 + 2x2
y2 = W2(x1, x2) = x1 + x2
Design Constraints:
A design solution for (x1, x2) must simultaneously satisfy the Design Constraints:
y1 > 20 (e.g. for detection)
y2 < 30 (e.g. for safety)
Design Objective Constraint (y1): y1 > 20
Design Objective Constraint
(y2): y2 < 30
Power Aperture2 = PA2 in linear units for bistatic detection
Power Aperture = PA in linear units for radiation safety.
Feasible Design Space
Constraint Driven Design
Feasible Design Space for radar system design
x2
x1
OMG Mathematical Formalisms SIG

## Slide 9
Information Required
Design Objective Constraints: y1, …, ym
Design Variables: x1, …, xn
with Design Ranges
S1 , S2 , …
Analytic Equations:
y1 = W1(x1, …, xn)
y2 = W2(x1, …, xn)
…
ym = Wm(x1, …, xn)
Feasible Design Space expressed in terms of
Feasible Ranges
Mathematical Viewpoint
ROSETTA seeks to access and annotate key information from MBSE System Model.
Design algorithms use the information a Feasible Design Space to seek solutions.
Constraint Driven Design
Information required
y1 > 20
y2 < 30
Feasible Design Space
x2
x1
OMG Mathematical Formalisms SIG

## Slide 10: ROSETTA Framework* for Modelling and Analysis Radar System Example of Power Transfer
Radar Design Variables include:
  : Radar Power
  : Radar Aperture
  : …
Key Radar Design Objectives include:
  : Detection Range
  : Radiation Safety
  : …
OMG Mathematical Formalisms SIG
Sensitivities captured as matrix elements in the ROSETTA Framework
Source model
(Design Variables):
Target model
(Design Objectives):

## Slide 11: Capturing CDD information using UPR Stereotypes UPR Foundation & Operator Library
UPRConstraint & Sensitivity (Clause 7)
    Extend UML Constraint and UML Dependency to facilitate the modeling of Design Constraint and Design Variable; the mathematical relations between them.
Operator Library (Clause 8)
    A library of comparison operators to be used for modeling a UPRConstraint
    e.g. =, >, <, etc.
OMG Mathematical Formalisms SIG

## Slide 12: Capturing CDD information using UPR Stereotypes Design Constraints
Design Constraints Package (Clause 9):
  Design Constraint extends UPRConstraint using
  2 additional operations and 1 attribute for model annotation and traceability
DOC, y1:
y1 > 20
DOC, y2:
y2 < 30
System Elements Traceability
Constrains the Property of
Class (SysML Requirement)
UseCase
Mathematical Element Traceability
DOC: Design Objective Constraint
OMG Mathematical Formalisms SIG

## Slide 13: Capturing CDD information using UPR Stereotypes Design Variables
Design Variable Package (Clause 10):
  Design Variable extends UPRConstraint using
  2 additional operations and 3 attributes for model annotation and traceability
Design Ranges:
DR1: x1 > 0
DR2: x1 < 40
Feasible Ranges:
FR1: x1 > 15
FR2: x1 < 30
Initial Design:
ID: x1 = 20
Mathematical Element Traceability
System Elements Traceability
Constrains the Property of
Class
State
Action
OMG Mathematical Formalisms SIG

## Slide 14: Capturing CDD information using UPR Stereotypes Analytic Equations
Relational Structure and Design Modeling (Clause 11):
  DO to DV Sensitivity extends Sensitivity to model relations between Design Constraint and Design Variable using
  3 additional rules and 1 (refined) attributes for model annotation and traceability
  Object oriented modeling of “mathematical models” *
DO: Design Objective
DV: Design Variable
Analytic Equation(s):
y1 = W1(x1, x2) = x1 + 2x2
* ... using constants, variables, and types of
mathematical expressions (e.g. RSE)
OMG Mathematical Formalisms SIG

## Slide 15: A Facility to Support Relational Transformation Unary Transformation
Unary Transformation (RT-U):
  Based on specified Analytic Equations, such as RSE, RT-U transforms Design Constraints to a Feasible Range of the each Design Variables
  (c.f. Clause 11.3.3 Example)
RSE: Response Surface Equation
OMG Mathematical Formalisms SIG
15

## Slide 16: ROSETTA Mathematical Analyses Capability Implementation algorithms for RT-U transformations
OMG Mathematical Formalisms SIG

## Slide 17: A Facility to Support Relational Transformation Binary Transformation
Binary Transformation (RT-B):
  Based on specified relations and associated Sensitives, RT-B identifies (harmonious/conflicting) relations between Design Constraints
  (c.f. Clause 9.3.3 Example)
RSE: Response Surface Equation
Target model
(Design Objectives):
OMG Mathematical Formalisms SIG
17

## Slide 18: Agenda
UPR 1.0
  Constraint Driven Design (CDD)
  Relational Transformation
  Application to commercialisation of EV wireless charging
Relation to Kernel Modeling Language and Predicates
Discussion of Pathway for UPR 1.0 Evolution
OMG Mathematical Formalisms SIG

## Slide 19: Application of UPR to Electric Vehicle(EV) Charging Home - AMiCC - Amicable Charging Research Project (projectamicc.com)
AMiCC is a commercialisation project for EV wireless charging supported by Innovate UK and funded by the Office for Zero Emission Vehicles (OZEV).
OMG Mathematical Formalisms SIG
UPR facilities are being developed for metric constraints but are also needed for logical constraints (e.g., topologies).
Design objective constraints include
  Rate of power transfer
  Electromagnetic field strength
Design variable constraints include
  VA size and circuit topologies
  Cooling for power transfer
  Communication protocols
VA: Vehicle assembly GA: Ground assembly
WPT: Wireless power transfer
VIU: Vehicle interface unit
HMI: Human Machine Interface
Ground assembly for WPT
EV retrofitted with VA, VIU and HMI for WPT

## Slide 20: Experimental Setup for Wireless Power Transfer (WPT)
Similar physics compared with transformers
  Primary coils generate magnetic field which then induces current in the secondary coil
  y
Design Objectives:
  Magnetic Flux Density emitted by the primary coil
  Power Transferred to secondary coil
Design Variables
  Current in the primary coils
  Separation of the coils
  Radius of the coils (fixed)
  Number of turns in the primary coil (fixed)
OMG Mathematical Formalisms SIG

## Slide 21: Wireless Charing for Electric Vehicle (EV)
GA: Ground Assembly
VA: Vehicle Assembly
Recall : Power Transferred, now with EVs
, where
: Operating Frequency (fixed)
: GA Current
: Coupling Coefficient
: GA Inductance (fixed)
: Quality Factor (fixed)
depends on structural properties which are a mix of
discrete variables, e.g. logical circuit topology
continuous variables, e.g. lateral misalignment
Wireless Charging for EV
OMG Mathematical Formalisms SIG

## Slide 22: Complex System Design Solutions Example of Electromagnetic Field Emissions1
Parts of the problem that can be ‘understood’ by conventional CDD:
   Design of continuous nature e.g.,
  as function of GA & VA separation
  as function of GA & VA alignment
Parts of the problem that requires further ‘development’ in CDD capability:
   Design of a discrete nature
  as function of coupling factor
1Campi T, Cruicani S, Maradei F, Feliziani M. Magnetic Field during Wireless Charging in an Electric Vehicle According to Standard SAE J2954. Energies. 2019;12:1795 [7]
OMG Mathematical Formalisms SIG

## Slide 23: Agenda
UPR 1.0
  Constraint Driven Design (CDD)
  Relational Transformation
  Application to commercialisation of EV wireless charging
Relation to Kernel Modeling Language and Predicates
Discussion of Pathway for UPR 1.0 Evolution
OMG Mathematical Formalisms SIG

## Slide 24: KerML [8]
[6.2 Document Conventions] Core mathematical semantics are generally expressed in terms of notations from first order logic.
UPR 1.0 is mathematically based; and conforms to first order model theory in logic.
Predicates are central to formalising object-oriented models.
KerML Element Hierarchy [8, Figure 3]
OMG Mathematical Formalisms SIG

## Slide 25: What is a Predicate? [9, 10] Example of use cases for a radar system
Actor 1 (ATC)
(e.g., subject of verb)
<Verb – Noun> Phrase 1
System
Actor 2 (Aircraft)
(e.g., object of verb)
A predicate is that part of a sentence containing a verb and stating something about the subject.
ATC <request detection> from system.
System <detect aircraft>.
Note that the System and <verb - noun> phrase always form a sentence.
<Verb – Noun> Phrase 2
ATC: Air Traffic Control
OMG Mathematical Formalisms SIG

## Slide 26: Architecture Specification
Semantic Structure
  A ‘clean’ structure that one would find in any model developed using standardised language such as UML/SysML:
Semantic Transformation
  provides a way to preserve semantic structures from one view to another
Domain Structure
  Semantic structure filled with domain knowledge
Interpretation
  Interpret domain knowledge into a semantic structure
A dedicated presentation to Ontology PSIG (Thursday)
OMG Mathematical Formalisms SIG

## Slide 27: Agenda
UPR 1.0
  Constraint Driven Design (CDD)
  Relational Transformation
  Application to commercialisation of EV wireless charging
Relation to Kernel Modeling Language and Predicates
Discussion of Pathway for UPR 1.0 Evolution
OMG Mathematical Formalisms SIG

## Slide 28: Pathway for UPR 1.0 Evolution
Scope of evolution is beyond UPR 1.0 RTF due to
  Inclusion of logical constraints
  Alignment of formal semantics with KerML/Predicates
  Utilising SysML 2 for design analysis
  Supporting CDD automation
Pathways
  UPR 2.0?
  Collaboration with SysML 2 Working Group?
  Collaboration with Ontology PSIG?
OMG Mathematical Formalisms SIG

## Slide 29: References (1 of 2)
[1] Dickerson, C.E. and S. Ji, Mathsig/2015-09-01, Profiling a Software Architecture for the Relational Oriented Systems Engineering Technology Trade-off and Analysis Framework (ROSETTA) v4.3.
[2] Dickerson, C.E. and D. Mavris, “Relational Oriented Systems Engineering (ROSE): Preliminary report,” in Proc. IEEE SoSE '11, Albuquerque, 2011.
[3] Dickerson, C.E., “A relational oriented approach to system of systems assessment of alternatives for data link interoperability,” IEEE Systems Journal, 16 May 2013.
[4] Mavris, D., K. Griendling and C. Dickerson, “Relational-Oriented Systems Engineering and Technology Trade-off Analysis Framework,” AIAA Journal of Aircraft, 28 August 2013.
[5] Dickerson, C.E., and D. Mavris, “A Brief History of Models and Model Based Systems Engineering and the Case for Relational Orientation,” IEEE Systems Journal, vol. 7, no. 4, 2013.
[6] (OMG) Object Management Group 2019, UML Profile for ROSETTA (UPR) Version 1.0
[7] Campi T, Cruicani S, Maradei F, Feliziani M. Magnetic Field during Wireless Charging in an Electric Vehicle According to Standard SAE J2954. Energies. 2019;12:1795
[8] (OMG) Object Management Group 2021, Kernel Modeling Language (KerML) Version 1.0 Release 2021-05
OMG Mathematical Formalisms SIG

## Slide 30: References (2 of 2)
[9] Dickerson, Charles E. et al, 2021. “Architecture definition in complex system design using model theory.” IEEE Systems Journal 15, no. 2: 1847 – 1860.
[10] Dickerson, C.E. and Siyuan Ji, Essential Architecture and Principles of Systems Engineering. Boca Raton Florida: CRC Press Auerbach Publication, September 2021.
OMG Mathematical Formalisms SIG